## Slide 1: Multi-link Aggregation Considerations
Date: 2019-09-15
Authors:

## Slide 2: Introduction
Multi-link Operation
  Key candidate feature of TGbe
  Transmission of frames of a TID over multiple links [1]
  Minimizing negotiation overhead for fast link switching [2]
Multi-link Aggregation
  Mechanism to boost high throughput applications
  Link with backoff countdown to 0 can aggregate second link if idle (e.g. for PIFS)
  Per-link PPDU provides more flexibility due to diverse link conditions
link A
link B
3
2
1
0
TXOP
6
5
4
BUSY
TXOP
TXOP
9
8
7
6
BUSY
5
4
3
2
1
0
BUSY
ML
STA

## Slide 3: Multi-link Aggregation Impact
Promising multi-link gain provided by aggregation [4, 5]
In addition, we need to consider multi-link BSS with varying distribution of single link STAs and multi-link STAs
In this presentation, we consider the impact of multi-link aggregation on single link STAs in multi-link BSS

## Slide 4: Aggregated link Backoff Procedure
In single link operation, CW resets to CW min upon successful transmission
Backoff counter did not reach zero on aggregated link prior to TXOP
Resetting CW to CW min on aggregated link can be unfair to single link STAs
Proposal: CW remains same as prior to TXOP on aggregated link and backoff counter resumes from value prior to TXOP
Failed transmission case can follow existing backoff procedure
link A
link B
3
2
1
0
TXOP
9
8
7
busy
TXOP
TXOP
6
5
4
3
busy
5
4
3
2
1
0
busy
Backoff countdown resumes with same value
ML
STA
TXOP: ML STA’s TXOP
Busy: other traffic

## Slide 5: Unidirectional Aggregation
Aggregation considered so far is bi-directional (link A “invites” link B and vice versa)
Scenario: Single link STAs operating on link A and multi-link aggregation enabled
In worst case, starvation of single link STAs if link B has no traffic other than of ML STAs
  Mean backoff value on link B is smaller than mean backoff value on link A
  Access delay on link B is smaller than access delay on link A
Proposal: Unidirectional Aggregation mode
  Aggregation limited from link A to link B
  Link A with backoff 0 can aggregate link B if link B is idle
  Link B with backoff 0 cannot aggregate link A even if link A is idle
link A
link B
3
2
1
0
TXOP
2
1
0
Single link STA
busy
busy
TXOP
TXOP
5
4
3
2
2
1
0
TXOP
busy
ML
STA
TXOP: ML STA’s TXOP
Busy: other traffic

## Slide 6: Summary
Fairness for single link STAs needs to be considered in design of multi-link aggregation protocol design
Backoff procedure on aggregated link needs further consideration
Unidirectional aggregation mode can benefit single link STAs in certain scenarios

## Slide 7: Straw Poll #1
Do you agree fairness for single link STAs needs important consideration in the design of multi-link aggregation protocols for TGbe?

## Slide 8: Straw Poll #2
Do you agree multi-link aggregation shall be enabled for non-STR STAs to boost their channel access opportunities?
  Non-STR STA in the context of a link pair is a multi-link STA that is not capable of simultaneous transmit and receive operation on that link pair [3]

## Slide 9: References
[1] 11-19/979, “EHT Multi-link Operation Follow-up”
[2] 11-19/822, “Extremely Efficient Multi-band Operation”
[3] 11-19/1405, “Multi-link Operation Channel Access Discussion”
[4] 11-19/764, “Multi-link Aggregation Gain Analysis”
[5] 11-19/1291, “Performance Aspects of Multi-link operations”