## Slide 1: Discussion on Multi-link Setup
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
Multi-link capable devices need to negotiate multi-link capability during a multi-link setup
  Multi-link setup would include scanning, authentication, and association
In this contribution, we discuss the multi-link setup for negotiating multi-link capability between multi-link capable devices
  We call an AP with multi-link capability a multi-link (ML) AP logical entity [1]
  We call a non-AP with multi-link capability a multi-link (ML) non-AP logical entity [1]

## Slide 3: Multi-link Capability and Setup
An ML AP logical entity and ML non-AP logical entities can have different ML capabilities (e.g., Number of links, Supported band/bandwidth)
Therefore, we need to discuss how and what ML capabilities information the ML AP logical entity and the ML non-AP logical entities should be negotiated during the ML setup

## Slide 4: Multi-link Setup Procedure
ML AP logical entity and ML non-AP logical entities would negotiate multi-link capability through one or more links
  Basically, the ML AP logical entity doesn’t know scanning channels of all non-APs of ML non-AP logical entities to be associated if the channels aren’t pre-determined in 11be
  Therefore, it would be better for the ML AP/non-AP logical entities to include all link-relevant information in each link to enable multi-link setup through one association [2]
ML AP logical entity would announce
its ML capabilities and Operation parameters (e.g., BSS channel information)
ML non-AP logical entity would announce
its ML capabilities

## Slide 5: ML Capabilities
ML Capabilities would be included in management frames for multi-link setup
  Probe Request/Response, Beacon, Association Request/Response frames, …
ML Capabilities can have Common and Per link information
  Common information can include the followings
    Number of Links per band, …
  Per link information can include the followings
    Link identifier, Band, Supported bandwidth, other capabilities,…
  Example (can be changed)

## Slide 6: Operation Parameters
Generally, Operation element includes operation parameters such as BSS channel information
  HT Operation element in 2.4GHz
  HT/VHT/HE Operation element in 5GHz
  HE Operation element in 6GHz
ML AP logical entity would include EHT Operation element in Beacon or (Re)Association response to announce operation parameters of each link
  It would be good not to modify (already existing) HT/VHT/HE operation element for legacy non-APs
We can have two options to indicate them, as follows
  Option 1: New composition for all links
  Option 2: Modifying and adding existing operation elements for each band

## Slide 7: Part of EHT Operation Element
Option 1: New composition
  It can be similar to 6GHz operation parameters in HE operation element
    Primary channel, Channel Width, CCFS,…
  Additional information can be included (e.g., Link ID, band information, and other information)
Option 2: Modifying and adding existing operation elements
  Using HT OE in 2.4GHz, HT/VHT OE combination in 5GHz, HE OE in 6GHz
  Some information for multi-link needs to be added, which may make it complex

## Slide 8: Discussion on Link Selection
Legacy Wi-Fi system uses a single link, i.e., non-APs can use the link based on the single link operation parameters from AP without any selection
However, 11be supports multi-link, which would require the link selection due to different multi-link capabilities

## Slide 9: Link Selection for Multi-link non-AP logical entity
Based on ML non-AP logical entity’s ML capabilities information, ML AP logical entity can select links which non-APs of ML non-AP logical entity can enable
  It would be included in Association Response
  ML non-AP logical entity may inform preferred links of ML AP logical entity in Association Request
  How to select links may be out of scope of 11be
For notification, ML AP logical entity may use EHT operation element or new element
  Option 1: Transmitted EHT operation element includes operation parameters of selected link only
  Option 2: Transmitted EHT operation element includes additional several information (e.g., link availability, AID)
  Option 3: New element can be used

## Slide 10: Example of Multi-link Setup Procedure

## Slide 11: Summary
We have discussed the multi-link setup for negotiating multi-link capability between Multi-link capable devices
Specifically, how and what ML capabilities information the ML AP logical entity and the ML non-AP logical entities, and link selection for the multi-link operation was discussed

## Slide 12: SP #1
Do you support that multi-link capabilities and operation parameters transmitted by a multi-link AP logical entity include those of all links supported by the multi-link AP logical entity?
  Specific information of multi-link capabilities and operation parameters of multi-link AP logical entity is TBD
Y/N/A

## Slide 13: SP #2
Do you support that multi-link capabilities transmitted by a multi-link non-AP logical entity includes those of all links supported by the multi-link non-AP logical entity?
  Specific information of multi-link capabilities of multi-link non-AP logical entity is TBD
Y/N/A

## Slide 14: References
[1] 802.11-19/0773r2 Multi-link Operation Framework
[2] 802.11-19/0821r2 Multiple Band Operation Discussion