## Slide 1: EHT Power saving considering multi-link
Date: 2019-09-15
Authors:
Name | Affiliations | Address | Email
Jeongki Kim | LG Electronics | LG Seocho R&D Campus, Korea | jeongki.kim@lge.com
Suhwook Kim |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  | js.choi@lge.com
Insun Jang |  |  | insun.jang@lge.com
Sungjin Park |  |  | allean.park@lge.com
Taewon Song |  |  | taewon.song@lge.com

## Slide 2: Introduction
PAR for TGbe [1]
  5.5 Need for the Project:
    …
    With the high throughput and stringent real-time delay requirements of these applications, users expect enhanced throughput, enhanced reliability, reduced latency and jitter, and improved power efficiency in supporting their applications over WLAN.
In this contribution, we propose the enhanced power saving mechanism for EHT STAs in 11be

## Slide 3: Background
Operating Mode (OM) Control in 11ax [2]
  Non-AP STA can inform its AP of the bandwidth and number of spatial stream to receive the DL PPDU or transmit the UL PPDU by using OM Control field
  AP sends DL frame to the STA based on the requested Receive Operating Mode Indication (ROMI) and allocates the UL resource to the STA based on the requested Transmit Operating Mode Indication (TOMI)
  Example of ROMI
STA
AP
UL Data
BA
Rx NSS =2, Rx BW= 40MHz
RX
RX
RX
DL Data
BA
TX
STA requests new Rx NSS=1, Rx BW=20MHz
STA receives BA using
Rx NSS=2, Rx BW=40MHz
Rx NSS=1, Rx BW=20MHz
Accept
AP sends DL Data with new changed Rx values
(Rx NSS=1, Rx BW=20MHz)

## Slide 4: Background
TWT operation in 11ax [2]
  Individual TWT: Non-AP STA wakes up every TWT service period negotiated with TWT REQ&RSP and sends/receives the frames with the associated AP
    The STA can enter the doze state until its TWT SP
  Broadcast TWT: Non-AP STA obtains the TWT information from the received Beacon every its TBTT negotiated with TWT REQ&RSP
    The STA can enter the doze state until the TBTT or its TWT service period
TWT req
TWT rsp
TWT SP
STA(1..n)
AP
Trigger
PS-Poll
M-BA
DL MU PPDU
BA
Doze

## Slide 5: Background
Intra-PPDU Power save in 11ax [2]
  When an HE non-AP STA receives a PPDU, the STA can enter the doze state until the end of the PPDU if the PPDU is determined as Intra-BSS PPDU using the following field
    In HE-SIGs: BSS Color, UL/DL flag, STA ID
    In VHT-SIG: Partial AID of UL PPDU
    In MAC header: MAC address fields (e.g., RA, TA, BSSID)
Legacy Preamble
(L-SIG)
HE Preamble
(RL-SIG, SIG-A, …)
PSDU
BSS Color, UL/DL Flag, STA_ID
Doze State

## Slide 6: Motivation
One of main features in TGbe is multi-band/multi-link operation [1], [3]~[8]
  A single device can support the multiple links and the data of the device can be delivered to another device through the multiple links
  Multi-link feature can increase the peak/average throughput of the device but require more complexity, cost, or power of the device
In this contribution we propose some enhanced power saving mechanisms considering multi-link feature
Device A
Device B
Link 1
Link 2
Data 1
Data 2
Data 3
Data 4

## Slide 7: OM Control for 11be
When an EHT device supporting the multi-link wants to reduce its power consumption, the STA can enable only one link and disable the other links using operating mode control
  A link may be disabled through different link
STA can enable the disabled links when the STA wants it
Link 1
Link 2
UL Data
BA
STA requests to disable Link 2
STA receives frame on only Link 1
BA
Link 1
Link 2
UL Data
AP
STA
Link 1 &2 is enabled
UL Data
BA
Disabled
DL Data
BA

## Slide 8: TWT operation for 11be (1/2)
A STA can setup the TWT SPs for multi-links through a link
The STA can enable only one link for TWT operation for more power saving (i.e., the other links will be disabled)
Link 1
Link 2
STA
TWT setup (link1&2)
TWT SP
TWT SP
TWT SP
TWT SP
Link 1
Link 2
STA
TWT setup (only link1,
Disable link2)
TWT SP
TWT SP
Power saving (e.g.,
doze state or disabling)
Power saving (e.g.,
doze state or disabling)

## Slide 9: TWT operation for 11be (2/2)
STA can enable disabled link(s) when the STA wants it or the AP command it during TWT SP
Link 1
Link 2
STA
TWT setup (only link1,
Disable link2)
TWT SP
Link 2
Link 1
AP
PS-Poll
RSP
Enable link 2
Enable link 2
DL frame
DL frame
Power saving (e.g.,
doze state or disabling)

## Slide 10: Intra-BSS PPDU PS for 11be
When an AP sends EHT PPDU via only a link, the AP can indicate if the other link (s) is available or not
The other link (s) of AP may not be available because
  Intra-BSS STA sends UL frame to the AP via the other link
  OBSS STA sends a frame via the other link and thus the strong interference exists
In that case, an Intra-BSS STA can disable the indicated link and enter the doze state for link 2
Link 1
Link 2
STA 1
Link 2
Link 1
AP
Disable link 2
DL frame TX
UL frame RX
Unavailability of link 2
Power saving (e.g.,
doze state or disabling)

## Slide 11: Conclusion
We need to consider the power efficiency of EHT STAs for 11be
We proposed some enhanced power saving mechanisms considering the multi-link concept
  OM Control
  TWT operation
  Intra-BSS PPDU Power save

## Slide 12: Reference
[1] 11-18/1231r6, EHT Proposed PAR
[2] Draft P802.11ax D4.3
[3] 11-18/1171, View on EHT objectives and technologies
[4] 11-18/1525, EHT features for Multi-Band Operation
[5] 11-18/1908, Overview of Full Duplex over Multi- Band (FD-MB) for EHT
[6] 11-19/773, Multi-link Operation Framework
[7] 11-19/777, Performance on Multi-band Operation
[8] 11-19/823, Multi-Link Aggregation

## Slide 13: Straw Poll 1
Do you agree to add the following into the TGbe SFD?
  When an EHT STA operating in multi-links wants to reduce more its power consumption, the STA can disable a part of multiple links operated by the STA and enable the disabled link(s) by using operating mode control procedure

## Slide 14: Straw Poll 2
Do you agree to add the following into the TGbe SFD?
  An EHT STA with multi-link capability can set up the TWT Service Periods for multiple links through a link

## Slide 15: Straw Poll 3
Do you agree to add the following into the TGbe SFD?
  An EHT STA with multi-link capability can request to the EHT AP the TWT Operation only through one link

## Slide 16: Straw Poll 4
Do you agree to add the following into the TGbe SFD?
  An EHT AP with multi-link capability can request for the EHT STA to enable the disabled link of the STA

## Slide 17: Straw Poll 5
Do you agree to add the following into the TGbe SFD?
  When an EHT AP with multi-link capability sends a EHT PPDU through a link, the AP can inform EHT STAs of whether other links is available or not through the EHT PPDU
    The detailed method is TBD

## Slide 18: Straw Poll 6
Do you agree to add the following into the TGbe SFD?
  When an EHT STA with multi-link capability receives an EHT PPDU through a link from an EHT AP, if the other link(s) is not available by the AP, the EHT STA can disable the other link(s) until the end of the PPDU