## Slide 1: Multi-link acknowledgment
Date: 2019-09-10
Authors:
Name | Company | Address | Phone | Email
Rojan Chitrakar | Panasonic Corporation |  |  | rojan.chitrakar@sg.panasonic.com
Lei Huang |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Overview
Multi-link transmission is being considered as one of the key technology to achieve the peak throughput goal of 802.11be.
In [1], we shared our opinions on some of the topics related to multi-link transmissions.
In this contribution, we will discuss the topic of acknowledgment for multi-link transmissions in more detail and propose the concept of multi-link block ack.

## Slide 3
Recap: Multi-link transmission [1]
In order to improve the peak throughput, MPDUs belonging to the same TID may be simultaneously transmitted over multiple links.
  At TX side UMAC performs the allocation of MPDUs to different links. The same SN space is used across all links.
  At RX side UMAC consolidates the MDPUs arriving over the different links, performs BA scoreboarding, MPDUs reordering etc.
  A consolidated acknowledgment may be transmitted over one of the links.

## Slide 4
Existing Block Ack setup mechanism
Block Ack mechanism is setup between an originator STA and a recipient STA by exchanging ADDBA Request/Response frames.
If existing Block Ack setup mechanism is used for multi-link transmissions, one possible option is to perform Block Ack setup (in each direction) between each pair of STAs between two Multi-link Entities.

## Slide 5
Existing Block Ack setup mechanism
The parameters of the Block Ack mechanism is negotiated by exchanging ADDBA Request/Response frames:
  TID: TID for the Block Ack mechanism
  Buffer Size: number of buffer for this particular TID
  Block Ack Timeout Value: duration in TUs after which the block ack setup is terminated.
  Block Ack Starting Sequence Control: sequence number of the first MSDU to be sent under this block ack agreement.
For multi-link transmissions of a particular TID, the Block Ack Starting Sequence Control may specify the same sequence number for all links.

## Slide 6
Possible limitations of per-link Block Ack
Since the MPDUs of a particular TID may be dynamically assigned to different links (e.g. due to channel access delays), the BA bitmaps of different links may cover the same sequence number range:
  Many of the bits of the BA bitmap can be expected to be ‘0’:
    Duplication/waste of bitmaps
    May cause confusion for the originator
  Transmission of immediate block ack may cause reception in other links to fail if the multi-link recipient is affected by in-device coexistence interference.

## Slide 7
Proposal: Multi-link Block Ack Setup
A single Multi-link Block Ack is setup between two Multi-link Entities for a multi-link TID.
Example: Multi-band elements in the ADDBA Request/Response frames can indicate the links for which the Multi-link Block Ack applies:
  The Block Ack parameters apply to all the involved links. Buffer Size needs to account for all involved links.
  The RA, TA fields may indicate the single MAC addresses (if applicable) assigned to the Multi-link Entities. Else indicate the MAC addresses associated with the links on which the setup frames are transmitted/received.

## Slide 8
Proposal: Multi-link Block Ack
Once the Multi-link Block Ack has been setup, in situations where per-link BA is not possible, a single Multi-link BlockAck frame may be used to acknowledge the MPDUs received over multiple links:
  The Block Ack bitmap consolidates the receipt status of the MPDUs received over multiple links.
  A Multi-link BlockAck Request frame may be transmitted over any one link to solicit the Multi-link BlockAck frame. The Multi-link BlockAck frame may be solicited on a link that does not cause in-device coexistence interference.

## Slide 9
Multi-link BlockAck frame
Example: A “Multi-link” bit in the BA Control field may be used to denote a Multi-link BlockAckReq/BlockAck frame.
The length of the Block Ack Bitmap of a Multi-link BlockAck frame may be increased (e.g. 128 octets or 256 octets) to acknowledge the higher number of MPDUs transmitted over multiple links.

## Slide 10
Conclusion
In this contribution, we discussed the setup mechanism of Multi-link Block Acks.
  To simplify the setup process, we propose that a single Multi-link Block Ack agreement is setup between two Multi-link Entities for a multi-link TID.
We also discussed the possible limitations of using per-link Block Ack frames to acknowledge multi-link transmissions.
  We propose that in situations where per-link BA is not possible, a single Multi-link BlockAck frame may acknowledge the MPDUs received over multiple links.

## Slide 11: Reference
IEEE 802.11-19/1128r0 – Multi-link transmission
IEEE 802.11-19/818r0 - Discussion on Multi-band operation
IEEE 802.11-19/773r1 - Multi-link Operation Framework
IEEE 802.11-19/823r0 - Multi-link aggregation
IEEE 802.11-19/979r0 - EHT Multi-link Operation Follow-up
IEEE 802.11-19/1291r1 - Performance aspects of Multi-link operations
IEEE 802.11-19/1213r0 – Discussion on Multi-link Operations

## Slide 12
Straw Poll 1
Do you support that a single Multi-link Block Ack agreement is setup between two Multi-link Entities for a multi-link TID (a TID that may be transmitted over multiple links)?
  The format of the setup frames is TBD.
  Y/N/A

## Slide 13
Straw Poll 2
Do you support that a common sequence space is used for MPDUs of the same TID transmitted over multiple links?
  Y/N/A

## Slide 14
Straw Poll 3
Do you support that a single BlockAck frame may indicate the receipt status of MPDUs received over multiple links?
  The format of the BlockAck frame is TBD.
  Y/N/A