## Slide 1: Further Thoughts on 11be Tone Plan
Date: 2019-09-16
Authors:
Name | Affiliations | Address | Phone | Email
Bin Tian | Qualcomm |  |  | btian@qti.qualcomm.com
Alice Chen |  |  |  | 
Lin Yang |  |  |  | 
Youhan Kim |  |  |  | 
Sameer Vermani |  |  |  | 
Steve Shellhammer |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
We have discussed the 11be tone plan in [1] and received strong support in SPs on following proposals on 11be
  Use the same subcarrier spacing for the data portion as in 11ax
  Reuse 11ax tone plan for 20/40/80/160/80+80MHz PPDU
  Add new 320/160+160MHz PPDU
  Use duplicated HE160 for 320/160+160 MHz OFDMA tone plan
In this presentation, we will further discuss the tone plan for
  320/160+160MHz Non-OFDMA
  240/160+80 MHz

## Slide 3: Non-OFDMA 320/160+160MHz
For 160+160MHz PPDU, it is desirable that each 160MHz segment reuses the same tone plan as the 160 MHz PPDU
  Defining two tone plans for 160MHz increases the complexity
For 320MHz PPDU, it is desirable to have the same tone plan as in the 160 + 160MHz case
  Implementation flexibility: allow using two chains (160+160) implementation to support contiguous 320MHz
  Simplicity: each 160MHz segment is the same as in 11ax, regardless of 160+160 or 320 MHz
  Efficiency percentage gain from having a special tone plan just for 320 MHz non-OFDMA mode is insignificant
    Even assume the best case of a new tone plan, there is 4096-(11+12) edge tones – 5 DC = 4068 total usable tone, which is only about 2% more than the existing simple 4x996 plan
Recommend that non-OFDMA 320/160+160MHz uses duplicated HE 160MHz tone plan, the same as in the OFDMA case

## Slide 4: 240/160+80 MHz Transmission
240/160+80 MHz transmission is useful when an 80MHz segment in 320/160+160MHz channel is occupied by incumbent or OBSS
For 160+80MHz transmission
  The 160 MHz segment uses the same tone plan as the EHT 160 which is the duplicated two EHT80
  The 80 MHz segment uses the same tone plan as EHT80
For 240 MHz transmission
  Due to non factor-2 FFT needed for 240 MHz, implementation may choose to use punctured 320 MHz or two chains 160+80 to support 240 MHz transmission
  It is desirable that 240MHz has the same tone plan as 160+80
Recommend the tone plan of 240/160+80 consists of 3x 80MHz while each 80MHz segment is the same as in HE80

## Slide 5: Straw Poll 1
Do you support adding 320MHz and 160+160MHz PPDUs to 11be?
  Already passed the SP
  Y: 61
  N: 0
  A: 13

## Slide 6: Straw Poll 2
Do you support the 11be uses the same subcarrier spacing for the data portion of EHT PPDU as 11ax data portion?
Already passed the SP
  Y: 70
  N: 0
  A: 10

## Slide 7: Straw Poll 3
Do you support the following EHT tone plans?
  Reuse 11ax tone plan for 20/40/80/160/80+80MHz
  320MHz and 160+160MHz use duplicated HE160 for OFDMA tone plan
  Note: puncturing design TBD. Non-OFDMA 320MHz/160+160MHz tone plan TBD
Already passed the SP
  Y : 42
  N : 0
  A :37

## Slide 8: Straw Poll 4
Do you support in 11be the 320/160+160 MHz non-OFDMA tone plan uses duplicated HE160?
  Note: puncturing design TBD.
  Y
  N
  A

## Slide 9: Straw Poll 5
Do you agree with in 11be the 240/160+80 transmission consists of 3x 80MHz while each 80MHz segment is the same as HE80 in 11ax?
  Y
  N
  A

## Slide 10: Motion 1
Move to add the following to the 11be spec framework document
  11be reuses 11ax tone plan for 20/40/80/160/80+80MHz PPDU
  For 320MHz and 160+160MHz PPDU, 11be uses duplicated HE160 for OFDMA tone plan
Move: Bin Tian Second:

## Slide 11: Motion 2
Move to add the following to the 11be spec framework document
The 11be 320/160+160 MHz non-OFDMA tone plan uses duplicated tone plan of HE160
  Note: puncturing design TBD
Move: Bin Tian Second:

## Slide 12: Motion 3
Move to add the following to the 11be spec framework document
11be 240/160+80 transmission consists of 3x80MHz segments while the tone plan of each 80MHz segment is the same as HE80 in 11ax
Move: Bin Tian Second:

## Slide 13: References
[1] Alice Chen, et. al., “320MHz Channelization and Tone Plan,” IEEE 802.11-19/0797r1, May 2019
[2] Eunsung Park, et. al., “Consideration on 320MHz Bandwidth and 16 Spatial Streams,” IEEE 802.11-19/0778r0, May 2019
[3] Eunsung Park, et. al., “Tone Plan Discussion,” IEEE 802.11-19/1066r0, July 2019