## Slide 1: Multi-link: Link Management
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2019-09-04

## Slide 2: Overview
There have been several presentations proposing a single association for multi-link setup [1][2][3]
Other contributions [1, 2, 4] have discussed how the unified framework can support packet-level aggregation and dynamic transfer of a TID between links.
Contribution [5] discusses TID-to-link mapping
This contribution discusses the topic of link enablement

## Slide 3: Motivation
A single radio client performs multi-link association for more than one link
  The device can operate on only one link at any time.
  MLO framework needs to provide a mechanism for (non-AP) entity to indicate disablement of link(s).
A multi-radio client device performs multi-link association for 2.4/5/6 GHz and indicates its capability to operate on two links at a time.
  Device shares a common radio between 5 GHz and 6 GHz link and therefore can operate on only one of the two bands at any time.
  MLO framework needs to provide a mechanism for an entity to indicate disablement of a certain link.

## Slide 4: Motivation
AP Power-save:
  An AP entity disables subset of links during off-peak hours
    For example, AP entity in a home setting shrinks operations to a single link during the night
    AP entity won’t be available to receive frames on the disabled link(s)
  MLO framework needs to provide a mechanism for an (AP) entity to indicate disablement of link(s) for all ML-capable STAs
Load balancing:
  An AP entity disables a subset of links for a STA while letting other STAs to exchange frames on one or more of the disabled link(s)
    AP may do so for loading balancing reasons
  MLO framework needs to provide a mechanism for an (AP) entity to indicate disablement of link(s) for a particular ML-capable STA
Co-ex conditions:
  A soft-AP may disable a link for co-ex reasons
    e.g., A softAP disables 2.4 GHz link for the duration of a BT session
    During such time, the AP entity is not available on disabled link
  MLO framework needs to provide a mechanism for an entity to indicate disablement of a certain link.

## Slide 5: Link Enablement
MLO framework needs to provide mechanism for entities to signal enablement or disablement of link(s)
Two examples of such signaling are discussed:
  Example 1: Explicit signaling to indicate which of the mapped links are enabled
  Example 2: TID-to-link mapping implicitly indicates enablement

## Slide 6: Example 1: Explicit enablement
Link enablement is independent of TID-to-link mapping
Involves dynamically enabling link(s) based on availability of an entity on a link
  Either entity could initiate a change
Disablement of a link makes it unavailable for all TIDs mapped to that link

## Slide 7: Example 1: Explicit enablement

## Slide 8: Example 2: Implicit enablement
Link enablement procedure is part of the TID-to-link mapping operation
  The mapping process indicates the links which are ‘enabled’ to transfer a TID.
Either peer entity can initiate the remapping process if there is a need to change to the link status (enabled/disabled)
If all the TIDs are not mapped to a link, that link is not in use.

## Slide 9: Example 2: Implicit enablement

## Slide 10: Power-save
Power-save mechanism is independent of link management
Existing power management schemes are utilized for power-save on enabled links
  Each non-AP STA instance of an MLLE on an enabled link independently maintains its own power states/modes defined in the existing spec

## Slide 11: Summary
This contribution clarifies the need to indicate enablement of a link that is setup part of a multi-link association
The contribution provides two options for indicating enablement/disablement of a link.

## Slide 12: Straw Poll 1
Do you support defining a link, that is setup as part of a multi-link association, as Enabled if that link can be used for frame exchange?
  Note: frame exchange is subject to the power states of corresponding STAs
  Y:
  N:
  A:

## Slide 13: Straw Poll 2
Do you support that the 802.11be amendment shall define a TBD signaling, within multi-link operation, to dynamically enable/disable link(s)?
  Y:
  N:
  A:

## Slide 14: Straw Poll 3
Do you agree that each non-AP STA instance (of an MLLE) maintains its own power-state/mode on enabled link(s)?
  Y:
  N:
  A:

## Slide 15: Appendix

## Slide 16: Reference
[1]: 11-19-0773
[2]: 11-19-0823
[3]: 11-19-0821
[4] : 11-19-1082
[5] : 11-19-0979

## Slide 17: Dynamic TID Link Switch [4]

## Slide 18: Shared radio

## Slide 19: AP Power save