## Slide 1: Discussion on Multi-link Acknowledgement
Date: 2019-9-16
Authors:
Name | Company | Address | Phone | Email
Ryuichi Hirata | Sony Corporation |  |  | Ryuichi.Hirata@sony.com
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka@sony.com
Kosuke Aio |  |  |  | Kosuke.Aio@sony.com

## Slide 2: Overview
We provided observations on potential QoS issues which could occur in multi-link operation[1].
In this contribution, we discuss details of one of the QoS issues related to ARQ (issue 2: unnecessary retransmission in [1]) and propose multi-link acknowledgement mechanism for synchronous and independent multi-link aggregation.

## Slide 3: Unnecessary retransmission
Unnecessary retransmission could be occurred due to unmanaged interference.
  In figures below, a block ack on link1 contains acknowledgement for data#1 and a block ack on link2 contains acknowledgement for data#2.
  If there are unmanaged interference on link2, an AP fails to receive the block ack on link2.
  In this case, the AP can’t recognizes whether data#2 is correctly received at the STA, so the AP initiates retransmission of data#2. The same thing happens in linke1.
    Note: this problem itself could occur in case of single band transmission.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA
BA
Data#2 (Re)
AP fails to receive
BA @link2
Unnecessary
retransmission
Data#1
Data#2
BA
BA
Data#2 (Re)
AP fails to receive
BA @link2
Unnecessary
retransmission

## Slide 4: Observation on unnecessary retransmission
We assume the case that the AP receives block ack on link1 correctly while the AP fails to receive block ack on link2.
If block ack on link2 contains acknowledgement for data#1 and #2, the AP can recognize data#1 is received by the STA correctly. After receiving the block ack, the AP can transmit next data.
It must be beneficial that the STA sends block ack on link1 and link 2 for redundancy and reliability improvement.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA
BA
Data#2 (Re)
AP fails to receive
BA @link2
Unnecessary
retransmission

## Slide 5: Proposal of multi-link acknowledgement
IEEE 802.11be should include mechanism to transmit a block ack which contains acknowledgement for all data received over all links on one ore more links.
This mechanism is easily applied to synchronous aggregation because reception end time of data#1 and data #2 are synchronized and transmission start time of immediate block ack on link1 and link2 are synchronized.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1)
BA (Data#1)
AP fails to receive
BA @link2
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1, 2)
BA (Data#1, 2)
AP can get
Acknowledgement
for all data

## Slide 6: Considerations on independent aggregation
The proposed mechanism is suitable for synchronous aggregation, but there are some considerations to apply it to independent aggregation.
  In independent aggregation, reception end time of data are independent between links, and transmission start time of block acks between links are also independent.
    The AP can’t always adjust PPDU length to finish transmission of data due to buffered data mount, MCS or available resource.
  The STA can’t send a block ack which contains acknowledgement for all data received over all links on a link where end time of data is earlier than other links.
    In this case, unnecessary retransmission occurs if the AP fails to receive a block ack which contains acknowledgement for all data received over all links.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1)
BA (Data#1,2)
Data#2 (Re)
AP fails to receive BA @link2
Unnecessary retransmission

## Slide 7: Observation on independent aggregation
One of possible solution for independent aggregation is to send block acks after the last reception end time of data.
  In the figure below, first the AP initiates transmission of data#1 on link 1, then the AP initiates transmission of data#2 on link 2.
  Even when the transmission of data#1 finished, a STA will wait until reception end time of data #2 without sending block ack on link 1.
  After the end time of data #2, the STA sends block acks on link 1 and link 2.
This sequence allows to send a block ack which contains acknowledgement for all data received over all links.
However, this sequence causes unsolicited but not immediate block ack transmission that is not regular operation of 802.11 specification.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1,2)
BA (Data#1,2)
Unsolicited but not immediate block ack

## Slide 8: Proposals of multi-link acknowledgement for independent aggregation
  Another possible solution for independent aggregation is to send block ack request to solicit block acks after the last reception end time of data.
  Block ack request is well accepted existing mechanism to solicit block ack.
  Block ack request enables transmitting block acks which contain acknowledgement for data received over multiple links.
  Block ack request can be sent on one or more links.
  Block ack request is compatible with UL MU transmission.
  IEEE 802.11be should include mechanism to transmit block ack requests on one or more links that trigger block acks that include acknowledgement for data received on multiple links.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1,2)
BA (Data#1,2)
BAR
BAR

## Slide 9: Conclusion
Unnecessary retransmission is one of the QoS issues. Enhancement of acknowledgement mechanism in multi-link operation could solve this issue.
IEEE 802.11be should include following mechanisms;
  mechanism to transmit a block ack which contains acknowledgement for all data received over all links on one ore more links.
  mechanism to transmit block ack requests on one or more links that trigger block acks that include acknowledgement for data received on multiple links.

## Slide 10: Reference
[1] 11-19-0818-01-00be-discussion-on-multi-band-operation

## Slide 11: SP1
Do you agree that IEEE 802.11be should include mechanism to transmit a block ack which contains acknowledgement for all data received over all links on one ore more links?

## Slide 12: SP2
Do you agree that IEEE 802.11be should include mechanism to transmit block ack requests on one or more links that trigger block acks that include acknowledgement for data received on multiple links?