## Slide 1: Discussion on Multi-link Acknowledgement
Date: 2019-9-16
Authors:
Name | Company | Address | Phone | Email
Ryuichi Hirata | Sony Corporation |  |  | Ryuichi.Hirata@sony.com
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka@sony.com
Kosuke Aio |  |  |  | Kosuke.Aio@sony.com

## Slide 2: Overview
Authors provided observations on potential QoS issues which could occur in multi-link operation[1].
In this contribution, we discuss details of one of the QoS issues related to ARQ (Issue 2: unnecessary retransmission in [1]) and propose multi-link acknowledgement mechanism for synchronous and independent multi-link aggregation.

## Slide 3: Unnecessary Retransmission
Unnecessary retransmissions may occur due to unmanaged interference.
  In figures below, a block ack on link1 contains acknowledgement for data#1 and a block ack on link2 contains acknowledgement for data#2.
  If there is unmanaged interference on link2, an AP fails to receive the block ack on link2.
  In this case, the AP can’t recognize whether data#2 is correctly received at the STA, so the AP initiates retransmission of data#2. The same thing happens in link1.
    Note: This problem also occurs in the case of single link transmission. Our internal simulations show that 5-15% block ack frames failed in TGax simulation scenarios (Residential, Enterprise and Indoor Small BSSs).
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
Data#2 (Re)
AP fails to receive
BA @link2
Unnecessary
retransmission
BA (Data#1)
BA (Data#2)
Data#1
Data#2
Data#2 (Re)
AP fails to receive
BA @link2
Unnecessary
retransmission
BA (Data#1)
BA (Data#2)

## Slide 4: Observations Regarding Unnecessary Retransmissions
We assume the case that the AP receives block ack on link1 correctly while the AP fails to receive block ack on link2.
If block ack on link2 contains acknowledgement for data#1 and #2, the AP can recognize data#1 is received by the STA correctly. After receiving the block ack, the AP can transmit next data.
It is desirable that the STA sends block ack on both link1 and link 2 for redundancy and reliability improvement.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
Data#2 (Re)
AP fails to receive
BA @link2
Unnecessary
retransmission
BA (Data#1)
BA (Data#2)

## Slide 5: Proposal of Multi-Link Acknowledgement
IEEE 802.11be should include a mechanism to transmit a block ack which contains acknowledgement for data received over multiple links on one or more links.
This mechanism is easily applied to synchronous aggregation because reception end time of data#1 and data #2 are synchronized and transmission start time of immediate block ack on link1 and link2 are also synchronized.
  If STA could not collect acknowledgement for data received over multiple links in SIFS immediately, then delayed block ack should be used.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1)
BA (Data#2)
AP fails to receive
BA @link2
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1, 2)
BA (Data#1, 2)
AP can get
acknowledgement
for all data

## Slide 6: Considerations on Independent Aggregation
The proposed mechanism is suitable for synchronous aggregation, but there are additional considerations to apply it to independent aggregation.
  In independent aggregation, reception end time of data are independent between links, and transmission start time of block acks between links are also independent.
    The AP can’t always adjust PPDU length to finish transmission of data due to buffered data mount, MCS or available resource.
  The STA can’t send a block ack which contains acknowledgement for data received over multiple links on a link where end time of data is earlier than other links.
    In this case, unnecessary retransmission occurs if the AP fails to receive a block ack which contains acknowledgement for data received over multiple links.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1)
BA (Data#1,2)
Data#2 (Re)
AP fails to receive BA @link2
Unnecessary retransmission

## Slide 7: Observations on Independent Aggregation
One of possible solution for independent aggregation is to send block acks after the last reception end time of data.
  In the figure below, first the AP initiates transmission of data#1 on link 1, then the AP initiates transmission of data#2 on link 2.
  Even when the transmission of data#1 is complete, a STA will wait until reception end time of data #2 without sending block ack on link 1.
  After the end time of data #2, the STA sends block acks on link 1 and link 2.
This sequence allows to send a block ack which contains acknowledgement for data received over multiple links.
However, this sequence causes unsolicited but not immediate block ack transmission that is not a normative operation of 802.11 specification.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1,2)
BA (Data#1,2)
Unsolicited but not immediate block ack

## Slide 8: Proposals of Multi-Link Acknowledgement for Independent Aggregation
  Another possible solution for independent aggregation is to send block ack request to solicit block acks after the last reception end time of data.
  Block ack request is a well-accepted existing mechanism to solicit block ack.
  Block ack request enables transmitting block acks which contain acknowledgement for data received over multiple links.
  Block ack request can be sent on one or more links.
  Block ack request is compatible with UL MU transmission.
  IEEE 802.11be should include a mechanism(s) to transmit block ack requests on one or more links that trigger block acks which include acknowledgement for data received over multiple links.
AP@link1
Data#1
AP@link2
STA@link1
STA@link2
Data#2
BA (Data#1,2)
BA (Data#1,2)
BAR
BAR

## Slide 9: Conclusion
Unnecessary retransmission is one of the primary QoS issues to be addressed in Multi-Link. Enhancement of the acknowledgement mechanisms in Multi-Link operation could solve this issue.
IEEE 802.11be should include following mechanisms;
  mechanism to transmit a block ack which contains acknowledgement for data received over multiple links on one or more links.
  mechanism to transmit block ack requests on one or more links that trigger block acks which include acknowledgement for data received over multiple links.

## Slide 10: Reference
[1] 11-19-0818-01-00be-discussion-on-multi-band-operation

## Slide 11: SP1
Do you support that the SFD includes the following statements:
  The amendment shall define a mechanism to transmit a block ack frame on one or more links to indicate the acknowledgement for data received over multiple links.

## Slide 12: SP2
Do you support that the SFD includes the following statements:
  The amendment shall define a mechanism to transmit a block ack request frame on one or more links that trigger block acks that indicate acknowledgement for data received over multiple links?