## Slide 1: Use of Uplink Persistent Allocation for RTA
Date: 2019-09-16
Authors:
Name | Company | Address | Phone | Email
Xin Zuo | Tencent | Tencent Building, Kejizhongyi Avenue, Hi-tech Park, Nanshan District, Shenzhen | +86-18621746207 | xinzuo@tencent.com
Kate Meng |  |  |  | 
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Background
Uplink persistent allocation (UPA) has been proposed to be enabled for 11be UL MU transmission for overhead reduction [1]
  For an UPA, resource allocation information is unchanged for a time period.
UPA can be used to shorten some specialized Trigger frames (e.g. BSRP, BQRP, etc) since the solicited UL OFDMA responses have small fixed size [1].
  In this contribution, we propose UPA can also be used to shorten basic Trigger frames for soliciting TB PPDU transmission carrying RTA traffic.

## Slide 3
RTA Challenge
RTAs are latency-sensitive.
  Several milliseconds could be desired.
Challenging to satisfy the latency requirements
  There will be even more devices, more applications/services running over Wi-Fi networks in the future.
  Unlicensed spectrum.
Even more challenging to satisfy the UL latency requirement.
  Basic trigger frame of 11ax could be helpful.

## Slide 4
Feasibility of Applying UPA to RTA
RTA UL traffic pattern:
  Typical mobile gaming:
    payload is a few hundreds of Bytes, and rarely larger than 500 Bytes.
    one service session lasting for a few minutes to ~20 minutes.
    1~3 users under the same Wi-Fi in home, and many more, up to 10~20, in café/restaurant/e-sport events.
  Therefore, the data rate required for gaming is about 10K~100K bps.
    A small fraction of spectrum resource can be assigned to RTAs as their UPA, for a relatively long period.
    HE-MCS 0 for 26-tone RU, either GI, could be sufficient for RTA UPA.
Chart: Tx time diff. (×10ms)
| 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100 | 100-110 | 110-120 | 120-130 | 130-140 | 140-150 | 150-160 | 160-170 | 170-180 | 180-190 | 190-200 | 200-210 | 210-220 | 220-230 | 240-250 | 250-260 | 260-270 | 270-280 | 280-290 | 290-300 | 300-310 | 310-320 | 330-340 | 340-350 | 350-360 | 360-370 | 370-380 | 380-390 | 390-400 | 410-420 | 420-430 | 430-440 | 440-450 | 450-460 | 460-470 | 470-480 | 490-500
UL | 132.0874 | 115.9462 | 124.443 | 124.3217 | 110.2177 | 111.9424 | 118.0225 | 120.8172 | 119.0769 | 120.9123 | 112.5517 | 110.4706 | 120 | 118.3125 | 112.2857 | 114.6 | 114 | 120 | 120 | 93 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 93 | 120 | 128 | 120 | 120 | 120 | 120 | 122.6667 | 106.5 | 93 | 120 | 120 | 120 | 120 | 120 | 120
Chart: Tx time diff. (×10ms)
| <0 or (blank) | 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100 | 100-110 | 120-130 | 130-140 | 160-170 | 180-190
UL | 0 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70
Chart: Tx time diff. (×10ms)
| 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 170-180 | 300-310 | 310-320 | 460-470 | 490-500 | 1000-1010 | 1010-1020 | 1020-1030 | 1040-1050 | 1050-1060 | 1170-1180 | >1200
DL | 121.6752 | 113.4884 | 74.75 | 92.1 | 111.5 | 174 | 89 | 292.5 | 193 | 181 | 57 | 170 | 114 | 115.133 | 108.8592 | 90.6667 | 133 | 157.5 | 126 | 94
The coordinates (x,y) of the circle center represents the ( transmitting time difference, payload size). The area of the circle represents the percentage.
≈ 10 Kbps
≈ 100 Kbps
< 100 Kbps
The statistics are collected at Tencent servers.

## Slide 5
  Industrial automation:
    Data rate requirement is < 1Mbps [2].
    Devices usually are simple, battery-enabled, etc.
    Could transmit data in the similar pattern for very long period, or the entire battery life.
    Many sensors/users under the same Wi-Fi network.
  Therefore, UPA may keep unchanged for relatively long time, to reduce the trigger overhead in UL.
    HE-MCS 0 for 26-tone RU, either GI, could be sufficient for RTA UPA.
Feasibility of Applying UPA to RTA
From the RTA TIG report [2].

## Slide 6
Examples of Applying UPA to RTA
  For a 11ax basic trigger frame containing X User Info fields, the shortened basic Trigger frame has a size of 30 + 1*X octets, reduced from 30 + 6 * X octets.
    MAC header: 16 octets
    Common Info: 8 octets
    User Info List: 6 octets * X (11ax basic Trigger)  UPA Indication: 1 * X octet (shortened basic Trigger)
    Padding: 2 octets
    FCS: 4 octets
  The reduction of overhead is ~14% (for 1 RTA STA), up to 56% (for 10 RTA STAs).
    Assume the same rate is used for transmission of 11ax basic Trigger frame and shortened basic Trigger frame
Previous submission in [3] has also demonstrated the benefit of reducing overhead, based on the similar ideas.
Slide 8 in [3]

## Slide 7
Summary
RTAs are usually latency-sensitive, and small in packet size. Trigger frame helps improve the uplink latency.
UPA could reduce the basic trigger overhead in UL, especially when the number of RTA STAs is large.

## Slide 8: Reference
[1] 11-19-0806-02-00be-enabling-persistent-allocation-for-EHT, July 2019
[2] 11-18-2009-06-0rta-rta-report-draft.docx
[3] 11-19-1118-01-00be-enhancements-for-time-critical-data-transmission, July 2019