## Slide 1: Legacy Performance Impact on Multi-Link Operation
Date: 2019-09-14
Authors:

## Slide 2: Recap: Multi-link logical entity architecture
A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
AP
1
operating
on
2
.
4
GHz
AP
2
operating
on
5
GHz
AP
3
operating
on
6
GHz
Multi
-
link AP logical entity
Non
-
AP STA
1
Non
-
AP STA
2
Non
-
AP STA
3
Link
1
Link
2
Link
3
Multi
-
link non
-
AP logical entity

## Slide 3: Multi-link logical entity modeling
The multi-link logical entity can be modeled with legacy STAs as the following.
  The primary 80 MHz channels of STAa and STAb in the multi-link logical entity are associated with the link 1 and link 2 respectively.
  The secondary 80 MHz channels of STAa and STAb in the multi-link logical entity are associated with the link 2 and link 1 respectively.
STAa (80+80)
Multi-link logical Entity
STAb (80+80)
Link 1
Link 2
Primary 80 MHz of STAa
Secondary 80 MHz of STAb
Secondary 80 MHz of STAa
Primary 80 MHz of STAb

## Slide 4: Performance Evaluation
Reference throughput of legacy 802.11ac/ax WLAN
  BSS1 consists of four 80+80 MHz STAs whose the primary 80 MHz channels are associated with the link 1 and the secondary 80 MHz channels are associated with the link 2.
  BSS2 consists of four 80+80 MHz STAs whose the primary 80 MHz channels are associated with the link 2 and the secondary 80 MHz channels are associated with the link 1.
Link 1
Link 2
P80
STA1
S80
P80
STA2
S80
P80
STA3
S80
P80
STA4
S80
S80
STA5
P80
S80
STA6
P80
S80
STA7
P80
S80
STA8
P80
BSS1
BSS2

## Slide 5: Performance Evaluation
Reference throughput of legacy 802.11ac/ax WLAN
  Topology
    8 STA and 2 AP.
    STA is 5m away from AP.
      The received signal strength level is always greater than the ED level.
  Parameters:
    Bandwidth: 80 MHz
    MCS: 3 (11ac 117 Mbps)
    Full buffered uplink UDP traffic. Each UDP packet is 1460 bytes.
    TXOP Time: 5.4ms
    STA1-4 are associated with AP1. STA5-8 are associated with AP2.
  The average throughput of legacy STA is 22.91 Mbps.

## Slide 6: Performance Evaluation
Legacy throughput impact depending the MLO
  Comparing with the legacy 802.11ac/ax WLAN scenario, the STA4 and STA5 are replaced to the multi-link logical entity.
Link 1
Link 2
P80
STA1
S80
P80
STA2
S80
P80
STA3
S80
STAa
STAb
S80
STA6
P80
S80
STA7
P80
S80
STA8
P80
Multi-link logical Entity
BSS1
BSS2

## Slide 7: Performance Evaluation
Legacy throughput impact depending the MLO
  MLO types
    Basic MLO: The MLO has no constraint.
      MLO on multiple primary channels (MLO-MPC)
        Each STA of a MLLE performs EDCA procedure independently and can initiate a frame exchange only when the back-off timer associated with the STA is expired.
TXOP
TXOP
Busy
TXOP
TXOP
TXOP
TXOP
TXOP
Busy
TXOP
Link 1/5GHz
(Primary Ch)
(Primary Ch)
Link 2/6GHz

## Slide 8: Performance Evaluation
Legacy throughput impact depending the MLO
  MLO types
    Constrained MLO (CMLO): The MLO has a constraint that does not allow an overlapping of Tx and Rx within a TXOP.
      CMLO on single primary channel (CMLO-SPC)
        Single STA of a MLLE performs EDCA procedure and can initiate a frame exchange when the back-off timer associated with the STA is expired.
        And, the MLLE can use other link if the CS of that link is idle for PIFS.
TXOP
TXOP
Busy
TXOP
TXOP
TXOP
Busy
TXOP
TXOP
Link 1/5GHz
(Primary Ch)
Link 2/6GHz
Busy

## Slide 9: Performance Evaluation
Legacy throughput impact depending the MLO
  MLO types
    Constrained MLO (CMLO): The MLO has a constraint that does not allow an overlapping of Tx and Rx within a TXOP.
      CMLO on multiple primary channels (CMLO-MPC)
        Each STA of a MLLE performs EDCA procedure independently and can initiate a frame exchange only when the back-off timer associated with the STA is expired.
Link 1/5GHz
(Primary Ch)
(Primary Ch)
Link 2/6GHz
TXOP
Busy
TXOP
TXOP
TXOP
TXOP
TXOP
Busy
Tx

## Slide 10: Performance Evaluation
Legacy throughput impact depending the MLO
  MLO types
    Constrained MLO (CMLO): The MLO has a constraint that does not allow an overlapping of Tx and Rx within a TXOP.
      CMLO on multiple primary channels with a CS secondary access (CMLO-MPC+)
        Each STA of a MLLE performs EDCA procedure independently and can initiate a frame exchange only when the back-off timer associated with the STA is expired.
        And, the MLLE can use other link if the CS of that link is idle for PIFS.
Link 1/5GHz
(Primary Ch)
(Primary Ch)
Link 2/6GHz
TXOP
Busy
TXOP
TXOP
TXOP
TXOP
TXOP
Busy
Tx
Even though the back-off timer is not expired, if the CS is idle for PIFS, the STA can initiate a frame exchange.

## Slide 11: Performance Evaluation
Legacy throughput impact depending the MLO
  When STAs in the multi-link logical entity uses the MLO-MPC, the average throughput of legacy STA is 22.71 Mbps
    The primary 80 MHz channels of STAa and STAb in the multi-link logical entity are associated with the link 1 and link 2 respectively.
Link 1
Link 2
P80
STA1
S80
P80
STA2
S80
P80
STA3
S80
P80
STAa
STAb
P80
S80
STA6
P80
S80
STA7
P80
S80
STA8
P80
BSS1
BSS2
Multi-link logical Entity

## Slide 12: Performance Evaluation
Legacy throughput impact depending the MLO
  When STAs in the multi-link logical entity uses the CMLO-SPC, the average throughput of legacy STA is 27.21 Mbps.
    The primary 80 MHz channel and the secondary 80 MHz channel of STAa in the multi-link logical entity are associated with the link 1 and link 2 respectively.
Link 1
Link 2
P80
STA1
S80
P80
STA2
S80
P80
STA3
S80
P80
STAa
S80
S80
STA6
P80
S80
STA7
P80
S80
STA8
P80
BSS1
BSS2
Multi-link logical Entity

## Slide 13: Performance Evaluation
Legacy throughput impact depending the MLO
  When STAs in the multi-link logical entity uses the CMLO-MPC, the average throughput of legacy STA is 24.33 Mbps.
    The primary 80 MHz channels of STAa and STAb in the multi-link logical entity are associated with the link 1 and link 2 respectively.
Link 1
Link 2
P80
STA1
S80
P80
STA2
S80
P80
STA3
S80
P80
STAa
STAb
P80
S80
STA6
P80
S80
STA7
P80
S80
STA8
P80
BSS1
BSS2
Multi-link logical Entity

## Slide 14: Performance Evaluation
Legacy throughput impact depending the MLO
  When STAs in the multi-link logical entity uses the CMLO-MPC+, the average throughput of legacy STA is 22.38 Mbps.
    The primary 80 MHz channels of STAa and STAb in the multi-link logical entity are associated with the link 1 and link 2 respectively.
    The secondary 80 MHz channels of STAa and STAb in the multi-link logical entity are associated with the link 2 and link 1 respectively.
Link 1
Link 2
P80
STA1
S80
P80
STA2
S80
P80
STA3
S80
P80
STAa
S80
S80
STAb
P80
S80
STA6
P80
S80
STA7
P80
S80
STA8
P80
BSS1
BSS2
Multi-link logical Entity

## Slide 15: Overall Throughput Comparison
Chart: 2AP-8STA UDP Uplink (80 + 80)
| STA1 | STA2 | STA3 | STA4 | STA5 | STA6 | STA7 | STA8 | EHT STA | Avg Legacy STA
Baseline (80+80) | 22.788 | 22.976 | 23.12 | 22.35 | 22.828 | 20.912 | 23.528 | 24.136 | 45.178 | 22.91
MLO-MPC | 23.546 | 21.396 | 22.986 | 47.774 | 0 | 22.734 | 23.844 | 21.79 | 47.774 | 22.716
CMLO-SPC | 24.47 | 23.164 | 21.846 | 21.976 | 0 | 32.32 | 30.648 | 30.844 | 21.976 | 27.2153
CMLO-MPC+ | 21.108 | 23.51 | 22.286 | 42.66 | 0 | 23.752 | 20.332 | 23.294 | 42.66 | 22.3803
CMLO-MPC | 23.164 | 24.978 | 24.864 | 35.028 | 0 | 24.91 | 23.368 | 24.742 | 35.028 | 24.3377

## Slide 16: Conclusion
The MLO-MPC does not have any impact on the performance of legacy STA.
But, when the MLLE has a constraint on simultaneous Tx and Rx, both the CMLO-SPC and CMLO-MPC have some throughput loss and instead the legacy STA is taking more throughput gain.
  But, it seems that allowing the multiple primary channels shows the best operation mode for both the legacy STA and the EHT STA.