## Slide 1: Multi-Link Operation and Channel Access Discussion
Date: 2019-11-13
Authors:

## Slide 2: Motivation
In this proposal, we discuss the multi-link operation of the AP having an in-device coexistence (IDC) interference between multiple links (eg. 5 GHz & 6 GHz).

## Slide 3: Multi-Link Simulation Set Up
Topology
  13 STA and 3 AP.
  5 STA associated with AP1 are on Link 1. 5 STA associated with AP2 are on Link 2. The third BSS has 3 target EHT devices for throughput measurement.
Parameters:
  Background traffic
    Symmetrical UDP traffic on both links/channels.
    Different % of loading will be tested.
    Randomized TXOP limit between 1ms and 5.4ms for each AP <-> STA.
  Each UDP packet is 1460B.
  AMPDU setting
    Legacy and background traffic STA/AP use 64. EHT AP/STA uses 128.

## Slide 4: Multi-Link Simulation Set Up
AP1
STA1
BSS1
BSS2
Link 1
STA2
STA3
STA4
STA5
Link 1
Link 1
Link 1
Link 1
AP2
STA6
Link 2
STA7
STA8
STA9
STA10
Link 2
Link 2
Link 2
Link 2
EHT AP
Link 1/Link 2
BSS3
EHT STA
EHT STA
EHT STA

## Slide 5: Multi-Link Simulation Set Up
EHT AP configuration : Multiple Primary Channel based link access ()
Link 1
Link 2
STA 1
STA 2
busy
busy
3 | 2 | 1 | 0
4 | 3
2 | 1 | 0
3 | 2 | 1 | 0
2 | 1 | 0
1 | 0
MLLE
TXOP
TX
RX
TXOP
TX
RX
TXOP
TX
RX
TXOP
TX
RX
TXOP
TX
RX
  A STA of a MLLE performs a contention independently on each primary channel of the link 1 and the link 2.
  After obtaining a TXOP on either link, the MLLE transmits frames on the link on which the TXOP is obtained.
    NOTE- PIFS based link access is not used.

## Slide 6: Multi-Link Simulation Set Up
Simulation cases:
  Case 0: baseline - Legacy single link operation
  Case 1: MPC with no IDC interference
    EHT AP transmits any frame on a link once it obtains a TXOP on the link
  Case 2: MPC with IDC interference constraints
    EHT AP does not transmit a frame except for a control response frame on one link while it is receiving a frame on the other link.
UL A-MPDU
BA
UL A-MPDU
BA
UL A-MPDU
BA
UL A-MPDU
BA
Link 1
Link 2
UL A-MPDU
BA
UL A-MPDU
BA
Back-off
Back-off
Back-off
Back-off
Back-off
Error
Error
Error
Back-off

## Slide 7: Multi-Link Simulation Results
Case 2 (light blue bar) has better total uplink throughput than that of case 1 (red bar)
Case 2 (light blue bar) has worse downlink throughput than that of case 1 (red bar)

## Slide 8: Multi-Link Simulation Results
  The uplink throughput difference between case 1 and case 2 shrinks as OBSS load increases
  Case 2’s uplink throughput decreases as OBSS load increases
  Case 2’s downlink throughput improved a little bit as OBSS load increases.

## Slide 9: Multi-Link Simulation Result Observations
For case 2 “MPC with IDC interference constraints”, the AP won’t start transmission if there is an ongoing Rx on the other link, UL total throughput is dramatically increased but with DL goodput sufferring a lot due to much less chance for DL traffic.
Fairness between downlink and uplink needs to be improved.

## Slide 10: Conclusion
  Some simulation results are shown for different channel access schemes for a pair of links with constraints have been discussed
  It is necessary to further consider about fairness issue on channel access rules to avoid Tx/Rx interference on the pair of links with IDC interference constraints.

## Slide 11: Reference
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1927-00-00be-multi-link-operation-simulation-methodology.pptx