## Slide 1: Multi-Link Operation and Channel Access Discussion
Date: 2020-01-12
Authors:

## Slide 2: Motivation
A constrained AP MLD supports the multi-link operation but has an in-device coexistence interference when the two links are close to each other
  The transmit power leakage from one link will severely interfere the reception of frames on the other link. Eg. DL + UL on two links.
  When there are legacy STAs or single link EHT STAs, different STAs contend the channels on different links without knowing the channel status of the other link
  A simple rule should be considered as the baseline operation for multi-link AP and non-AP devices with IDC constraints to improve the spectrum efficiency for multiple links with IDC constraints
  Some contributions has discussed the issues [1] [2]
  In this proposal, we discuss the multi-link operation of the AP having an in-device coexistence (IDC) interference between multiple links.

## Slide 3: Constrained AP MLD operation
A constrained AP MLD which supports the multi-link operation but has an in-device coexistence interference operates as the following:
  A STA of the constrained AP MLD performs a contention on the primary channel of link 1 (Single Primary Channel mode).
    After obtaining a TXOP on link1 (backoff to 0), the AP MLD checks the channel status of link 2.
      If the STA of the AP MLD is not a TXOP responder on link2, the STA of the MLD can transmit frames over link1.
        If the channel status of Link 2 is IDLE, ie. Virtual CS idle and/or PIFS CS idle, the STAs of the MLD can transmit frames over both link 1 and link 2 simultaneously. (Fig.1 case 1)
        If the channel status of link 2 is not IDLE, the STA of the MLD can transmit frames on link 1 only. (Fig.1 case1 )
      Otherwise, the STA of the MLD shall not transmit frames on link 1. (Fig.2 case 2)

## Slide 4: Constrained AP MLD operation - Single primary channel
TX
RX
STA1
STA2
AP MLD
Link1
Link2
3
2
1
0
TX
RX
OBSS busy
1
0
TX
RX
3
2
DL TXOP
DL TXOP
IDLE
Fig.1
Case 1: link 2 is OBSS busy

## Slide 5: Constrained AP MLD operation - Single primary channel
Fig.2
STA1
STA2
AP MLD
Link1
Link2
TX
RX
UL TXOP
of intra BSS
TX
3
2
1
0
4
TX
RX
3
2
1
0
TX
RX
OBSS busy
1
0
TX
RX
3
2
DL TXOP
DL TXOP
No Tx due to
receiving on link2
Case 2: link 2 is intra BSS busy

## Slide 6: Non-AP STA operation associated with a constrained AP MLD
The non-AP STA associated with the constrained AP MLD operates as the following
  The AP MLD signaled the primary channel of link 1 to allow contention based channel access
  Legacy STAs and single-link non-AP STAs can only operate on link1
  A multi-link non-AP MLD STAs can operate on both link 1 and link 2 if the AP MLD allows the operation on the link 2. (see next slides). Otherwise, it only operates on link1.

## Slide 7: Non-AP MLD STA operation associated with a constrained AP MLD(ctnd.)
A multi-link channel access for non-AP MLD STAs can be controlled by the AP (Fig.3)
  If the AP MLD signaled the primary channel of link 2 to allow contention based channel access on link 2, the STA of the non-AP MLD performs channel contention independently on each primary channel of link 1 and link 2.
      Transmits over both link 1 and link 2 simultaneously if backoff to zero on one link with IDLE status on the other link.
      Transmit on link 1 only if backoff to zero on link 1 with non IDLE status on link 2
      Whether allow transmission on link 2 only is TBD. More restrictions may need to be considered
  Otherwise, the AP MLD disallows channel contention on link 2
      The non-AP MLD STA performs a contention only on the primary channel of link 1 as Single Primary Channel mode.

## Slide 8: Non-AP MLD STA operation associated with a constrained AP MLD (Example)
Fig.3
STA1
STA2
Non-AP MLD
3
2
1
0
Link1
Link2
TX
RX
TX
RX
UL TXOP
UL TXOP
OBSS busy
1
0
TX
RX
UL TXOP
5
4
3
2
3
2
IDLE
1
0
TX
RX
TX
RX

## Slide 9: Conclusion
  Constrained AP MLD operation and non-AP MLD STAs operation associated with the constrained AP MLD are discussed.
  Some restrictions on multi-link channel access may need further considerations.
  Proposed single primary channel mode for constrained AP MLD operation.
  Proposed multiple primary channel mode for non-AP MLD STA controlled by AP MLD.

## Slide 10: Straw Poll 1
Do you support that a constrained AP MLD shall support single primary channel operation mode?

## Slide 11: Straw Poll 2
Do you support that a constrained AP MLD can enable or disable contention based channel access for each link?

## Slide 12: Straw Poll 3
Do you support that non-AP legacy and single link STAs associated with a constrained AP MLD shall operate on the common link?

## Slide 13: Straw Poll 4
Do you support that non-AP MLDs associated with a constrained AP MLD may contend on the different link from the common link on which legacy and single link STAs operate when the associated AP MLD indicates to allow contention based channel access on the link?

## Slide 14: Reference
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1574-01-00be-multi-link-auxiliary-link.pptx
[2] https://mentor.ieee.org/802.11/dcn/19/11-19-1116-04-00be-channel-access-in-multiband-operation.pptx