## Slide 1: Channel Access Design for Synchronized Multi-Links
Date: 2019-09-07
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Guogang Huang |  |  |  | 
Yuchen Guo |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
There are two types of multi-links (ML) base on the capability of simultaneous TX/RX on different links
  Synchronized ML
  Asynchronized ML
The channel access in asynchronized MLs could be independent, it is simple to design;
The transmissions in multiple links are need to be synchronized in synchronized MLs, and many issues need to be considered for channel access.

## Slide 3: TXOP setup
A ML entity transmits TXOP initial frames (e.g. RTS) on the links that are idle at the time when backoff is finished;
TXOP could only be set up on the links that successfully get response frames (e.g. CTS) when the responses are needed;
RTS
CTS
Data
BA
Data
…
RTS
Busy
…
RTS
CTS
Data
BA
Data
…
Link 1
Link 2
Link 3
Link 4
TXOP
Backoff finished

## Slide 4: TXOP setup
Different TXOP initial frames may be sent on different links;
  The end times of initial data should be aligned if responses are needed.
RTS
CTS
Data
BA
Data
…
RTS
…
Data (ACK)
BA
Data
BA
Data
…
Link 1
Link 2
Link 3
Link 4
TXOP
Backoff finished
CTS to Self
Data (ACK)
…
Data (No ACK)
Link 5
Link 6
Link 7
Data
BA
Data
…
Data
BA
Data
…
…
OR

## Slide 5: Primary 20MHz and BW on each link
No matter single primary link, multiple primary links or no primary link for ML, each link may has a primary 20MHz sub-channel;
  It will be convenient to support dynamic bandwidth, otherwise receiver side will needs multiple decoder in each link
TXOP bandwidth on each link is base on bandwidth negotiation on its own link;
RTS
CTS
Data
BA
Data
…
RTS
CTS
Data
BA
Data
…
Link 1
Link 2
TXOP
RTS
RTS
RTS
CTS
RTS
P 20MHz
P 20MHz

## Slide 6: Problem Statement
Non-AP ML entity (MLE)1 only obtains link 1 after backoff finished, and transmits PPDU 1 to AP MLE;
Later, non-AP MLE 2 sends PPDU2 on link 2 to the same AP MLE during the transmission period of PPDU1;
AP MLE can not replies BA for PPDU 1 in link 1 in this case. How to handle that?
PPDU 1
BA
Link 1
PPDU 2
Link 2
Non-AP ML Entity 1
Non-AP ML Entity 2
AP ML Entity
?
Busy

## Slide 7: Intra BSS solution 1
When non-AP MLE2 receives PPDU 1 on link 1 and identifies it as an intra-BSS PPDU, the non-AP MLE2 defers EDCA contention on link 2 after the TXOP set by PPDU 1;
PPDU 1
BA
Link 1
PPDU 2
Link 2
Non-AP ML Entity 1
Non-AP ML Entity 2
AP ML Entity
AIFS
TXOP

## Slide 8: Intra BSS solution 2
When non-AP MLE2 receives PPDU11 and identifies it as an intra-BSS PPDU, the non-AP MLE2 immediately start EDCA contention on link 2. When transmits PPDU21 on link2, its end time should be aligned with the end time of PPDU11;
Non-AP MLE2 doesn’t know the end time of PPDU12, so it needs to first decode the preamble of PPDU12 to get the PPDU length, and then aligns the end times of PPDU22 and PPDU12.
PPDU 11
BA
Link 1
PPDU 21
Link 2
Non-AP ML Entity 1
Non-AP ML Entity 2
AP ML Entity
AIFS
TXOP
PPDU 12
BA
BA
PPDU 22
BA

## Slide 9: Inter BSS solution
When non-AP MLE2 receives PPDU 1 and identifies it as an inter-BSS PPDU, the non-AP MLE2 starts EDCA contention immediately;
The time that identifies PPDU1 as an inter-BSS PPDU could be
  The end time of PHY preamble of PPDU1, or
  The end time of first MPDU in PPDU1, or;
  others.
PPDU 1
BA
Link 1
PPDU 2
Link 2
Non-AP ML Entity 1
Non-AP ML Entity 2
AP ML Entity
AIFS
Pre-amble

## Slide 10: Summary
Some rules for TXOP setup in synchronized ML are discussed;
One problem of multi-link transmission is showed, and several potential solutions are prepared for discussion.

## Slide 11: Straw Poll 1
Do you agree that there is a primary 20MHz sub-channel in each link of synchronized multiple links?
  Yes
  No
  Abstain