## Slide 1: Multi-link Association
Date: 2019-09-05
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Multi-link operation is an important feature in EHT [1];
A non-AP multi-link device associates with an AP multi-link device through single link is mentioned in several presentations, in order to save signaling overhead [2,3];
For flexibility, each link could be enable or disable after multi-link association;
Several potential solutions are prepared for discussion.

## Slide 3: Solution 1
There are two elements related to multi-link
  Multi-band element, and Neighbor report element
Some important subelements can not be carried in Multi-band element, e.g. Capabilities subelement, so Neighbor report element may be more suitable for multi-link association in solution 1.
Multi-band Element
Neighbor report Element

## Slide 4: Solution 1
Association Response frame
Association Request frame
Multiple neighbor report elements are included in Association Request frame;
  Which neighbor report elements are used for multi-link setup need to be indicated;
Same neighbor report elements are included in Association Response frame;
  Which neighbor elements are agreed for multi-link setup need to be indicated
Neighbor report element 1 = Y
Neighbor report element 2 = Y
Neighbor report element 3 = Y
Neighbor report element 4 = N
Neighbor report element 1 = Y
Neighbor report element 2 = Y
Neighbor report element 3 = N
Multi-link base on neighbor report element 1 &2 are established
N means no for MLs

## Slide 5: Solution 2
Association Response frame
Association Request frame
Multiple multi-link elements are included in Association Request frame;
  Multi-link element is an new element which different from multi-band element;
  Only the IEs that have different content from IEs in the transmitted link are included;
Same multi-link elements are included in Association Response frame;
Multi-link element 1 = Y
Multi-link element 2 = Y
Multi-link element 3 = Y
Multi-link element 1 = Y
Multi-link element 2 = Y
Multi-link element 3 = N
Multi-link base on multi-link element 1 &2 are establised

## Slide 6: Solution 3
On-channel tunneling (OCT) is supported in current spec;
The management MPDU (MMPDU) of one band can be transmitted on another band through OCT;
Only single MMPDU can be transmitted in one OCT frame;
Order | Information
1 | Category
2 | FST Action
3 | OCT MMPDU
4 | Multi-band
On-channel Tunnel Request frame Action field format

## Slide 7: Solution 3
On-channel tunneling (OCT) be extended to carry multiple MMPDUs to support MLs;
  Either extend OCT, or introduce a new type of OCT frame
The information of multiple links can be carried in one OCT frame;
Order | Information
1 | Category
2 | FST Action
3 | OCT MMPDU
4 | Multi-band
OCT Request frame Action field
Order | Information
1 | Category
2 | FST Action
3 | Number of links
4 | OCT MMPDU
5 | Multi-band
… | …
n-1 | OCT MMPDU
n | Multi-band
Extended OCT Request frame Action field
Link 1
Link k

## Slide 8: Summary
When perform multi-link association through single link, the signaling overhead can be reduced;
Several potential solutions are prepared for discussion.

## Slide 9: Straw Poll 1
Which solution do you prefer for ML association?
  Solution 1: Multiple Neighbor report elements
  Solution 2: Multiple Multi-link elements (exact name TBD)
  Solution 3: Extended OCT
  Other solutions.

## Slide 10: Reference
[1] EHT PAR document, 11-19-0244-00-0eht-eht-par-document
[2] 11-19-0821-00-00be-multiple-band-discussion
[3] 11-19-0773-00-00be-multi-link-operation-framework