## Slide 1: Simultaneous Tx/Rx Capability indication for multi-link operation
Date: 2019-09
Authors:
Name | Affiliations | Address | Phone | email
Yifan Zhou | Huawei | Bantian, Shenzhen, China |  | zhouyifan8@huawei.com
Jason Yuchen Guo | Huawei |  |  | 
Yunbo Li | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction
Multi-link operation is one of the features in 11be.
Which link to choose for transmission depends on the capabilities of involved links.
Link capability (i.e. simultaneous Tx/Rx) should be announced before link selection and data transmission.

## Slide 3: Multi-link operation
Suppose link 1 and link 2 are selected for link aggregation between the AP and the STA.
If two links are far apart and support simultaneous Tx/Rx, then both AP and STA can freely choose link 1 and/or link 2 for data transmission.
AP
Device
STA
Device
Link 2
Link 1

## Slide 4: Multi-link operation
Suppose the two links are too close to each other, and the STA doesn’t support simultaneous Tx/Rx due to interference leakage.
Therefore, when the STA is transmitting to the AP on link 1, the AP shall not transmit to the STA on link 2.
Link 2
Link 1
AP
Device
STA
Device

## Slide 5: Simultaneous Tx/Rx Capability Indication
Comparing these two scenarios, the STA and AP in the multi-link operation should take different actions, given different simultaneous Tx/Rx capabilities.
Therefore, to make better link selection in multi-link operation, the simultaneous Tx/Rx capability of both STAs should be announced.

## Slide 6: How to indicate – 1st method
There are two cases to indicate simultaneous operation of each link pair, i.e., link 1 and link 2:
  Case 1: Only 1 bit for whether link 1 and link 2 support simultaneous Tx/Rx or not.
  Case 2: there are 2 bits, where one bit indicates whether link 1 can receive while link 2 is transmitting, and the other bit indicates whether link 2 can receive while link 1 is transmitting.
Pairwise indication bits can be carried in the existing multi-band elements or neighbor report elements separately.
  For N links, N*(N-1)/2 bits are needed to indicate for case 1, N*(N-1) bits are needed for case 2.

## Slide 7: Indicate in multi-band element
In multi-band element, the band ID, operating class and channel number specify the channel frequency for which the multi-band element applies.
The indication bits can be filled into the reserved subfields in multi-band control field or multi-band connection capability field. 1 indicates that the simultaneous Tx/Rx of the transmitting channel and the element-specified channel is supported by the transmitter, otherwise not.

## Slide 8: How to indicate – 2nd method
Another method is that based on a predefined frequency gap threshold provided by the transmitter to the receiver.
If two links are not closer than this threshold, then the receiver assumes that the transmitter support simultaneous Tx/Rx on these two links, otherwise not.
Those thresholds can be delivered in the new EHT Capabilities element.

## Slide 9: Frequency gap between links
Definition: gap between center or edge working frequencies of two links.
There are several options to determine the frequency gap threshold
  Transmitter-specific: each transmitter determine its own threshold
  BSS specific: an AP determines the threshold adopted within the BSS
  commonly defined: the Spec unifies a common and reasonable threshold for all devices.

## Slide 10: Conclusion
Link capabilities should be announced before link selection and data transmission.
In this proposal, two methods are provided to indicate the simultaneous Tx/Rx capabilities of link pairs for AP/STA devices.