## Slide 1: Consideration on HARQ feedback
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
There have been lots of contributions dealing with the HARQ features on 11be
  E.g., Performance analysis, complexity, HARQ units, HARQ framing, ...
We think PHY-level unit as an HARQ unit is appropriate due to its lower PHY-MAC interaction overhead and higher performance than MAC-level unit
In PHY-level units, it is important to design HARQ feedback frame
In this contribution, we address two candidates for the HARQ feedback frame and estimate their feedback overhead

## Slide 3: Recap on HARQ unit [1]
HARQ unit definition
  An HARQ unit represents an error-check unit for HARQ retransmission
There are two candidates for HARQ unit [See Appendix]
  PHY-level unit
    Some bits for error-checking can be included in the unit (E.g., CRC)
  MAC-level unit
    Padding bits can be included between codewords to align borders of an MPDU and a codeword
We assume the HARQ operates based on PHY-level unit and the HARQ unit consists of multiple codeword in which the length of HARQ unit is approximately equal to the length of MPDU for fair comparison

## Slide 4: 0. Existing BlockAck
In case of Compressed BlockAck frame with non-HT format (up to 256 MPDUs supportable, lowest MCS), it takes 100 us
  L-part: 20 us
  BlockAck size: 470 bits
  Data duration: ceil(470/24)*4 us = 80 us
  PPDU duration: 100 us
In case of Compressed BlockAck frame with HE format (up to 256 MPDUs supportable, lowest MCS, 160 MHz), it takes 68 us
  L-part: 20 us
  RL-SIG+HE-SIG+HE-STF+HE-LTF-4X: 32 us
  BlockAck size: 470 bits
  Data duration: ceil(470/980)*16 us = 16 us
  PPDU duration: 68 us

## Slide 5: 1. Using frequency tone mapping
HE-LTF tone mapping can be utilized
  For example:
In existing HE TB feedback NDP, 12 tones are required for one tone set
  The maximum number of HARQ units supported for 20 MHz is 18
  According to the number of the corresponding HARQ units, additional symbols can be concatenated or additional streams can be used to increase supportable number
L-part | RL-SIG | EHT-SIG | EHT-STF | EHT-LTF
HARQ feedback frame
Tone sets
...

## Slide 6: 1. Using frequency tone mapping
Assuming 80 MHz, CW size = 1944b, MPDU length = 1538B, lowest MCS, 4x HE-LTF 3.2 μs GI for HE-LTF, the estimated time for HARQ feedback is as follows (Existing preambles, i.e., HE-SIG-A and HE-STF are assumed, HE-LTF symbols are concatenated as the size of PPDU increases)
In this scenario, one HARQ unit consists of 13 codewords to make length of HARQ unit equal to length of MPDU
Number of MPDUs in A-MPDU | 256
PSDU length (bytes) | 395264
PPDU without preamble (bits) | 6324224
Number of CWs | 3254
Number of HARQ units | 251 (=3254/13)
Required number of HE-LTF symbols for 80 MHz | 4 (=(251/18)/(80MHz/20MHz))
HARQ feedback duration (us) | 104

## Slide 7: 2. Using SIG field
Designing NDP packet which consist of only PHY preamble and SIG can be considered
  For example:
This type of frame has been used for NDP BlockAck in 11ah
Type | BlockAck ID | Sequence Control | BlockAck Bitmap | CRC | Tail | Reserved
2 | 6+6 (BSS Color + HARQ ID) | 12 | 256 | 16 | 6 | 8
L-part | RL-SIG | EHT-SIG | EHT-STF | EHT-LTF | HARQ-SIG
HARQ feedback frame

## Slide 8: 2. Using SIG field
Assuming 80 MHz, CW size = 1944b, MPDU length = 1538B, lowest MCS, 4x HE-LTF 3.2 μs GI for HE-LTF, the estimated time for HARQ feedback is as follows (Existing preambles, i.e., HE-SIG-A, HE-STF, and HE-LTF are assumed)
Bitmap size / Supportable CWs | 256
PPDU without preamble (bits) | 6469632
HARQ-SIG length (bits) | 312
Required number of HE-LTF symbols for 80 MHz | 3 (=(312/26)/(80MHz/20MHz))
Duration for HARQ SIG (us) | 12
HARQ feedback duration (us) | 64

## Slide 9: Feedback duration comparison
 | BlockAck with non-HT format | BlockAck with HE format | Frequency tone mapping | SIG field
Unit size (an MPDU after encoding / a codeword) | 24608 bits | 24608 bits | 25272 bits | 25272 bits
The number of distinguishable units | 256 | 256 | 251 | 256
Feedback duration | 100 us | 68 us | 104 us | 64 us

## Slide 10: Conclusion
We proposed two candidates of HARQ feedback frame, analyzed their estimated transmission durations, and compared them with existing BlockAck frame
Based on the similar size of unit lengths among them, feedback methods perform tolerable durations compared to the existing BlockAck frame

## Slide 11: References
[1] 19/1131r1, “Consideration on HARQ unit”

## Slide 12: Appendix A: PPDU format example - Codeword as an HARQ unit without CRC
Codeword
#1
Data
Codeword
#2
Codeword
#3
Codeword
#4
Codeword
#5
PHY
HDR
MPDU
#1
MPDU
#2
MPDU
#3
Erroneous unit
PHY
HDR
CW#1 will be retransmitted on the next retransmission
HARQ error check is performed using LDPC checksum on the PHY layer

## Slide 13: Appendix A: PPDU format example - Codeword as an HARQ unit with CRC
Data
PHY
HDR
Codeword
#1
Codeword
#2
Codeword
#3
Codeword
#4
Codeword
#5
Erroneous unit
PHY
HDR
CW#1 will be retransmitted on the next retransmission
HARQ error check is performed using frame check sequence on the PHY layer
CRC
CRC
CRC
CRC
CRC
MPDU
#1
MPDU
#2
MPDU
#3

## Slide 14: Appendix A: PPDU format example - MPDU as an HARQ unit without padding to align
Codeword
#1
Data
Codeword
#2
Codeword
#3
Codeword
#4
Codeword
#5
PHY
HDR
MPDU
#1
MPDU
#2
MPDU
#3
FCS
FCS
FCS
PHY
HDR
Erroneous unit
CW#2 and CW#3 will be retransmitted on the next retransmission
HARQ error check is performed using FCS field on the MAC layer

## Slide 15: Appendix A: PPDU format example - MPDU as an HARQ unit with padding to align
Data
PHY
HDR
MPDU
#1
MPDU
#2
MPDU
#3
Padding
Codeword
#1
Codeword
#2
Codeword
#3
Codeword
#4
Codeword
#5
FCS
FCS
FCS
PHY
HDR
Erroneous unit
CW#3 will be retransmitted on the next retransmission
HARQ error check is performed using FCS field on the MAC layer