## Slide 1: Frame aggregation for BCS
Date: 2019-09-11
Authors:

## Slide 2: Background
802.11bd is considering frame aggregation concept for NGV (11bd) Outside the Context of a BSS (OCB)
It seems reasonable that frame aggregation for broadcast services (BCS) is considered within a BSS.

## Slide 3: High level concept
Visualization of non-aggregated and aggregated frames

## Slide 4: The situation
The two main types of aggregation are:
  A-MSDU
    See 802.11-2016 § 10.12 A-MSDU operation
  A-MPDU
    See 802.11-2016 § 10.13 A-MPDU operation
Both types of aggregation currently have limitations that will affect their use in 802.11bc.

## Slide 5: Various statements from 10.12 A-MSDU operation [1]
The Address 1 field of an MPDU carrying an A-MSDU shall be set to an individual address or to the GCR concealment address.
...
The following rules apply to the transmission of an A-MSDU:
  — A non-DMG STA that has a value of false for dot11HighthroughputOptionImplemented shall not transmit an A-MSDU.
  — A non-DMG STA shall not transmit an A-MSDU to a STA from which it has not received a frame containing an HT Capabilities element.
Summary:
A-MSDU doesn’t work for uni-directional broadcast
Requires exchange of capabilities
A-MSDU requires block ACK

## Slide 6: Various statements from 10.13 A-MPDU operation
A STA indicates in the Maximum A-MPDU Length Exponent field in its HT Capabilities element
...
A STA shall not transmit an A-MPDU in an HT PPDU that is longer than the value indicated by the Maximum A-MPDU Length Exponent field in the HT Capabilities element received from the intended receiver.
...
A STA that is neither an AP nor a mesh STA shall not transmit an A-MPDU containing an MPDU with a group addressed RA.
Summary:
Should work for broadcast BSS with minimal updates.
Need to clarify block ack behavior for broadcast (i.e. unacknowledged)
The main capabilities exchanged are to do with maximum lengths.

## Slide 7: More about A-MPDU from 802.11ac
802.11ac introduced the concept of a “VHT single MPDU”.
Basically all VHT frames are transmitted with the A-MPDU frame structure even if they only carry one MPDU.
Should 802.11bc use this approach, requiring A-MPDU for all BSS transmissions?

## Slide 8: Specific Capabilities for BCS
A-MPDU Parameters field of the HT Capabilities element (802.11-2016 §9.4.2.56.3) [1]
VHT Capabilities Information field of the VHT Capabilities element (802.11-2016 §9.4.2.56.3)
BCS Capabilities
  Within a BSS, where capabilities can be exchanged, this is straightforward, as existing mechanisms can be used.
  However, if capabilities cannot be exchanged then it may be difficult to decide on a default set of parameters.

## Slide 9: Things for 11bc to do
Add/change text to enable A-MDPU for broadcast BSS (10.13).
Broadcast mode doesn’t allow for exchange of HT Capabilities of VHT Capabilities, so a specific fixed set of capabilities needs to be specified. Need to define these “BCS Capabilities” as a fixed set of capabilities so all BCS STAs know what can be transmitted/received by other BCS stations. (i.e. max number of MxDU in an A-MxDU, max length, etc.)
Another consideration is that TGbd “Next Generation V2X” is also working on the issue of aggregation for group-addressed/broadcast frames for a broadcast OCB. Need to coordinate aggregation for broadcast BSS (11bc) with broadcast OCB (11bd).

## Slide 10: Straw poll 1
Should 802.11bc amendment enable at least one of A-MSDU or A-MPDU operation to work for broadcast frames?
Yes
No
Abstain

## Slide 11: References
IEEE Std 802.11-2016
802.11-19/0375