## Slide 1: Further Discussion on Multi-link Operations
Date: 2019-09-12
Authors:

## Slide 2
Abstract
In this contribution, we follow up on the discussion on using a single ID/MAC address to identify MLE and MLD, and include such address in data frames in order to simplify data flows in multi-link operations.

## Slide 3: Introduction
Multi-link operations have been identified as a feature for 802.11be
Architectures enabling multi-band/multi-link operations for 802.11be have been discussed, e.g., in [1] [2]
  Proposed the concept of Multi-link entity (MLE) and Multi-link Device (MLD)
  A common identifier for MAC-SAP or by DSM either on MLE level or MLD level
We have had some initial discussions on design choices that may simplify data flow [4]
  Multi-link devices such as MLD or MLE should be identified by the ID or MAC address of their “high” MAC SAPs
  For multi-link data flows, it may be beneficial to include in the data frames a single ID or MAC address of the “high” MAC-SAP of the target MLD and MLE
In this contribution, we discuss some approaches to include such single ID or MAC address of the “high” MAC-SAP of the target MLD and MLE

## Slide 4: Recap of the previous multi-link discussion in [4]
UL and DL data flows are between the “high” MAC-SAPs of the MLEs/MLDs that contain APs and non-AP STAs
Hence, the “high” MAC-SAPs should be identified by IDs or MAC addresses
Therefore, it is beneficial to have these IDs or MAC addresses included in the MAC frames
  E.g., in one of the address fields in data frames

## Slide 5: Recap of benefits using a single ID for multi-link data transmissions
A data frame can be clearly identified to be meant for higher layers if it contains the ID or MAC address of the target higher MAC SAP of the target MLD or MLE
Sequence numbers can be generated uniquely from the same sequence number space and it is easy to re-assemble fragments, packets and detect duplication
If dynamic link switching is desired, a packet can be transmitted over any link without having to regenerate MAC headers
It is easier to identify packets when multi-channel/multi-band aggregation is used to transmit a wide-bandwidth frame
Some of these benefits may depend on the particular design of multi-link operations defined in 802.11be

## Slide 6: Possible approaches (1/4)
During the previous discussions, there were some questions on the exact methods of including in data frames the “high” MAC SAP ID/MAC Address for target MLE and MLE
Some possible approaches to indicate “high” MAC SAP ID in a data frame/PPDU may be:
  In the preamble
  In the MAC header
  In the Frame body
  Not include “high” SAP ID in data frames/PPDUs, instead making the mapping internal to an MLE/MLD
  Other options

## Slide 7: Possible approaches (2/4)
Option 1: Including the “high” MAC SAP ID in the preamble
  PAID/Group ID are currently included in preambles
  Traditionally, the preamble is not a place to provide MAC level identifications for data flow; e.g., the PAID/Group ID in the preamble may be used for power saving purposes
  Can consider using multi-link AID if TGbe decides to define it
  May not be the best place to include “high” MAC SAP ID
Option 2: Including the “high” MAC SAP ID in the MAC header
  MAC addresses currently may be included in one of the four Address fields in a data frame
  Other fields in the MAC header may be used as well
  Spec modification is required for receiving STAs to add more addressing filtering rules for “high” MAC SAP IDs in order to make the scheme plausible
  Data flow can benefit from multi-link operations as discussed above
    The exact benefits will depend on the particular design for multi-link operation

## Slide 8: Possible approaches (3/4)
Option 3: Including the “high” MAC SAP ID in the frame body of a data frame
  Can provide some benefits from multi-link operations as discussed above
    May not be able to be link-agnostic for link switching, link aggregation, etc., depending on the MAC header addressing schemes
    May ease duplication detection, fragmentation re-assemble and acknowledgement procedures for multi-link operations
  Requires additional rules to be defined by TGbe for receiving STAs to recognize “high” MAC SAP IDs

## Slide 9: Possible approaches (4/4)
Option 4: Not include the “high” MAC SAP ID in data frames/PPDUs, instead making the mapping to “high” MAC SAP ID internal within an MLE/MLD
  Was mentioned as an option during discussions
  No changes to the current over the air MAC protocols
  Requires additional queueing/duplication detection designs over multiple links
  May require new acknowledgement procedures for multi-link operations
  Requires additional rules between “low” MAC and “high” MAC SAP
  May not be able to be link-agnostic for link switching, link aggregation, etc., depending on the MAC header addressing schemes
Option 5: Other options

## Slide 10: Conclusions
In this contribution, we followed up on the topic of including a single ID/MAC address of the “high” MAC SAP of the target MLE/MLD in data frames, which may be beneficial for multi-link data flows
We provided analysis of a number of approaches of providing such indication for data frames/PPDUs

## Slide 11
References
[1] IEEE 11-19/0822r0, Extreme Efficient Multi-band Operation, May 2019
[2] IEEE 11-19/0823r0, Multi-link Aggregation, May 2019
[3] IEEE 11-19/0731r0, Multi-link Operation, May 2019
[4] IEEE 11-19/1213r0, Discussion on Multi-link Operation, July 2019

## Slide 12: Strawpoll
Do you agree that the ID (e.g. MAC Address) of the “high” MAC SAP of the target MLD should be included in the data frames?
  The ID for the “high” MAC SAP is TBD
  The location in the data frames to include the ID of the “high” MAC SAP is TBD
  Y/N/A