## Slide 1: One Channel Information Feedback Method for Multi-AP Coordination
Date: 2019-09-15
Authors:
Name | Affiliations | Address | Phone | email
Dandan Liang | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | Dandan.liang@huawei.com
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yu Jian |  |  |  | 
Yuchen Guo |  |  |  | 

## Slide 2: Introduction
The Multi-AP coordination sounding has been discussed in [1]-[3], [1] analyzed different options of collecting channel information:
  Opt1: each AP collects its own channel information (such as: Compressed Beamforming Report (BFR))
  i.e., AP1 collects BFR (AP1STA1, AP1STA2), AP2 collects BFR (AP2STA1, AP2STA2).
  Opt2: each AP collects BFR only from its associated STA(s), then the BFR needs to be exchanged between APs.
  i.e., AP1 collects BFR (AP1STA1, AP2STA1), AP2 collects BFR (AP1STA2, AP2STA2).
  Opt3: master AP collects BFR for all the APs, then channel information needs to be exchanged between APs.AP1STA2), AP2 collects CSI (AP2STA1, AP2STA2).
  Opt2: each AP collects CSI only from its associated STA(s), then the channel information needs to be exchanged between APs.
  i.e., AP1 collects CSI (AP1STA1, AP2STA1), AP2 collects CSI (AP1STA2, AP2, STA2).
  Opt3: master AP collects CSI for all the Aps, then then channel information needs to be exchanged between APs.
  If AP1 collects all BFR among each APs to each STAs, the overhead of BFR feedback will be a serious problem. Hence, the method of reducing channel information feedback for Multi-AP coordination shall be designed.
AP 1 – the master AP, AP2 - the slave AP

## Slide 3: Our proposed method
For reducing the channel information (such as: compressed beamforming report (BFR)) feedback, we propose one potential method that based on the channel quality, the STA feedbacks BFR selectively.
  More explicitly, because the STA knows its channel quality to APs, so
  If the channel quality between the STA and the AP is good, the STA feedbacks BFR to the AP.
  If the channel quality between the STA and the AP is not good, the STA does not feedback BFR to the AP.

## Slide 4: Option 1
Option 1 Proposal: only BFR of the selected AP is fed back
  APs send NDPA and NDP (Note that NDPs can send sequentially or in parallel.)
  The STA measures the channel with different APs, then the STA feedbacks BFR selectively. For example:
    Feedback method 1: when the channel quality is bad between AP3 and the STA, the STA broadcasts BFR1 and BFR2 to AP1 and AP2, which also means that AP1 and AP2 will attend next data sharing/transmission stage.
    Feedback method 2: when the channel quality is bad between AP3 and the STA, the STA feedbacks BFR1 and BFR2 to AP1 and AP2 sequentially, which also means that AP1 and AP2 will attend next data sharing/transmission stage.
AP1
AP2
AP3
STA
Sounding Procedure
BFR 1
BFR 2
Feedback method 1
BFR 1 + BFR 2
Feedback method 2
Data sharing/transmission between the selected APs

## Slide 5: Option 2
Option 2 Proposal: Both BFR of the selected AP and CQI of the non-selected AP is fed back
  APs send NDPA and NDP (Note NDPs can send sequentially or in parallel.)
  The STA measures the channel with different APs, then the STA feedbacks BFR to the selected APs and the CQI to the non-selected APs. For example:
    Feedback method 1: when the channel quality is bad between AP3 and the STA, the STA broadcasts BFRs to AP1 and AP2 and CQI to AP3, which also means that AP1 and AP2 will attend next data sharing/transmission stage.
    Feedback method 2: when the channel quality is bad between AP3 and the STA, the STA feedbacks BFRs to AP1 and AP2 and CQI to AP3 sequentially, which also means that AP1 and AP2 will attend next data sharing/transmission stage.
AP1
AP2
AP3
STA
Sounding Procedure
BFR 1
BFR 2
Feedback method 1
BFR 1 + BFR 2 + CQI 3
Feedback method 2
Data sharing/transmission between the selected APs
CQI 3

## Slide 6: Conclusion
  In this contribution, we propose that the STA can feedback the channel information selectively for reducing channel feedback overhead in Multi-AP coordination system.
    Option 1: Only BFR of the selected AP is fed back by the STA
    Option 2: Both BFR of the selected AP and CQI of the non-selected AP is fed back by the STA

## Slide 7: References
[1] IEEE 802.11-19/1097r0 <Sounding Procedure in AP collaboration>, Ross Jian Yu, Huawei Technologies.
[2] IEEE 802.11-19/1134r1<Consideration on Multi-AP Sounding>, Kosuke Aio, Sony Corporation.
[3] IEEE 802.11-19/0488r1<Multi-AP Transmission Procedure>, Sungjin Park, LG Electronics.

## Slide 8: Straw Poll 1
  Do you support the proposed channel feedback method that STA can feedback channel information selectively?
    Y
    N
    A

## Slide 9: Straw Poll 2
  Which option of the proposed channel feedback method for Multi-AP Coordination is preferred?
    Option 1:
    Option 2:
    Both Option 1 and Option 2: