## Slide 1: Multi-link BA Operation
Date: 2019-08-23
Authors:
Name | Affiliations | Address | Phone | Email
Zhou Lan | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | zhou.lan@broadcom.com
Chunyu Hu |  |  |  | 
George Kondylis |  |  |  | 
Peyush Agarwal |  |  |  | 
Matthew Fischer |  |  |  | 
Srinath Puducheri |  |  |  | 
Notes: September 2012

## Slide 2: Recap of the Current Discussions
Multi-Link Operation (MLO) has been discussed as a major 11be feature for throughput improvement and latency reduction
  [1, 2] discusses the synchronized and asynchronized MLO rules
  [3, 4] discusses the terminology and architecture
  [4] discusses the multi link aggregation
    Packet switch, TID mapping, common BA session etc.
This presentation discusses MLO operation that supports the flexibility of accommodating different implementation architectures

## Slide 3: Common BA Session?
Assuming that a single TID between two MLO STAs is split across >1 link
How many BA sessions are negotiated?

## Slide 4: Proposal
  Define an architecture that supports the benefits of the MLO operation while accommodating different implementation choices
  TX: Packet flow is split between links somewhere between the MAC SAP and the WM
  RX: Packet flow from different links is merged somewhere between the antenna and the MAC SAP
  Desire a protocol that allows packet flow split location to be an implementation choice

## Slide 5: Low MAC MLLE Link Split
Low split
EDCA0
EDCA1
PHY0
PHY1
RX
DEFRAG
DEAGG
REORDER
EDCA0
EDCA1
PHY0
PHY1
MAC SAP
MAC SAP
ADDR_A
ADDR_B
ADDR_C
ADDR_Y
ADDR_Z
ADDR_X
AMSDU
AMPDU
MACSEQ
FRAG
BACON
BACON
TX
RX

## Slide 6: High MAC MLLE Link Split
High split
EDCA0
EDCA1
PHY0
PHY1
RX
DEFRAG
DEAGG
REORDER
EDCA0
EDCA1
PHY0
PHY1
MAC SAP
MAC SAP
ADDR_A
ADDR_B
ADDR_C
ADDR_Y
ADDR_Z
ADDR_X
MACSEQ
RX FIFO
RX FIFO
BACON
BACON
AMSDU
AMPDU
FRAG
AMSDU
AMPDU
FRAG
BACON
BACON
TX
RX

## Slide 7: High MAC split
Requires some sequencing information
  If the split is above the MPDU, then the sequencing information needs to be generated on the TX side above the MPDU generation and carried up to the merge point on the RX side
  E.g. sequence value associated with MSDUs
  Maintain existing BA for MPDU sequencing
  Separate queue management
Single BA or Multiple per-link BA
  Single BA might impose minor restrictions

## Slide 8: Low MAC split
Requires TX queue sharing
Requires RX queue sharing
  Or merge above the RX queue, i.e. asymmetric split between TX and RX
Single BA
  Assuming BA Control above the split

## Slide 9: High vs Low
The pros and cons of each split point can be debated
But such a debate is best left as an implementation decision
TGbe protocol definition should support a range of options
  Let the market select the winning implementation choice

## Slide 10: High MAC Split Requirement
The main requirement of the high MAC split is sequencing information available at the high end of the MAC
  E.g. per MSDU sequencing information
MSDU sequencing information can be:
  In addition to MPDU sequencing
  Tightly coupled to MPDU sequencing

## Slide 11: Separate MSDU Sequencing
Each MSDU could contain its own MSDU sequencing numbering
  GSN = Global Sequence Number
  Only needed by high MAC devices
  Could be negotiated to be used, only on links that need it
Can be zero-overhead
  See next slides

## Slide 12: Zero Overhead GSN SNAP
  Use LLC/SNAP headers to pass the global MSDU sequence number
      LLC/SNAP protocol (802.2) is used to encapsulate all MSDUs when forming an 802.11 frame
      The SNAP/DSAP and SNAP/SSAP fields are set to 0xAA to create a SNAP header and this value is not changed while the frame is inside of the 802.11 domain
      Proposal: At the TX side, replace SNAP/DSAP and SNAP/SSAP field values 0xAAAA with the GSN when creating the 802.11 frame from the MSDU and replace the GSN with 0xAAAA when leaving the 802.11 domain (i.e. top of the MLLE at the RX side)

## Slide 13: Zero Overhead GSN MACSEQ
GSN uses existing SEQCON Field
  i.e. SEQCON of MAC header
  Nearly transparent vs architectural choices
FRAG (4)
SEQ (12)
Existing SEQ Con field definition:

## Slide 14: GSN MACSEQ Field Size
Do we need to repartition the SEQ Control field?
Existing MAC SEQCON Sequence field is 12 bits
  New BA limit of 1024 (10 bits)
    Only half of SEQ space is usable to avoid ambiguity > vs <
  Existing field permits AMSDU aggregation average of 2 MSDU
    I.e. MPDU count remains the same if BA limit is increased to 2048
Desire higher average AMSDU aggregation
  SEQ 14 bits = BA x 1024 (10 bits), AMSDU x 8 (4 bits)
    FRAG 2 bits (Level 3 MAX)
  Increase BA Window max to 8192 (8192 MSDU => 1024 MPDU)
  New DATA Subtype

## Slide 15: GSN BAR
Do we need a BA function for the GSN?
  In the case of a TX queued MSDU that has a timeout or for some other reason is deleted from the TX queue, the RX side needs to move past the GSN hole
    In MACSEQ case, this is done by sending a BAR
    Need something similar for GSN
    If single BA, then no need for GSN BA action, use regular BAR
    BAR and BA must be transmitted on the link associated with the frames of reference
  If multiple BA, then need to define at least GSN BAR
    GSN ADDBA, GSN DELBA optional

## Slide 16: Negotiate use of GSN
If GSN is embedded in MSDU
  E.g. GSN in SNAP
  GSN use is negotiated
If GSN is embedded in MACSEQCON
  No GSN negotiation needed

## Slide 17: RA TA Values and BA Sessions
RSNA using MAC SAP addresses
  Generally agreed, not formally agreed
Beacons using LMAC addresses?
  Or all Beacons using common TA, but indicating other MAC addresses within elements in the Beacon?
Data MPDUs use which addresses?
How many BA sessions?

## Slide 18: Option 1: 1 Address
Use MAC SAP address for everything
No need for other addresses
Loss of explicit link differentiate within MPDU
Single BA across links
  Multiple BA session is difficult
What about non-MLLE STA?
  E.g. non-MLLE 11be and 11ax STA
  Scanning Non-MLLE device sees same BSS in Beacons on multiple link channels
    Confusing at best

## Slide 19: Option 2: Multiple Addresses
Use WM Addresses for everything ON THE AIR
Use MAC SAP address for RSNA only:
  Perform address substitution for encrypt/decrypt if MLLE device
  No substitution if non-MLLE device
BA per link

## Slide 20: Option 3: Mixed Addresses
Use MAC SAP address for MLLE devices
Use WM Addresses for non-MLLE devices
  And Beacons, Probe Responses, etc
Loss of explicit link differentiate within MPDU
One BA negotiated per device connection

## Slide 21: Straw poll 1
Do you support that
  BAR and BA shall be transmitted on the link associated with the frames of reference?
  YES
  NO
  ABS

## Slide 22: Straw poll 2
Do you support that
  A new DATA Subtype is defined with SEQCON redefined as 2 bits of FRAG and 14 bits of SEQ?
  YES
  NO
  ABS

## Slide 23: Straw poll 3
Do you support that
  A BAR may be aggregated within an AMPDU that includes DATA Subtypes?
  YES
  NO
  ABS

## Slide 24: Straw poll 4
Do you support that
  There is a negotiation of whether there is one BA session per link or one BA session, per TID per MLLE pair?
  YES
  NO
  ABS

## Slide 25: Reference
  https://mentor.ieee.org/802.11/dcn/19/11-19-1116-00-00be-channel-access-in-multi-band-operation.pptx
  https://mentor.ieee.org/802.11/dcn/19/11-19-0821-02-00be-multiple-band-discussion.pptx
  https://mentor.ieee.org/802.11/dcn/19/11-19-0773-02-00be-multi-link-operation-framework.pptx
  https://mentor.ieee.org/802.11/dcn/19/11-19-1082-00-00be-multi-link-operation-dynamic-tid-transfer.pptx