## Slide 1: An HARQ Transmission Scheme for 11be
Date: 2019-11-07
Authors:

## Slide 2: Background
Various contributions on Hybrid Automatic Repeat Request (HARQ) have been presented in previous meetings [1-7]
In this contribution, we want to discuss some issues related to supporting HARQ in 802.11, in particular to aligning HARQ with the existing 802.11 LDPC design
We then present a solution that requires minor changes to transmitter side and is relatively simple to support at receiver side
This solution also has no impact on the existing Block ACK mechanism

## Slide 3: Existing Rules and Restrictions
The 802.11 specs (and hence respective implementations) assume the following:
    The PHY receives a PSDU from the MAC layer and is not aware of the MPDU boundaries, their length, delimiters, etc.
    The FEC (LDPC) operates on blocks of information bits, regardless of MPDU boundaries
    A Block ACK (BA) indicates which MPDUs (within the A-MPDU) were decoded correctly, so retransmission occurs only for incorrectly decoded MPDUs

## Slide 4: Existing Rules and Restrictions
Assuming an A-MPDU was transmitted and some of the MPDUs were incorrectly decoded, the transmitter will have to retransmit only those MPDUs that failed
For example, in the figure, an A-MPDU containing 5 MPDUs (2000 bits each) is transmitted using coding rate 1/2, where the 2nd and 3rd MPDUs failed and need to be retransmitted
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
FEC #1
Info: 910
Coded: 1820
MPDU of size 2000 bits
FEC block
MPDU Boundary
FEC Boundary
Padding 20 bits
FEC #2
Info: 911
Coded: 1822
FEC #3
Info: 911
Coded: 1822
FEC #4
Info: 911
Coded: 1822
FEC #5
Info: 911
Coded: 1822
FEC #6
Info: 911
Coded: 1822
FEC #7
Info: 911
Coded: 1822
FEC #8
Info: 911
Coded: 1822
FEC #9
Info: 911
Coded: 1822
FEC #10
Info: 911
Coded: 1822
FEC #11
Info: 911
Coded: 1822

## Slide 5: Existing Rules and Restrictions
A retransmission of the failed MPDUs will include different coded bits due to a different setting of the scrambler + FEC, as shown here, so the LLRs cannot be combined
This is a major problem – reusing the existing (retransmission) mechanism, the LLRs respective to retransmitted coded bits cannot simply be combined with old LLRs, as there is no alignment between old and new codewords
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
Retransmitted
Retransmitted
MPDU of size 2000 bits
FEC block
Different info bits at input to FEC, hence different coded bits at output
Padding 20 bits
FEC #1
Info: 804
Coded: 1612
FEC #2
Info: 804
Coded: 1613
FEC #3
Info: 804
Coded: 1613
FEC #4
Info: 804
Coded: 1613
FEC #5
Info: 804
Coded: 1613

## Slide 6: Existing Rules and Restrictions
The example in the previous two slides shows how the misalignment of the MPDUs and the LDPC codewords poses a problem for HARQ
  Furthermore, changing MCS between transmission and retransmissions is limited to the same coding rate, so that the same LDPC matrices are used
As mentioned earlier, our aim is to find a simple method to incorporate HARQ with as few changes as possible to existing spec/designs
We present an idea which requires very little to minimal changes at the transmitter side (no extra buffers/memory required) as well as no changes to the retransmission (reTx) protocol using the Block ACK
  It also supports a different MCS between first transmission and retransmissions

## Slide 7: Solution Highlights
As mentioned before, we want a simple HARQ solution, especially simplifying the transmitter (no need for extra buffers) as well as maintaining the existing Block ACK mechanism
  The highlight of our solution is the following: a Transmission scheme such that HARQ combining can be performed on the LLRs corresponding to info bits only (generally speaking – any transmission scheme, including existing mechanism, can be used); due to the systematic property of the LDPC codes being used in 802.11, we can do so easily
    Combining (or evaluating different sets of) LLRs corresponding to parity bits at the (possibly multiple-hypothesis) decoding stage is an option

## Slide 8: Using Existing Transmission Scheme
The figure below depicts an example for the alignment of codewords against MPDUs in the 1st Tx and the reTx (using coding rate ½)
In the reTx, the failed MPDUs are retransmitted and processed by the PHY layer like in any new transmission (regular operation)
Info bits in the reTx are identical to those in the 1st Tx (alignment shown), parity bits are different
  We can also consider different puncturing of info bits between 1st Tx and reTx
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
Info 910
Padding 20 bits
parity910
Codeword #1
Info 911
parity911
Codeword #2
Info 911
parity911
Codeword #3
Info 911
parity911
Codeword #4
Info 911
parity911
Codeword #5
Info 911
parity911
Codeword #6
Info 911
parity911
Codeword #7
Info 911
parity911
Codeword #8
Info 911
parity911
Codeword #9
Info 911
parity911
Codeword #10
Info 911
parity911
Codeword #11
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
Padding 20 bits
Info 804
Parity 808
Codeword #1
Info 804
Parity 809
Codeword #2
Info 804
Parity 809
Codeword #3
Info 804
Parity 809
Codeword #4
Info 804
Parity 809
Codeword #5

## Slide 9: Using Existing Transmission Scheme
Transmission block diagram is unchanged, and no MAC/PHY interaction is needed (minor MAC changes may be required)
Block-ACK mechanism is unchanged
Changes required for receiver side:
    Needs to know if bits are retransmitted
    Need to combine new LLRs associated with info bits with respective old LLRs of info bits; LLRs of parity bits, to be fed also into the FEC decoder, can be taken from first transmission or later retransmission(s)
    MAC layer would probably need to indicate to the PHY layer which LLRs to discard and which to maintain for future combining (based on MPDUs which were successfully decoded)

## Slide 10: Retransmitting Uncoded Bits
In reTx, only info bits are transmitted – no parity bits
This enables simpler processing at receiver side, and significantly improves the efficiency since the reTx is much shorter
MPDU #1
Bits 0-1999
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
MPDU #4
Bits 6000-7999
MPDU #5
Bits 8000-9999
failed
failed
Info 910
Padding 20 bits
parity910
Codeword #1
Info 911
parity911
Codeword #2
Info 911
parity911
Codeword #3
Info 911
parity911
Codeword #4
Info 911
parity911
Codeword #5
Info 911
parity911
Codeword #6
Info 911
parity911
Codeword #7
Info 911
parity911
Codeword #8
Info 911
parity911
Codeword #9
Info 911
parity911
Codeword #10
Info 911
parity911
Codeword #11
MPDU #2
Bits 2000-3999
MPDU #3
Bits 4000-5999
Padding 20 bits
Info
4020

## Slide 11: Simulation Results
The following figure compares the performance for three different HARQ schemes, assuming 2x2 MIMO with 2 streams, 1500B, TGn-D NLOS, LDPC, perfect CHEST, MCSs 0-2; we compare between:
    No combining
    Combining LLRs of info bits and using parity LLRs from 1st transmission (parity bits in reTx may not be transmitted at all)
    Combining LLRs of info bits and using parity LLRs from 2nd transmission
    Combining LLRs of info bits and choosing (i.e. evaluating both) parity LLRs from 1st or 2nd transmissions (~0.2dB gain)
    IR HARQ combining (black dashed line) - reuse existing LDPC codes with effectively higher coding rate (more puncturing, ~20% of total # of bits); the original (existing) coding rate is reproduced after combining

## Slide 12: Simulation Results
The following figures compare the throughput – assuming all overheads (Preamble, SIFS, ACK etc.); we look at 5 schemes:
    No HARQ
    Chase combining (everything is retransmitted)
    Info Only HARQ (in a retransmission only info bits are transmitted)
    CW retransmission (only failed codewords are retransmitted)
    IR HARQ (where in the first transmission the last bits are punctured, and in the retransmission the preceding bits are punctured)
For the optimal MCS selection, we find the MCS, at each SNR, which maximizes the throughput
We can see that the info-only HARQ scheme outperforms the no-HARQ scheme by a significant gap; it also outperforms most other HARQ schemes for most SNR values

## Slide 13: Simulation Results
The figure below compares the throughout for the same 5 schemes, assuming suboptimal MCS selection
Here we find the MCS, at each SNR, which maximizes the throughput with an additional constraint that PER (before combining) < 10% (similar to [7])
We can see that the gap between the HARQ schemes is relatively small
For most SNR values, the HARQ schemes yield 3-4dB improvement
The Info-only HARQ scheme requires relatively few changes to protocol and design

## Slide 14: Conclusions
One of the major hurdles for supporting HARQ in 802.11 is the (mis)alignment of codewords and MPDUs, which calls for a complicated receiver implementation and additional buffers in transmitter side
We presented here an idea for supporting HARQ within 11be which requires almost no design changes at the transmitter side
The receiver implementation is relatively simple, and there is no modification to the Block-ACK protocol
This idea allows us to freely change the MCS between the first transmission and any retransmission (any coding rate can be used)

## Slide 15: References
11-18-1587: HARQ for EHT, Sep. 2018
11-18-1955: HARQ for EHT – Further Information, Nov. 2018
11-18-1963: Discussion on HARQ for EHT, Nov. 2018
11-19-1992: HARQ Feasibility, Jan. 2019
11-19-2029: HARQ in EHT, Jan. 2019
11-19-1979: HARQ performance analysis, Jan. 2019
11-19-780: Consideration on HARQ, May 2019