## Slide 1: Adapting the 802.11be Channel Model to Modern (Doppler) Use-Cases
Date: 2019-09-12
Authors:

## Slide 2: Introduction
The TGn indoor channel models A-E defined a temporal Doppler component corresponding to an environmental speed
The motivation for using the ‘environmental speed’ is given by the following passage from Section 4.7.1 of the TGn channel model [1]:
  In indoor wireless systems transmitter and receiver are stationary and people are moving in between, while in outdoor mobile systems the user terminal is often moving through an environment.
In the TGac model [2] the environmental speed was reduced to 0.089km/h
An additional Doppler component due to fluorescent lights was also incorporated (removed in 11-09-0308-04-00ac and re-introduced in 11-09-0308-05-00ac)
In this contribution, we will discuss the applicability of these Doppler models to prevalent scenarios today; we will also present lab measurement results showing the Doppler PSD with movements

## Slide 3: Modern Use-Cases
Back in 2004, when the TGn channel model was developed, the vast majority of transmitters and receivers were indeed stationary
This was probably the case for the TGac channel model as well, as smartphones were in their early days
Today, with the proliferation of smartphones, there are numerous use-cases where the STA would be moving while communicating with its AP; for example, consider:
  Convention centers (e.g. IEEE F2F venues)
  Airports/Train Stations
  Schools & Universities
  Stadium
We need to understand how this affects the channel model, so that we can more realistically evaluate the performance of various schemes

## Slide 4: Test Setup
In order to measure the Doppler PSD associated with moving transmitters, we used the following setup:
Keysight MXG transmitting an 80MHz 11ax signal repeatedly @2.5GHz
Keysight Scope recording the transmission over-the-air; analysis done via MATLAB
Frequency locked

## Slide 5: Test Setup
We transmitted an 11ax signal every 500usec, and recorded over 0.5sec for a total of 1024 packets
Omni antennas were used at both Tx & Rx
  Instead of using directional antennas, which suppress the multipath and hence the impact of ‘environmental’ movements
The measurements were carried out for several scenarios:
  Static transmitter/receiver with no movement
  Static transmitter/receiver with person moving between them
  Transmitter moves away/towards the receiver

## Slide 6: Analysis
For every packet (of the 1024) we perform channel estimation
We compute the channel taps in the delay domain, and for each tap we compute the PSD
Finally, we average the PSD for all taps to obtain a single PSD for the measurement
We expect the Doppler spread to be very narrow for static measurements, and wider with movements; we further expect to see the impact of a moving transmitter in the form of a peak around the maximal Doppler shift

## Slide 7: Analysis
For movement towards the receiver at ~2km/h (~=0.5m/sec), the corresponding maximum Doppler shift is
Similarly for movement away from the receiver the shift is -4.6Hz
We hence expect to see the measured Doppler PSD around these (approximate) values for the measurements with a moving transmitter
  We performed several measurements for each movement direction in order to see that results are consistent and adhere to theory

## Slide 8: PSD Results
In case of stationary measurements, the PSD is very narrow (similar to the TGn-D 0.089km/h PSD)
For the moving person case, the PSD is wider and similar to the TGn-D 1.2km/h PSD

## Slide 9: PSD Results
The results for the moving transmitter cases, compared with TGn-D NLOS (using both 0.089km/h & 1.2km/h environmental speeds) are shown below
Moving away from Rx, PSD around ~-5Hz
Moving towards Rx, PSD around ~+3Hz

## Slide 10: Conclusions
Unlike a decade ago, smartphone usage today means Wi-Fi STAs are – in many cases – moving at pedestrian speeds in various indoor cases; such movement creates a Doppler PSD which should be accounted for in the 802.11be channel model
We presented the PSD corresponding to various measurements in an office scenario, with and without movements
We’ve shown that the existing TGn/TGac channel model Doppler PSD does not reflect the true PSD generated by STA movement
The 11be group should work on accommodating real-life Doppler such that simulations capture the real-life impact of indoor movements
Potential future work:
  Measurements at the 5GHz band
  Measurements with multiple antennas
  Evaluate how to accommodate practical/real-life Doppler within the 11be channel model

## Slide 11: References
11-03-0940-04-000n-tgn-channel-models
11-09-0308-12-00ac-tgac-channel-model-addendum-document