## Slide 1: Multi-Link BSS Operations
Date: 2019-09-06
Authors:

## Slide 2: Abstract
This submission discusses some of the major MLME functions for the Multi-Link model:
Pre-association operations
Authentication and Association
Post-association power management

## Slide 3: An Example of Overall Architecture

## Slide 4: Phases in Multi-Link Setup
Authentication exchange
Authentication exchange
Multi-Link AP
Link1
2.4G
Link1
2.4G
Link2
5G
Link2
5G
Link3
6G
Link3
6G
Association exchange
4-way handshake
Pre-association
Post association
Pre-association
Post association
Data channels
Data channel in 5G
Data exchange
AP discovery
Discover EHT APs and their links
Authenticate and create master keys
Associate to an EHT AP and signal/negotiate capabilities
Setup the pairwise and group transient key
Multi-Link STA

## Slide 5: Multi-Link Setup (1/2)
A Multi-Link AP is discoverable on all channels in which it operates, i.e. beacons and probe responses are transmitted on all links
  EHT STAs may discover the Multi-Link AP with multiple links in different channels
  Legacy STAs may discover multiple BSSs with the same SSID in different channels
A single authentication, association and 4-way handshake enable a Multi-Link STA to securely join a Multi-Link BSS
  Authentication and Association may be done in any link

## Slide 6: Multi-Link Setup (2/2)
The multi-link capabilities and operations are signaled / negotiated / confirmed during the association
  e.g. A Multi-Link STA can select its own operating link(s), based on a Multi-Link AP’s capabilities and operating links, and indicate its selection in the Associate Request frame
After association, a Multi-Link STA may use the Power Management and/or A-Control fields in MAC header to dynamically signal / change the availabilities of its operating links
  Examples are shown at the end of the submission

## Slide 7: Example:

## Slide 8: Power Management / Link Availability Examples
Indicate doze for the whole Multi-Link STA
Indicate awake for the whole Multi-Link STA
Indicate unavailability of a different link

## Slide 9: Power Management / Link Availability Approaches

## Slide 10: Summary
This submission discussed on major MLME functions of the Multi-Link BSS
The main principles of Multi-Link power save and link availability mechanisms are described

## Slide 11: Straw poll 1
Do you agree that a Multi-Link STA may signal on one link the availability of all links and/or other link(s)?
Yes:
No:
Abstain: