## Slide 1: What Should be the HARQ Unit and Why?
Date: 2019-09-15
Authors:
Name | Affiliation | Address | Email
Imran Latif | Quantenna Communications, division of ON Semi. | 1704 Automation Parkway, 95131, San Jose, CA, USA | ilatif@quantenna.com
Sigurd Schelstraete |  |  | sschelstraete@quantenna.com
Debashis Dash |  |  | ddash@quantenna.com
Huizhao Wang |  |  | hwang@quantenna.com
Sep, 2019

## Slide 2: Background
Hybrid-ARQ is a strong candidate feature for TGbe
Many results (MPDU and CW) have shown the benefits of HARQ
However, the HARQ unit is not defined yet
Definition of HARQ unit is extremely important towards standardization of HARQ
Therefore, in this presentation we present the HARQ unit which is most practical and natural to HARQ
Sep, 2019

## Slide 3: HARQ Unit
Many contributions [2-3] have shown and presented the HARQ unit as an option between the following two:
  MPDU
  Codeword (CW)
We want to highlight that considering MPDU as a HARQ unit candidate is not even an option
In the layered architecture of 802.11 there is no 1-to-1 mapping between MPDUs and CWs
Hence, CW is the only and most natural candidate for HARQ unit

## Slide 4: Framing in 802.11
MPDU-1
MPDU-2
MPDU-3
MPDU-N
MPDU-1
MPDU-2
MPDU-3
MPDU-N
A-MSDU
MPDU Header
Delimiters
…
…
EOF Padding
PSDU
Pre-FEC padding
Tail bits
Post-FEC padding
Scrambled DATA
Scrambling
Encoding
MAC
PHY
Service field
Codewords
There is no MPDU to CW mapping apparent in this layered architecture

## Slide 5: MPDU Level Limitations - I
It was shown in [1] that HARQ cannot be supported at the MPDU level due to,
  Misalignment of CWs in retransmitted MPDUs (from [1]) makes combining impossible
  Arbitrary numbers of delimiters (DL) among the MPDUs
  Each MPDU Header’s flipped retry bit upon retransmission
  Different Cipher Text on retransmissions
  Different CRC bits on retransmissions
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
MPDU Header
Ext-IV
Cipher Text
MIC
CRC
DL (Delimiter)
Pre-FEC Padding
Failed MPDU
…
CW-4
CW-5
Re-Tx MPDU
…
CW-1
CW-2
CW-3
At the Tx for Retransmission
At the RX
Sep, 2019

## Slide 6: MPDU Level Limitations - II
Though MPDU is perceived to be desired and simple HARQ unit we want to highlight that it is not even an option for HARQ for following reasons,
  different payload (even few bits) in each MPDU in retransmissions,
    the contents of the CWs will change, thus no combining at the PHY level
  the misalignment in the MPDU to CW mapping between first transmission and the retransmissions,
    Due to this misalignment it is not possible to combine LLRs for retransmitted MPDU at the PHY
  no knowledge of MPDUs at the PHY,
    MPDU is a MAC construct and has no notion at the PHY
Therefore, MPDU cannot be a unit for HARQ in 802.11be
Sep, 2019

## Slide 7: CW as HARQ Unit - I
Codeword level HARQ was presented in [1] for 802.11be
HARQ combining is closely tied to the forward error correction (FEC) that happens at the PHY level
  FEC unit is the codeword (CW)
    MDPUs are not FEC unit
    there is no 1-1 mapping between MPDUs and FEC unit
MPDU cannot be used as a unit for PHY layer since it is a MAC construct
Therefore, CW is the natural unit for HARQ as it provides the basic unit for PHY layer where the combining is supposed to happen
Sep, 2019

## Slide 8: Efficiency of CW as HARQ Unit
Lets consider an example with CW as HARQ unit and show how it can be beneficial
For Example,
Only three CWs are decoded wrong and due to this all of the MPDUs CRC fails
Not only that the retransmission of these MPDUs is spectrally in-efficient but it is also not possible to combine the failed codewords at the receiver due to the reasons mentioned previously
Sep, 2019
MPDU-1
MPDU-2
MPDU-3
MPDU-4
…
…
…
MAC
CRC Failed
CRC Failed
CRC Failed
CRC Failed
CW-1
CW-2
CW-3
CW-4
CW-5
CW-6
CW-7
CW-8
CW-9
CW-10
CW-11
Decoding Failed
Decoding Failed
Decoding Failed
PHY

## Slide 9: Flow of CW Retransmissions
In this case,
  RX sends back the CW level feedback
  TX receives this CW level feedback and it prepares for the transmission such that it informs the PHY to attach the failing CWs to the next transmission
  RX will receive this retransmission and decodes the HARQ-SIG part to find out which CWs are to be combined
Sep, 2019
Rx
PHY
Rx
MAC
A-MPDU
CW/dual FB
Data
HARQ-SIG
HARQ Combining
A-MPDU
Data
HARQ-SIG
ReTx CWs
CW/Dual FB
Tx
PHY
Tx
MAC
SIG Decoding
Data Decoding
SIG Decoding
Data Decoding
. . .

## Slide 10: Summary
MPDU is a MAC construct
  Not identifiable on PHY layer
When handled by the MAC, retransmitted MPDUs:
  don’t have the same bit content
  don’t map to the same codewords as the original transmission
Even an entire A-MDPU retransmission does not result in the same bit stream on the PHY layer (PSDU)
Combining (both CC and IR) is closely tied to error correction and happens at the PHY level
  MDPUs do not have self-contained FEC unit
  No consistent mapping between MPDUs and CWs
    Multiple CW per MPDU
    CW can overlap multiple MPDUs

## Slide 11: Conclusion: HARQ Unit = Codeword
PHY provides natural unit for HARQ and that is Codeword
MPDU as a HARQ unit is a practical impossibility
Therefore, we propose to use the codeword as a HARQ unit and perform all simulations and studies with CW level retransmissions

## Slide 12: Straw-Poll
Do you agree that HARQ unit for 802.11be shall be based on codewords?
Y
N
A
Sep, 2019

## Slide 13: References
[1] 11-19/0873r1 – HARQ Framing – Imran Latif (Quantenna)
[2] 11-19/1038r1 – HARQ with A-MPDU – Shimi Shilo (Huawei)
[3] 11-19/1131r0 - Consideration on HARQ Unit - Taewon Song (LG Electronics)

## Slide 14
Backup Slide

## Slide 15: What about BCC ?
Previous slides showed HARQ unit for LDPC encoders
However, in BCC there is no notion of codewords
BCC has very limited support in 11ax (only 20 MHz)
LDPC is the de-facto FEC encoder/decoder for 11ax onwards
Therefore, focus of HARQ for TGbe should be on LDPC
It is not necessary to define HARQ for BCC