## Slide 1: Simulation Results for coordinated OFDMA in multi-AP operation
Date: 2019-08-02
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yiqing Li |  |  |  | 

## Slide 2: Introduction
Multi-AP operation is considered as a major candidate feature for 802.11be [1].
There are four modes of Multi-AP operation that are under discussion in EHT SG and TGbe:
  Coordinated BF [2][3][5][7][8]
  Coordinated OFDMA [2][3][8]
  Coordinated SR [4][9]
  Joint transmission [2][3][5][6][10][11]
Among the four modes, Coordinated OFDMA has been proposed without simulation results, while other three modes are demonstrated by simulation results to show performance gain in different scenarios [4-11].
In this contribution, we evaluate the performance of coordinated OFDMA by system level simulation results.

## Slide 3: Simulation Scenario
We consider a two-BSS scenario (e.g., home environment), where two APs are 20 meters away from each other.
In each BSS, there is one STA randomly placed in the coverage range of each AP.
Total bandwidth: 160MHz
Packet size: 1500bytes
A-MPDU: 64 (Maximum)
MCS: 9
Nsts: 1

## Slide 4: Simulation Scenario
Traffic Model: Burst traffic
  Packets arrive in the form of bursts, for each burst, there are 400 packets
  Packets are assumed to arrive at the beginning of each burst, all arrive at the same time
  The traffic data rate affects the burst interval: the higher traffic data rate, the shorter burst interval
…
Burst 1
…
Burst 2
…
Burst 3
……
Burst interval
……
…
Burst 4
Performance Metric: Burst throughput
  Burst throughput = Number of bits in a burst / (T1 – T0)
    T0 is the time that the first bit of the burst comes into the buffer
    T1 is the time that the whole burst is transmitted successfully
  We simulate 150 bursts, and calculate the average burst throughput as the performance metric
  Delay (T1 – T0) is also used as a performance metric

## Slide 5: Transmission Procedure
Coordinated OFDMA
  Two APs share the whole 160MHz bandwidth
  Two APs stay on the same primary channel, and contend to access the channel using EDCA.
  When the backoff counter reaches zero, each AP will do the following
    With probability p, the AP will send a slave trigger frame to the other AP to initiate co-OFDMA transmission, where each AP can use 80MHz to do the data transmission
    With probability 1-p, the AP will use the whole 160MHz channel to do the data transmission
Baseline
  Two APs will use two different 80MHz channels for data transmissions
  The two 80MHz channels are non-overlapping with each other
 | Coordinated OFDMA | Baseline
Pros | Dynamic bandwidth | Dedicated channel No collision
Cons | Collision may happen Slave TF overhead | Maximum bandwidth is limited

## Slide 6: Simulation Results
When traffic data rate is low, co-OFDMA has a wide dynamic range of burst throughput, depending on the probability of using co-OFDMA
  When co-OFDMA is not used, each AP can occupy the whole 160MHz, making it faster to finish the transmission of a burst
When traffic data rate is high, using baseline is slightly better, since the packet loss rate is lower, but there’s not much different between all the schemes
In conclusion, using co-OFDMA with lower probability is better

## Slide 7: Simulation Results
Delay is a direct transform of burst throughput
Under low traffic data rate, using co-OFDMA with lower probability can provide better delay performance, because using wider bandwidth can reduce the delay significantly;
Under high traffic data rate, baseline is slightly better, but there are not much difference among all the schemes.

## Slide 8: Conclusion
  We evaluate the performance of co-OFDMA by system level simulation results in home environment.
  The results show that using co-OFDMA with higher probability does not provide much performance gain regarding burst throughput and latency, conversely, using co-OFDMA with lower probability is better.
  It is encouraged for people to do more simulation on co-OFDMA to show the performance gain.

## Slide 9: Reference
[1] 11-18-1231-06-0eht-eht-draft-proposed-par
[2] 11-18-1576-01-0eht-considerations-on-ap-coordination
[3] 11-18-1509-00-0eht-features-for-multi-ap-coordination
[4] 11-19-801-00-0eht-ap-coordination-in-eht
[5] 11-18-1510-01-0eht-ap-coordinated-beamforming-for-eht
[6] 11-19-0800-00-00be-joint-processing-mu-mimo-update
[7] 11-19-0638-00-00be-nulling-and-coordinated-beamforming
[8] 11-18-1155-01-0eht-Multi-AP Enhancement and Multi-Band Operations
[9] 11-19-0071-00-0eht-Coordinated Multi-AP Transmission for EHT
[10] 11-19-0763-00-00be-measurements-for-distributed-mu-mimo
[11] 11-19-0779-01-00be-performance-investigation-on-multi-ap-transmission