## Slide 1: Joint Sounding for Multi-AP Systems
Date: 2019-09-12
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | jianhan.liu@mediatek.com
Li Ma |  |  |  | 
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Channel Sounding for Multi-AP systems
Spatial nulling, coordinated OFDMA and SU beamforming all required channel state information (CSI) available at the transmitter.
Implicit sounding can not completely replace the explicit channel sounding in 11be
  For example, for MU-MIMO (from a single AP), implicit sounding quality may not be good enough.
  Implicit sounding requires calibrations. Calibration accuracy is up to each vendor.
We investigate the different channel sounding schemes for multi-AP systems.

## Slide 3: Option 1: Sequential channel sounding
Sequential channel sounding:
  Based on single AP sounding
  Each AP performs channel sounding separately, similar to the single AP sounding in 11ax.
  Given the fact that 11be shall have the single AP sounding protocol, there is no way to disallow sequential channel sounding for multi-AP systems.
Two Major Issues:
  Sequential channel sounding suffers efficiency degradation compared to other Joint sounding schemes for multi-AP systems.
  Sequential channel sounding can not enable joint transmissions because each STA only feedbacks the compressed V matrix between each AP and itself.

## Slide 4: Option 2: Joint channel sounding
  The coordinate AP initiates the Joint sounding.
  The sounding APs send out sounding packet simultaneously.
  The sounded STAs feedbacks CSI.
  The above is just an example, the detailed sounding procedure is TBD.

## Slide 5: Option 2a: 11ax-like LTFs
Global Antenna Indexing: For example, as shown in the following figure, there are two sounding APs: AP 2 with N2 antennas and AP 3 with N3 antennas.
11ax-like LTFs: All sounding APs send LTFs by regarding its own antennas as a subset of all antennas from all sounding Aps

## Slide 6: Option 2a: 11ax-like LTFs (continues)
Each non-pilot subcarrier of the Stacked LTFs are multiplied by the matrix P and transmitted by every sounding AP.
 | Multiplied Coefficient for LTF #1 | Multiplied Coefficient for LTF #2 | Multiplied Coefficient for . . . | Multiplied Coefficient for LTF # (N2+N3)
Global Tx Antenna # 1 | P(1,1) | P(1,2) | . . . | P(1, N2+N3)
Global Tx Antenna # 2 | P(2,1) | P(2,2) | . . . | P(2, N2+N3)
. . . | . . . | . . . | . . . | . . .
Global Tx Antenna # (N2+N3) | P(N2+N3,1) | P(N2+N3,2) | . . . | P(N2+N3, N2+N3)

## Slide 7: Pros and Cons of Option 2a
Pros:
  Option 2a reduces the number NDPAs and NDPs compared to sequential sounding.
  Similar sounding approach as in 11ax
Cons:
  Not high efficiency: A lot of BE-LTFS needs to be transmitted
    2x LTFs can be used to reduce sounding overhead
  Large P matrix which increases the complexity of channel estimation and CFO estimation and correction.

## Slide 8: Option 2b: Subcarrier Interleaved LTFs
Local Antenna Indexing: For example, as shown in the following figure, there are two sounding APs: AP 2 with N2 antennas and AP 3 with N3 antennas.
Subecarrier Interleaved LTFs : Each sounding APs send LTFs on its allocated subcarriers.

## Slide 9: Option 2b: Subcarrier Interleaved LTFs
Non-pilot subcarriers of each LTF are allocated among the sounding APs such that each non-pilot is only allocated to one AP.
  The transmit signal are multiplied by a matrix P
  For example, if there are two sounding APs, then
    The odd-indexed subcarriers (subcarriers in green color) are allocated to one sounding AP
    The even-indexed subcarriers (subcarriers in red color) are allocated to the other sounding AP.

## Slide 10: Pros of option 2b
Option 2b further reduces the number of LTFs compared to option 2a.
Option 2b applied with small size P matrix and therefore reduces CFO estimation and correction.

## Slide 11: Simulation Results
We simulated the channel sounding qualities for different sounding schemes.
Simulated settings:
  Two sounding AP’s each with 2 Tx’s. AP1 sounding on odd tones and AP2 sounding on even tones.
  STA to be sounded has 2 Rx’s.
  20MHz BW
  D-NLOS channel
  Normal distributed residual CFO after synchronization, zero-mean, STD in Hz.
  Received power differences

## Slide 12: 11ax like LTFs with perfect synchronization

## Slide 13: 11ax like LTFs with residual synchronization errors
4x LTFs are more vulnerable to CFO errors.

## Slide 14: Subcarrier Interleaved LTFs with perfect synchronization
No considerable loss associated with interleaved 2AP Joint sounding.

## Slide 15: Subcarrier Interleaved LTFs with residual synchronization errors
Negligible loss for CFO with STD smaller than 100Hz.

## Slide 16: Performance with residual synchronization errors and receive power difference
Little performance loss due to power differences.

## Slide 17: Straw Poll #1
Do you agree that 11be shall provide a joint NDP sounding scheme as optional mode for multiple-AP systems?
Note: Sequential sounding scheme can also be used for multi-AP systems.