## Slide 1: Preamble Puncturing and SIG-B Signaling
Date: 2019-11-09
Authors:
Name | Affiliations | Address | Phone | email
John (Ju-Hyung) Son | WILUS, Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0524 | john.son@wilusgroup.com
Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Sanghyun Kim | Seoul Nat’l Univ. of Science and Technology | ​232 Gongneung-ro, Nowon-gu, Seoul, Korea | +82-2-970-6455 | shk0787@seoultech.ac.kr
Wisnu Murti |  |  |  | wisnumurti@seoultech.ac.kr
Ji-Hoon Yun |  |  |  | jhyun@seoultech.ac.kr
Young Seok Oh | SK Telecom | 9-1 Sunae-dong, Bundang-gu, Seongnam-si, Gyeonggi-do, Korea | +82-31-710-5370 | ysoh0705@sk.com

## Slide 2: Introduction
EHT supports wider bandwidth operation
  EHT PAR [1] includes support for 320MHz bandwidth
  However, it is hard to expect the whole 320MHz channel to be idle in dense environments
  EHT needs to enhance the utilization of non-contiguous channel access method [2][3]
SIG-B content channel design and Preamble puncturing
  With support of 320MHz PPDU and 16 spatial streams, the signaling overhead of EHT-SIG-B will be increased [4]
  EHT may need to extend 11ax’s SIG-B content channel design to further distribute signaling overhead to multiple 20MHz channels
  Therefore, EHT’s preamble puncturing modes should also consider SIG-B content channel design
In this submission, we discuss various preamble puncturing modes in 320MHz under several SIG-B content channel options
  To investigate trade-off between signalling overhead and channel access flexibility in various OBSS load environments

## Slide 3: Backgrounds: HE-SIG-B content channels
HE-SIG-B has two content channels
  20 MHz HE MU PPDU contains one SIG-B content channel
  40, 80, 160 MHz HE MU PPDU contain two SIG-B content channels
  The two SIG-B content channels distribute signaling overhead of multiple STAs into two channels
  However, receivers should be able to decode two SIG-B content channels simultaneously to decode its per-STA information

## Slide 4: Backgrounds: HE MU PPDU BW modes
HE-SIG-A’s BW subfield indicates the overall PPDU BW and SIG-B channel locations
HE-SIG-B’s RU allocation subfield further indicates each secondary 20MHz’s puncturing
BW=0
P20
P20
P20
P20
Busy
Busy
Busy
Busy
Busy
Busy
Busy
Busy
P20
P20
P20
P20
P20
P20
P20
BW=1
BW=2
BW=3
BW=4
BW=5
BW=6
BW=7
1
2
1
2
1
2
1
2
HE-SIG-B
Channels
1
2
1
2
1
2
1
2
HE-SIG-B
Channels
Idle
Busy
Idle or
Busy
The limited puncturing patterns within P80 is to let receivers to decode both SIG-B channels within the Primary 80MHz

## Slide 5: EHT-SIG-B content channel options
There can be at least three SIG-B content channel options as follows:
  Option 1 (1, 1, 1, 1): duplicating SIG-B information per 20MHz
  Option 2 (1, 2, 1, 2): duplicating SIG-B information per 40MHz, with different SIG-B information in each 20MHz within the 40MHz
  Option 3 (1, 2, 3, 4): duplicating SIG-B information per 80MHz, with different SIG-B information in each 20MHz within the 80MHz
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
320 MHz
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
1
2
1
2
1
2
1
2
1
2
1
2
1
2
20 MHz
320 MHz
40 MHz
320 MHz
80 MHz

## Slide 6: 320MHz EHT PPDU BW modes (Option 1)
High signaling overhead vs. Most flexible puncturing pattern
  The same SIG-B content per 20MHz incurs high signaling overhead
    May reduce the overhead by using the higher modulation on SIG-B
  Enables most flexible preamble puncturing patterns in secondary channels
    May freely occupy idle 20MHz secondary channels if the Primary is idle
P20
P20
320MHz
1
1
1
1
1
1
1
1
EHT-SIG-B
(1,1,1,1)
1
1
1
1
1
1
1
1
320MHz
Preamble
Puncturing
Idle
Busy
Idle or
Busy
320 MHz
20 MHz

## Slide 7: 320MHz EHT PPDU BW modes (Option 2)
Mid signaling overhead vs. Flexible puncturing pattern
  The same SIG-B content channel design as 11ax
  11ax’s preamble puncturing pattern extended upto 320MHz
P20
Busy
Busy
Busy
Busy
Busy
P20
P20
P20
P20
320MHz
1
2
1
2
1
2
1
2
EHT-SIG-B
(1,2,1,2)
1
2
1
2
1
2
1
2
320MHz
Preamble
Puncturing
Idle
Busy
Idle or
Busy
320 MHz
40 MHz

## Slide 8: 320MHz EHT PPDU BW modes (Option 3)
Low signaling overhead vs. Inflexible puncturing patterns
  Different SIG-B information per 20MHz upto 80MHz
  Receiver should decode four SIG-B content channels in Primary 80MHz, therefore the puncturing is only enabled in the other secondary channels excluding the P80
P20
P20
320MHz
1
2
3
4
1
2
3
4
EHT-SIG-B
(1,2,3,4)
1
2
3
4
1
2
3
4
320MHz
Preamble
Puncturing
Idle
Busy
Idle or
Busy
320 MHz
80 MHz

## Slide 9: Simulation Setup
Investigate performances of different preamble puncturing options in OBSS environments
EHT BSS
  1 BSS operating BW: 320MHz
  1AP-1STA, DL only, full buffer
  MCS 7 fixed, A-MPDU (Max 64 MPDUs), 1 MPDU=1500 Bytes
  PPDU BW: P20, P40, P80, P160, P320, and preamble puncturing BW based on its CCA results
  Assume SIG-B overhead of 4 symbols (16us) required per 20MHz in PPDU BW
OBSS
  Among 320MHz channels, 3 OBSSs exist per each 80MHz segment
  Each OBSS’ operating BW: 80MHz / 40MHz / 20MHz each
  Primary channel is randomly chosen within each 80MHz segment
  PPDU BW: P20, P40, or P80 based on CCA results (no puncturing)
  Each OBSS has 1AP-1STA, DL only, CBR 10Mbps or CBR 50Mbps
  MCS 7 fixed, A-MPDU (Max 64 MPDUs), 1 MPDU=1500 Bytes

## Slide 10: Simulation Setup (OBSS example)
P20
EHT BSS
(320 MHz)
OBSS 1
(80 MHz)
OBSS 2
(40 MHz)
OBSS 3
(20 MHz)
Fixed P20
location
3 OBSS per 80MH segment
random P20 location for each OBSS
80 MHz
320 MHz

## Slide 11: Simulation Results (EHT BSS’s PPDU BW)
Chart: OBSS Load : 10 Mbps
| 20 MHz | 40 MHz | 80 MHz | 120 MHz | 160 MHz | 200 MHz | 240 MHz | 280 MHz | 320 MHz
Option 1 | 0.1 | 0.32 | 0.66 | 1.58 | 2.75 | 3.95 | 6.12 | 8.38 | 9.9 | 12.05 | 11.86 | 12.3 | 9.45 | 7.9 | 4.58 | 2.3
Option 2 | 3.23 | 0.21 | 0.38 | 1.41 | 2.11 | 3.7 | 5.38 | 8.15 | 8.81 | 11.64 | 11.74 | 11.82 | 9.85 | 8.37 | 4.57 | 2.8
Option 3 | 12.42 | 30.82 | 0 | 0.34 | 0.23 | 0.75 | 1.12 | 2.52 | 2.43 | 4.63 | 5.43 | 7.68 | 6.21 | 7.65 | 6.35 | 5.95
Option 0 | 12.99 | 33.52 | 0 | 25.36 | 0 | 0 | 0 | 15.7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.95
Option 1 utilizes wide PPDU BW due to its flexible puncturing mode
Option 2 also utilizes wide PPDU BW comparable performances to Option 1
  However, as OBSS Load increases, Option 2 fails to secure its SIG-B channels in P80, thus failing preamble puncturing transmission (increased 20MHz PPDU percentage)
Option 3 shows poor performances from its inflexible puncturing option in Primary 80MHz
  Option 3 rarely uses preamble puncturing under high OBSS Load in P80
Chart: OBSS Load : 50 Mbps
| 20 MHz | 40 MHz | 80 MHz | 120 MHz | 160 MHz | 200 MHz | 240 MHz | 280 MHz | 320 MHz
Option 1 (1,1,1,1) | 0.01 | 0.2 | 1.62 | 4.89 | 10.27 | 15.08 | 19.16 | 16.7 | 13.81 | 7.31 | 3.4 | 1.32 | 0.25 | 0.05 | 0.03 | 0.11
Option 2 (1,2,1,2) | 11.46 | 0.08 | 0.62 | 3.37 | 8.39 | 13.55 | 16.72 | 15.14 | 13.46 | 6.74 | 3.49 | 1.1 | 0.2 | 0.06 | 0.04 | 0.17
Option 3 (1,2,3,4) | 26.4 | 53.06 | 0 | 0.14 | 0.39 | 1.31 | 2.16 | 2.92 | 3.02 | 2.55 | 1.38 | 0.49 | 0.17 | 0.05 | 0.04 | 0.14
Option 0 (No puncturing) | 26.27 | 53.31 | 0 | 13.86 | 0 | 0 | 0 | 0.25 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.16

## Slide 12: Simulation Results (EHT BSS’s TPUT)
Option 1 shows the best channel accessibility, but throughput is lower than Option 2 under small OBSS load due to its SIG-B overhead
Option 2 shows good balance in terms of channel accessibility and SIG-B overhead, but the performance is highly affected by OBSS loads
Option 3 cannot benefit from its short SIG-B lengths, since it cannot utilize preamble puncturing in OBSS loads
Chart: Throughput (Mbps)
| Option 1 (1,1,1,1) | Option 2 (1,2,1,2) | Option 3 (1,2,3,4) | Option 0 (No puncturing)
OBSS Load : 10 Mbps | 312.1869 | 345.9866 | 195.5251 | 158.4333
OBSS Load : 50 Mbps | 204.2624 | 190.2413 | 88.2406 | 87.4266

## Slide 13: Conclusions
We presented several preamble puncturing patterns based on three SIG-B content channel design options
Simulation results show that preamble puncturing drastically increase channel access opportunity in dense OBSS environments
Among three SIG-B channel options discussed
  Option 1 (1,1,1,1) and 2 (1,2,1,2) show favorable performance with signaling overhead tradeoffs
  Option 3 (1,2,3,4) shows low performance due to the limited preamble puncturing pattern in Primary 80MHz
We propose to further study preamble puncturing options in 11be

## Slide 14: References
[1] 11-18-1231-06-0eht-eht-draft-proposed-par
[2] 11-19-1242-00-00be-wider-bandwidth-channel-access-in-eht
[3] 11-19-1190-00-00be-improved-preamble-puncturing-in-802-11be
[4] 11-19-1099-00-00be-preamble-structure-in-11be