## Slide 1
Authors:
Multi-band/Multi-channel(Multi-link) Operation for Low Latency and Jitter
Date: 2019-11-7
Name | Affiliation | Address | Phone | Email
Liuming Lu | ZTE Corporation | No.889 Bibo Road, Shanghai, P.R.China |  | lu.liuming@zte.com.cn
Liquan Yuan |  |  |  | 
Bo Sun | ZTE Corporation | No.9 Wu Xing Section, Xi Feng Road, Xi’an, Shaanxi Province, P.R.China |  | 
Nan Li |  |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Introduction
Multi-link operation has been proposed as a main candidate feature in TGbe. And at least one mode of operation capable of improved worst case latency and jitter will be defined in TGbe.[1][2]
This contribution gives some views on multi-link operation to improve worst case latency and jitter for the real-time transmission of RTA data.

## Slide 3: Background
Multi-link operation can improve the worst case latency and jitter since it uses two or more bands or channels (links) to transmit data and the effective control of the traffic transmission on different links is beneficial to the improvement of latency performance.
However how much multi-link operation can improve the worst case latency and jitter needs to be considered.
Multi-band operation has been specified in the current 802.11 standard, which supports transparent fast session transfer (FST) and nontransparent FST, but lacks the detailed mechanisms to support the real-time transmission of RTA data.
The current 802.11 standard has specified admission control at the HC which supports two distinct admission control mechanisms: one for contention based access and another for controlled access. The contention based admission control is for ACs with EDCA parameters, and no admission control for links is involved.

## Slide 4: Requirements for the optimization of multi-link operation
Contribution[3] has presented latency gains with multi-link aggregation, showing that adding an auxiliary link significantly improves the worst-case latency. But the latency gains seem to be not enough to support the RTA, such as virtual reality or augmented reality.
Use cases |  | Intra BSS latency/ms | Jitter variance/ms | Packet loss | Data rate/Mbps
Real-time gaming |  | < 5 | < 2 | < 0.1 % | < 1
Cloud gaming |  | < 10 | < 2 | Near-lossless | <0.1 (Reverse link) >5Mbps (Forward link)
Real-time video |  | < 3 ~ 10 | < 1~ 2.5 | Near-lossless | 100 ~ 28,000
RTA use cases and requirements (examples) [4]
Latency gain results of simulation [3]
MCS0 | 1 OBSS STA per link | 2 OBSS STAs per link | 4 OBSS STAs per link | 8 OBSS STAs per link
Multi Link (80MHz+20MHz) | 9.24 | 22.89 | 61.88 | 325.2
The mechanisms for multi-link operation, such as channel access method, time scheduling, admission control etc., need to be optimized to satisfy the requirements for low-latency and jitter performance.

## Slide 5: Channel access methods for multi-link operation
Flexible channel access methods can be considered for multi-link operation. Different kinds of channel access methods can be respectively adopted for different links.
The channel access methods to support time scheduling for RTA data are preferred to be adopted, and the contention-based channel access methods are suitable for the non-RTA data.
For the manageable environment in some link HCCA can also be considered besides CSMA/CA and triggered-based channel access method.
link1
AP
link2
STAs
CSMA TXOPS
CAP (Controlled Access Phase)
CSMA TXOPS
link1
link2
Schedulable TXOPs
for RTA data
TXOPs through contention
for non-RTA data

## Slide 6: Admission control for multi-link operation
Since admission control is a direct method to lower latency and jitter, flexible admission control strategies can be adopted for different bands or channels according the types of application, the priorities of the services, the types of STAs, etc.
Different kinds of applications can be loaded on different bands or channels. For example, the RTA data which needs low latency and jitter is controlled to be transmitted on one channel or band, and the data of best-effort applications is controlled to be transmitted on the other channels or bands.
The number of the STAs to access the channel which transmits the data of RTA applications is strictly limited to guarantee the low latency and jitter performance.

## Slide 7: Conclusions
The combination of multi-link operation, time scheduling and admission control needs to be considered to further lower the latency and jitter so as to satisfy the requirements for RTA.
Flexible channel access methods can be considered for multi-link operation. Different kinds of channel access methods can be respectively adopted for different links according to the environment of the links and the types of the applications loaded on the links.

## Slide 8: Straw Poll 1
Do you agree that admission control could be applied on each link independently?
Y/N/A=

## Slide 9: References
11-18-1231-06-0eht-eht-draft-proposed-par, 802.11 EHT Proposed PAR
11-18-1233-07-0eht-eht-draft-proposed-csd, IEEE 802.11 EHT draft Proposed CSD
11-19-1081-01-00be-multi-link-aggregation-gain-analysis-latency,Multi-Link Aggregation: Latency Gains
11-19-0065-06-0rta-rta-tig-summary-and-recommendations, RTA report summary

## Slide 10
Thank you!