## Slide 1: Multi-Link Power Save
Date: 2019-09-09
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | Marvell |  |  | 

## Slide 2: Recap: Multi-link
A multi-link AP/STA entity includes multiple links.
  Each link has one AP/STA affiliates with it.
  The multiple APs/STAs of a multiple-link AP/STA entity share the same MLLE.
It is not clear how to define power save for multi-link AP/STA entity.

## Slide 3: Recap: 11baseline Power Save
Operation mode change:
  NSS, BW change from STA side and AP side.
  The following power save feature works with the available BW announced by operating mode change.
Power save at STA.
  Power save mode,
  Power save state when working in Power Save Mode
SM (Spatial Multiplexing) power save.
…

## Slide 4: Link Enablement/Disablement
The reason to decouple link enablement/disablement from power save (Active + Power Save, Awake + Doze):
  This can be a specific mode of operating mode change, BW change announcement where the BW of a link can become 0.
  Multi-link AP entity can disable its links also.
Once a link is disabled, no traffic can be transmitted in the link and no power save mode negotiation is done in the link
Different links in a multi-link STA/AP entity can be in different state (enable, disable).
Multi-link AP entity can request link enablement/disablement of the links of a multi-link STA entity.
Multi-link STA/AP entity can notify its peer multi-link entity of the link enablement/disablement of its links.
When a link is enabled, a multi-link STA entity can change its power save mode in the link.
With link enablement/disablement, a multi-link STA entity can
  Save power compared with the mode that all links are in on state
  Guarantee real-time requirement since a multi-link AP entity can transmit DL frames to the multi-link STA entity right away.

## Slide 5: STA Power Save
The power save mode of different links of a multi-link STA entity can be different.
  The power save mode of a link can be announced through another link or the same link.
  The power save mode announcement of other link can be carried in HE Control field.
Buffered frame indication in one link can be broadcasted in another link, e.g. in master link.
  Multi-link AP entity and multi-link STA entity can negotiate which link to receive the buffered frame indication.

## Slide 6: STA Power Save (Cont’d)
The multi-link STA entity notifies power save STA’s awake through PS-Poll, QoS Null etc. (HE Control could be used when link2’s awake is notified in link1’s frame exchange).
Link1 (master link)
Link2 (slave link)
Multi-link AP entity1
MAC Addr11
Common MAC
Link1
MAC Addr21
Link2
MAC Addr19
Common MAC
Link1
MAC Addr29
Link2
Multi-link STA entity
Power Save mode
Beacon
Beacon
Beacon
Beacon
QoS Null
Ack
Buffered frames for Addr19, Addr29 (the indication can be in TIM of link2 Beacon also)
A-MPDU2
MAC Addr19, Addr29 are awake.
BA
MAC Addr29 is doze
Frames for Addr29 is coming.
Frames for Addr19 is coming.
MPDU
Ack
MAC Addr19 is doze

## Slide 7: Straw Poll 1
Do you agree that for a MLLE each STA on an enabled link maintains its own power save mode/state?

## Slide 8: Straw Poll 2
Do you support that
  An AP of an AP MLLE may transmit on a link a frame that carries an indication of individually addressed frames buffered for transmission on other link(s)
    An non-AP MLLE needs to be aware on which link(s) the AP MLLE provides the indication
    The mechanism to determine on which link(s) the AP MLLE provides the indication is TBD
  An AP of an AP MLLE may transmit on a link a frame that carries an indication of individually addressed frames buffered for transmission on any enabled links
    An non-AP MLLE needs to be aware on which link(s) the AP MLLE provides the indication
    The mechanism to determine on which link(s) the AP MLLE provides the indication is TBD
  An AP of an AP MLLE may be restricted to indicate individually addressed frames buffered for transmission on a link within frame only transmitted on that link