## Slide 1: TESLA Based Frame Authentication
Date: 2019-09-17
Authors:

## Slide 2: Abstract
This presentation describes an additional information about TESLA based frame authentication that is proposed in 11-19/451r3.

## Slide 3: TESLA
TESLA is an algorithm that enables all receivers check integrity and authenticate the source of each frame in multicast or broadcast data stream.
TESLA uses One-way key chain.
One-way key chain is based on the nature of one-way hash function.
  In case of Vi+1 = Hash(Vi)
    Calculating Vi+1 from Vi is easy.
    Calculating Vi from Vi+1 is difficult. (practically impossible)
Vi
Vi+1
easy
difficult

## Slide 4: Key Generation
A transmitter generates a series of keys by using hash function.
K0
K1
Hash
K2
Hash
Hash
KN-1
Hash
K’0
K’1
K’2
K’N-1
Hash’
Hash’
Hash’
Hash’
Random Seed
KN
Hash
K’N
Hash’

## Slide 5: Authenticator Generation
The transmitter generates authenticator by HMAC hash function with the generated key.
The key to generate the authenticator is changed in a fixed duration Tk in reverse sequence of the key chain.
Data
HMAC-Hash(Key = K’i)
Authenticator
time
TK
K’N-1
TK
K’N-2
TK
K’N-3
TK
K’N-4
TK
K’N-5
TK
K’0

## Slide 6: Key Disclosure
The transmitter discloses the keys after d * Tk (d >= 2)
time
TK
K’N-1
TK
K’N-2
TK
K’N-3
TK
K’N-4
TK
K’N-5
TK
K’0
KN-1
KN-2
KN-3
Disclosed Key
(d = 2)
K2
Authenticator Key
Data
Auth (K’N-1)
Data
Auth (K’N-2)
Data
Auth (K’N-3)
KN-1
Data
Auth (K’N-4)
KN-2
Data
Auth (K’N-4)
KN-3
Data
Auth (K’0)
K2

## Slide 7: Frame Authentication
Receiver buffers frames until the key is disclosed.
The key integrity is verified as following:
  If Hash(Ki-1) = Ki and Ki is already verified, Ki-1 is correct.
The buffered frames are authenticated by the key calculated from the disclosed key.
K’N
K’N-1
K’N-2
K’N-3
K’N-4
K’N-5
KN
KN-1
KN-2
KN-3
time
Key for authenticator
Disclosed Key
Verify
Verify
Verify
K’N
Hash’
Authenticate frames
signed by K’N

## Slide 8: The First Key Verification
The first key, KN, has to be verified by other method.
KN should be verified by public key algorithm
KN
Signature

## Slide 9: The Last d keys Disclosure
The last d keys, K1 and K0 when d = 2, should be disclosed after the key sequence finished.
time
K’0
K2
Data
Auth (K’0)
K2
K1
K0
Tk

## Slide 10: Frame Sequence
eBCS Info frame
Transmitted in TI interval
TK
TI
eBCS Data frames
  eBCS Info frame includes
  Ks,N (where s is the seq num of eBCS Info)
  Ks-1,L (where L is the last used key index)
  Ks-1,L+1 (if d = 2)
  Timestamp
  TI
  TK
  d
  eBCS Info sequence number
  Public key with CA signature
  Signature by the sender’s private key
Sender generates one-way key chain before
generating each eBCS Info frame
(Ks,N, Ks,N-1, Ks,N-2, …, Ks,0)
  eBCS Data frame includes
  Ks,i+2 (where s is the seq num of eBCS Info, d=2)
  As,i (Authenticator generated by the key K’s,i)
  Key index: i
  eBCS Info seq num: s

## Slide 11: Recovery from Missing Frames
Sequence S
AS,0
KS,2
Sequence S+1
KS,0
KS,1
KS+1,8
AS,1
KS,3
AS,2
KS,4
AS,3
KS,5
AS,4
KS,6
AS,5
KS,7
KS-1,0
KS-1,1
KS,8
In case of missing KS,5 and KS,4:
KS,5 and KS,4 can be calculated from KS,3
KS,4 = Hash(KS,3)
KS,5 = Hash(KS,4)
In this case, the receiver has to buffer the frames
that have the authenticator generated by KS,5 and KS,4
until receiving KS,3.

## Slide 12: Dummy Data Frame
Sequence S
AS,0
KS,2
Sequence S+1
KS,0
KS,1
KS+1,8
AS,1
KS,3
AS,2
KS,4
AS,3
KS,5
AS,4
KS,6
AS,5
KS,7
KS-1,0
KS-1,1
KS,8
TESLA key is usually piggybacked in eBCS frames.
In case of no data to be sent in a TK, the transmitter transmits a dummy data frame which
includes the key to be disclosed at the end of the TESLA key period.
Dummy Data Frame

## Slide 13: Parameters
d: Fixed to 2 is reasonable
TK: Longer TK requires receivers’ memory to buffer received frames. The clock of the transmitter and the receivers have to be roughly synchronized with the accuracy of TK to prevent from replay attack.
TI: Longer TI requires the transmitter’s memory to store a sequence of key chain.