## Slide 1: Multiple Link Asynchronous and Synchronous Transmission
Name | Affiliations | Address | Phone | email
Alan Jauh | Unisoc |  | +86-131-6727-1685 | alan.jauh@unisoc.com
Yanchao Hsu |  |  |  | 
Henry Yu |  |  |  | 
Long Wang |  |  |  | 
Date: 2019-09-18
Authors:

## Slide 2: Introduction
In multiple link transmission, the asynchronous mode has better performance compared to synchronous mode
When the isolation between two links is not good enough, the TX in one link will have significant interference to the other link. In this case, asynchronous transmission is not possible and synchronous mode is required
We propose a mixed asynchronous and synchronous transmission mode

## Slide 3: Asynchronous vs. Synchronous
Asynchronous:
  In an asynchronous multiple links mode, the transmission between links is independent
Synchronous:
    Several links in a synchronous mode form a synchronous group
    The transmission in a synchronous group is synchronized
      “Synchronized” means to avoid simultaneous TX and RX within a synchronous group
    The backoff process is TBD. In a single primary case, the backoff process is in primary link

## Slide 4: Primary Channel in Synchronous Mode
Single primary channel and Multiple primary channels have been proposed.
The proposed mixed synchronous and asynchronous solution do not have the limitation on the number of primary channels in a synchronous group
Single primary channel in a synchronous group is slightly preferred due to
  The operation is similar to 80+80 mode and the interoperability is proved

## Slide 5: Mixed Synchronous & Asynchronous Configuration
A synchronous group can be an asynchronous multiple link element, (here use primary link to represent the synchronous group) e.g.
  A multiple links system is configured having links A, B, C and D
  The isolation between link B and link C is not good enough, so link B and link C form a synchronous group and link B is the primary link
  In this case, the transmission between link A, B, D is asynchronous
  Link C is the secondary link of a synchronous group with primary link B. The transmission of link C will be based on the primary link B

## Slide 6: Mixed Synchronous & Asynchronous Configuration Example
AP
STA1
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Link A
PHY1
PHY2
PHY1
PHY2
STA2
MAC
LMAC1
LMAC2
PHY1
PHY2
Asynchronous
Synchronous
Primary link B
LMAC3
PHY3
LMAC4
PHY4
Link B
Link C
Link D
Asynchronous between Link A,B,D
Link B,C in the same Synchronous group. Link B is the Primary link, Link C is secondary link
LMAC3
PHY3
Primary link
Synchronous group

## Slide 7: Mixed Synchronous & Asynchronous Connection
Multiple asynchronous links can form a virtual synchronous group and connect to a synchronous group. E.g., a multiple links device having asynchronous links A and B can connect to
  Devices with asynchronous links A and B (pure asynchronous connection)
  Devices with a synchronous group where primary link is link A and secondary link is link B (mixed connection)
  Devices with a synchronous group where primary link is link B and secondary link is link A (mixed connection)

## Slide 8: Mixed Synchronous & Asynchronous Connection Example (1/)
AP
STA1
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
STA2
MAC
LMAC1
LMAC2
PHY1
PHY2
Asynchronous
Asynchronous
Synchronous
Primary link ch1
The transmission between AP and STA2 is asynchronous
The transmission between AP and STA1 is synchronous
AP cannot use ch2 only to send data to STA1
AP can use ch1 only to send data to STA1. If the channel is also idle in ch2, then AP can use ch1+ch2 to send data to STA1
Primary link
Synchronous group

## Slide 9: Mixed Synchronous & Asynchronous Connection Example (2/)
AP
STA1
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
STA2
MAC
LMAC1
LMAC2
PHY1
PHY2
Asynchronous
Synchronous
Primary link ch1
The transmission between AP and STA1 are synchronous
AP cannot use ch2 only to send data to STA1
AP can use ch1 only to send data to STA1. If the channel is also idle in ch2, then AP can use ch1+ch2 to send data to STA1
Primary link
Synchronous group
Synchronous
Primary link ch2
The transmission between AP and STA2 are synchronous
AP cannot use ch1 only to send data to STA2
AP can use ch2 only to send data to STA2. If the channel is also idle in ch1, then AP can use ch2+ch1 to send data to STA2

## Slide 10: Other Asynchronous/Synchronous Mixed Multiple Links Coexistence Examples (1/)
AP
STA1
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch1
PHY1
PHY2
PHY1
PHY2
STA2
MAC
LMAC1
LMAC2
PHY1
PHY2
Synchronous
Primary link ch2
LMAC3
PHY3
LMAC4
PHY4
Ch2
Ch3
Ch4
LMAC3
PHY3
Primary link
Synchronous group
Asynchronous
Synchronous
Primary link ch4

## Slide 11: Other Asynchronous/Synchronous Mixed Multiple Links Coexistence Examples (2/)
AP
STA1
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch1
PHY1
PHY2
PHY1
PHY2
STA2
MAC
LMAC1
LMAC2
PHY1
PHY2
Synchronous
Primary link ch2
LMAC3
PHY3
LMAC4
PHY4
Ch2
Ch3
Ch4
LMAC3
PHY3
Primary link
Synchronous group
Asynchronous
Asynchronous

## Slide 12: Conclusion
Asynchronous multiple links system can have better performance but need good isolation between links
Synchronous multiple links system can avoid the requirement of isolation between links, although the performance is worse
Besides pure synchronous/asynchronous configuration/connection, we may also need to support mixed configuration/connection
We propose a mixed multiple links system that can support mixed configuration and mixed connection

## Slide 13: References
[1] 11-19/760r1 Multi-band Opinion
[2] 11-19/1116r1 Channel Access in Multi-band operation
[3] 11-19/1144r1 Channel Access for Multi-link Operation
[4] 11-19/0821r0 Multiple Band Operation Discussion

## Slide 14: Straw Poll #1
Do you agree to support mixed synchronous & asynchronous configuration in TGbe multiple links operation
Y:
N:
A:

## Slide 15: Straw Poll #2
Do you agree to support mixed synchronous & asynchronous connection in TGbe multiple links operation
Y:
N:
A:

## Slide 16: Backup Slides

## Slide 17: Fairness in Asynchronous/Synchronous Mixed Mode
Definition:
  Primary link data: the data that can be sent out without further constraint on other link
  Secondary link data: the data that can be sent out together with its corresponding primary link data
  Asynchronous transmission data can be treated as primary link data
For a synchronous transmission, when its primary link data get the TXOP, if there is other primary link data in front of its secondary link queuing list, the transmission in secondary link is not allowed

## Slide 18: Mixed Multiple Links Fairness Example(1/)
AP
STA1
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
STA2
MAC
LMAC1
LMAC2
PHY1
PHY2
Asynchronous
Asynchronous
Synchronous
Primary link ch1
MAC
LMAC1
PHY1
Primary link
Synchronous group
STA3

## Slide 19: Mixed Multiple Links Fairness Example(2/)
A1
A2
B1
B2
Channel 1 queuing list
A1
A2
B1(S)
Channel 2 queuing list
In this example, ch1 and ch2 has transmit opportunity in a round robin manner. The transmission sequence is as below:
A1 in ch1
A2 in ch2
B1 in ch1 and B2 in ch2 synchronously (ch2 is also idle)
...
...
Dispatch
...
Descriptors
A1(1,2)
A2(1,2)
C1(2)
B1(P1S2)
B2(P1S2)
B2(S)
C1
Asynchronous
Synchronous
Ks(i,j)
Destination
sequence
Assigned links
When ch2 is also idle, B2 can be sent with B1

## Slide 20: Mixed Multiple Links Fairness Example(3/)
A1
A2
B1
B2
Channel 1 queuing list
A1
A2
C1
C2
B1(S)
Channel 2 queuing list
In this example, ch1 and ch2 has transmit opportunity in a round robin manner. The transmission sequence is as below:
A1 in ch1
A2 in ch2
B1 in ch1 (in ch2 queuing list, C1 and C2 are in front of B1 and B2, no secondary transmission to B)
C1 in ch2
...
...
Dispatch
...
Descriptors
A1(1,2)
A2(1,2)
C1(2)
C2(2)
B1(P1S2)
B2(P1S2)
B2(S)
Asynchronous
Synchronous
Single link
Ks(i,j)
Destination
sequence
Assigned links
B2 cannot be sent with B1 since there are C1, C2 in front of it