## Slide 1: TESLA Improvement
Date: 2019-11-11
Authors:

## Slide 2: Abstract
This presentation describes an improvement of TESLA based frame authentication that is proposed in 11-19/451r5.

## Slide 3: Key Disclosure
The transmitter discloses the keys after d * Tk (d >= 2)
Receivers have to buffer the frames until the key disclosed.
time
TK
K’N-1
TK
K’N-2
TK
K’N-3
TK
K’N-4
TK
K’N-5
TK
K’0
KN-1
KN-2
KN-3
Disclosed Key
(d = 2)
K2
Authenticator Key
Data
Auth (K’N-1)
Data
Auth (K’N-2)
Data
Auth (K’N-3)
KN-1
Data
Auth (K’N-4)
KN-2
Data
Auth (K’N-4)
KN-3
Data
Auth (K’0)
K2

## Slide 4: 11-19/1675r0: Attack scenario: Injection of fake Data frames
Injection of false eBCS Data frames (i.e., frames carrying false authenticator information) can easily exhaust the receiver buffer
  For example:
    an attacker injects many eBCS Data frames that have the same sequence # and Key (both of which are not confidential info) but different data and authenticator
    By nature of the protocol, the receiver is required to store all frames as it doesn’t know which one is the correct one until the corresponding verification key disclosed later.
    In other words, there would be one correct data frame out of 100 frames, but the STA can only tell which one is correct after getting the key.

## Slide 5: EMSS (Efficient Multi-chained Stream Signature)
The issue is caused by receiver side buffering.
To solve the issue, buffer packets in transmitter side.
Data frames include additional hash value of the data that will be sent later.
No one-way key chains are required.
It is no longer TESLA.
Data
(D1)
Hash
(D3)
Data2
(D2)
Data3
(D3)
Data4
(D4)
Data5
(D5)
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Data6
(D6)
Frame 6
Data7
(D7)
Frame 7
Hash
(D4)
Hash
(D5)
Hash
(D6)
Hash
(D7)
Hash
(D8)
Hash
(D9)
Hash
(D1)
Hash
(D2)
eBCS Info
Time

## Slide 6: Improve Packet Loss Tolerance 1
A Data frame can contain multiple hash values.
Hash size: 32 octets (SHA256, SHA3-256)
In case of lost Frame 3, Frame 5 can be authenticated from Hash(D5) in Frame 1.
Data
(D1)
Hash
(D3)
Data2
(D2)
Data3
(D3)
Data4
(D4)
Data5
(D5)
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Data6
(D6)
Frame 6
Data7
(D7)
Frame 7
Hash
(D4)
Hash
(D5)
Hash
(D6)
Hash
(D7)
Hash
(D8)
Hash
(D9)
Hash
(D5)
Hash
(D6)
Hash
(D7)
Hash
(D8)
Hash
(D9)
Hash
(D10)
Hash
(D11)
Hash
(D1)
Hash
(D2)
eBCS Info

## Slide 7: Improve Packet Loss Tolerance 2
A Data frame contains a hash value for a specific frame and a hash value for some specific frames.
This is more efficient than the previous slide.
Hash(Dm,n) = Hash(Hash(Dm)||Hash(Dn)) (Merkle Hash Tree)
In case of lost Frame 3, Frame 5 can be authenticated.
  H4: from Frame 2 or Frame 4
  H5: calculate from Frame5
  H4,5: Calculate from H4 and H5
  If H4,5 == Hash(D4,5) in Frame1, Fram5 is correct.
Data
(D1)
Hash
(D3)
Data2
(D2)
Data3
(D3)
Data4
(D4)
Data5
(D5)
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Data6
(D6)
Frame 6
Data7
(D7)
Frame 7
Hash
(D4)
Hash
(D5)
Hash
(D6)
Hash
(D7)
Hash
(D8)
Hash
(D9)
Hash
(D4,5)
Hash
(D5,6)
Hash
(D6,7)
Hash
(D7,8)
Hash
(D8,9)
Hash
(D9,10)
Hash
(D10,11)
Hash
(D1)
Hash
(D2)
eBCS Info

## Slide 8: References
“Efficient Authentication and Signing of Multicast Streams over Lossy Channels”, Adrian Perrig (UC Berkeley), et. al. https://netsec.ethz.ch/publications/papers/stream.pdf