## Slide 1: Multi-link setup follow up
Date: 2019-11-5
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Daniel F Bravo |  |  |  | 
Notes: September 2012

## Slide 2: Background
Multi-link framework has been proposed below [1]
Multi-link setup also has been discussed [2]
We provide follow up to clarify the procedure
AP1
AP2
AP3
STA1
STA2
STA3
AP MLLE
Non-AP MLLE
AP1
Non-AP STA1
Request frame for multi-link setup
Response frame for multi-link setup

## Slide 3: Detailed Multi-link setup procedure
Any STA of an non-AP MLLE may initiate the multi-link setup in a link with the request frame including the capability and parameters of all the requested links
The AP that receives the request frame respond with the response frame including the capability and parameters of all the links that are setup
  AP MLLE uses implementation specific criteria to decide which requested links are accepted for multi-link setup
After the multi-link setup, AP MLLE serves as the interface to the DS for the non-AP MLLE

## Slide 4: Multi-link setup and association
Association is a term used in the current spec for setup between one AP and one non-AP STA
Multi-link setup extends the concept for setup between on AP MLLE and one non-AP MLLE
  Multi-link setup can be called multi-link association if we reuse association request/response frame. Multi-link setup needs to be called a different name from association if we use a new management frame for request/response
We continue to use multi-link setup until the container for request/response frame is decided

## Slide 5: Need for additional mechanism to teardown the setup
For the association between an AP and a non-AP STA, we have disassociation to teardown the setup
For the multi-link setup between an AP MLLE and an non-AP MLLE, we expect that Multi-link teardown is also required for a non-AP MLLE or AP MLLE to teardown the setup links

## Slide 6: Container for Multi-link teardown
We expect that
  if association request/response is reused for multi-link setup, then disassociation can also be reused for multi-link teardown
  if new request/response is designed for multi-link setup, then new teardown frame is designed for multi-link teardown
We think that the frames to do multi-link setup and multi-link teardown should be discussed together

## Slide 7: Conclusion
We provide the detailed procedure for multi-link setup
  Non-AP MLLE requests the links to be setup
  AP MLLE accepts one or more links among the links requested by non-AP MLLE for setup
  The link selection above should be implementation specific
We discuss the need for multi-link teardown
We discuss the container for multi-link setup and multi-link teardown
  Reuse association request/response and disassociation frame or
  Have new management frames for the purpose

## Slide 8: Straw poll #1
Do you support 11be shall define a mechanism to teardown an existing multi-link setup?

## Slide 9: Reference
[1] 19/0822r4 Extremely efficient multi-band operation
[2] 19/0773r7 Multi-link operation framework