## Slide 1: Latency enhancement in multi-link
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Taewon Song |  |  |  | taewon.song@lge.co
Sungjin Park |  |  |  | allean.park@lge.com

## Slide 2: Introduction
We have presented how to enhance latency performance in 11be [1]
  New queue for latency, worst case handling and OFDMA enhancement have been addressed
There were submissions which have discussed latency performance in multi-link [2][3][4][5]
We will address detail operations for enhancing latency performance and discuss how we deal with it from the multi-link view

## Slide 3: Latency traffic in EDCA
In order to improve latency performance, it may be basically necessary to give priority to the specific traffic
  IEEE 802.11 have defined EDCA for supporting prioritization
If the traffic has low latency requirement, it would be transmitted by AC_VO or AC_VI
However, the low latency traffic cannot use the AC_VO or AC_VI exclusively, because there will be other non latency traffic on these ACs
So it is difficult to manage priority for the low latency traffic individually by current EDCA

## Slide 4: Low Latency Queue
As mentioned in [1], intra-AC prioritization (IAP) which has been defined in 11aa can be used for low latency
  A_VO or A_VI is assigned only
  for low latency traffic
  A_VO or A_VI which is assigned
  for low latency traffic has to share
  EDCAF with VI or VI, respectively
  The AP cannot assign a specific
  EDCAF for low latency traffic
Low Latency Traffic Only

## Slide 5: Low Latency Queue
We propose that defining additional EDCAF for low latency
The low latency queue/EDCAF may have following characteristics
  Uses different EDCA parameter set
  Temporarily be activated/terminated
  Only be buffered by low latency traffic
  Supports worst case operation
  Detail is TBD

## Slide 6: Low Latency Queue in multi-link
As shown in [2], multi-link has capability to enhance latency naturally because the STA may have more TXOP
However, if we define EDCAF for low latency queues, we may have following additional advantages in multi-link
  AP can manage priority of latency traffic more detail regarding current load of each link
  AP can assign a specific role to the a link
    If overheads such as BSR/BQR report are transmitted in the other link, the latency performance of the link can be improved because the STA can transmit UL latency data only in the link

## Slide 7: Low Latency Queue in multi-link: Example
 | Link 1 | Link 2
Link load | Low | High
Traffic: low latency
EDCAF of LL (AIFSn = 2, CWmin = 7, CWmax = 15)
STA 1
Traffic: extremely low latency | Traffic: low latency
EDCAF of LL (AIFSn = 2, CWmin = 3, CWmax = 7) | EDCAF of LL (AIFSn = 2, CWmin = 3, CWmax = 7)
STA 2 | 

## Slide 8: Low Latency Queue in multi-link: Example
 | Link 1 | Link 2
Link load | Low | High
Traffic: AC_VO (non-latency) | Traffic: extremely low latency | Traffic: management of low latency
EDCAF of VO (AIFSn = 2, CWmin = 7, CWmax = 15) | EDCAF of LL (AIFSn = 2, CWmin = 3, CWmax = 7) | EDCAF of LL (AIFSn = 2, CWmin = 3, CWmax = 7)
STA 2 |  | 

## Slide 9: Summary
We have addressed how to give priority to the low latency traffic over other traffic via additional EDCAF and queue
Also we have discussed additional advantages in multi-link when we define EDCAF for low latency queues

## Slide 10: Straw poll 1
Do you agree to add the following into the TGbe SFD?
  TGbe shall define a EDCAF and corresponding AC/Queue for traffic requiring low latency

## Slide 11: Straw poll 2
Do you agree to add the following into the TGbe SFD?
  TGbe shall define a EDCAF and corresponding AC/Queue for traffic requiring low latency
    EDCAF for traffic requiring low latency can operate independently in multi-links

## Slide 12: Reference
[1] 11-19-1524-00-00be-latency-enhancement-for-eht
[2] 11-19-1081-01-00be-multi-link-aggregation-gain-analysis-latency
[3] 11-19-1615-00-00be-multi-band-multi-channel-operation-for-low-latency-and-jitter
[4] 11-19-1613-00-00be-multi-link-txop-sharing-for-delay-reduction
[5] 11-19-1622-00-00be-use-auto-repetition-in-low-latency-queue