## Slide 1: WLAN based radars in the 60GHz band
Date: 2019-11-3
Authors:

## Slide 2: Abstract
In this presentation we show how 11ad/11ay devices can be used for radar application with minimal HW changes. We also show how can radar (position/speed) information can be improved if device collaborate.

## Slide 3: How can 11ad device be used for radar application?
In a nutshell: transmit a PPDU (possibly in a specific direction), receive the reflection from target and measure the time difference between the transmission and received signal to estimate the distance to the target and also use the directivity of the antenna to estimate the direction from which the reflections arrive.
  Target speed towards the 11ad device can be estimated by Doppler effect
Why is the 60GHz band and DMG good for (short range) radar application?
  Large bandwidth enables high range accuracy
  Antenna arrays used by DMG devices enable direction estimation.
  Disadvantages:
    Oxygen Attenuation prevents long range application -
    Large arrays needed for long range applications cause slow scanning
    In short ranges, the reflected signal arrives before the end Tx – need to deal with that

## Slide 4: DMG system typical Architecture
A DMG system will typically be composed of:
A Baseband chip
  Digital part to perform MAC and digital PHY functions
    Preparation of signal transmission
    Detection and reception of packets, equalization error correction
  Analog part
    For Tx
      DAC, Mixer to IF, amplifier
    For Rx
      Amplifier, Mixer from IF to baseband, ADC
An RF chip
  IF to RF mixer
  Multiple TX chains containing amplifiers, phase shifter and PA
  Multiple RX chains containing LNA, phase shifter and amplifiers (some may be shared with TX)
Antenna (array)

## Slide 5: DMG system typical Architecture (cont.)
In a typical system the antenna (array) is lumped with the RF chip on the same board.
  Very high attenuation of RF cables
It is possible to lump the RF and baseband chip
  Better performance
  However, in many application a location (in the system) which is good for an antenna is not good for the baseband and vise versa.
In some systems, several antennas (arrays) and RF chips may be connected to the same baseband chip
  Provide spatial diversity
  Enable simultaneous TX and RX - necessary for radar applications
    An RF chip cannot receive and transmit at the same time due to leakage from the transmit chain to the receive chain

## Slide 6: Typical DMG system block diagram

## Slide 7: What do we need for a radar system

## Slide 8: How can the DMG waveform be used for radar
The DMG waveform has a Channel Estimate Field (CEF) that is composed of 9 Golay sequences of length 128.
It enables accurate and efficient channel estimate with zero auto-correlation zone of 128 chips (10.9 meters).
  It is possible to extend the range with delayed correlation with the CEF
The channel estimate (CIR) contains the reflections
  It also contains the leakage, the high gain of the CEF enables recovery of the reflection from under the leakage
TRN fields may also be used for CIR estimations – if transmitted in different directions can be use for radar scan within a single PPDU

## Slide 9: What accuracy can we expect from a DMG based radar?
A Chip rate of 1760MHz implies 8.5cm range resolution.
  Using interpolation or super-resolution methods the resolution can be reduced to ~1cm.
A Uniform Linear Array with N elements λ/2 separation has a beam width of 70°/N. With N=16 this amounts to 4.5°.
  Accuracy may be increased by interpolation or more complex methods.
Doppler Accuracy – accurate frequency estimation require (very) long sequence:
  Human motion of 1m/s cause a Doppler shift of 2Hz at 60GHz – an FFT on 0.5 second is needed for that accuracy
  Doppler is estimated using multiple packets.
  Movement is estimated by comparing the phase of the same reflection in CIR estimates from different packets

## Slide 10: How can we use the signal transmitted by one DMG STA to perform radar function in another STA?
The Tx STA transmits a PPDU in a direction known to the Rx STA.
The Rx STA receives the direction signal and synchronizes to it.
The Rx STA receives the reflection from the target, measures the time difference from the direct signal and the direction
The RX STA now determines the target direction and distance
Bi-STATIC Radar

## Slide 11: Can this work without spec changes?
Yes, if:
  The RX STA knows the location TX STA
    We already have methods to share this information, adding also TX direction will increase accuracy
  The RX STA received both the direct signal and the reflection (needed to estimated the differential time of arrival)
    This works if RX STA was in omni mode, however, this reduces the effective range.
What can we add to spec to make it work better
  Define how location and TX direction information is shared
  Methods for the RX STA to send information on reflections to the TX STA
    Collaborative radar – increases accuracy
    Can be increased to many stations
  Increase probability that both reflection and direct signal are received

## Slide 12: What is the advantage of using multiple STAs for measurement
Increased accuracy:
  Target may reflect better to some directions
  Target may be in a direction towards one STA array in which it has higher angular resolution
    Using several STAs with different orientation, increases the probability of a good viewing angle to the target.
Facilitates radar functionality in devices that cannot transmit and receive simultaneously

## Slide 13: Summary
We showed how we can use a DMG system using DMG PPDUs to perform radar functions.
  Measure range, direction, speed.
We showed how DMG STA can collaborate on radar measurements.

## Slide 14: References
[1] 11-19-1551-01-wng-Wi-Fi Sensing in 60GHz band
[2] Grossi, Emanuele, Marco Lops, Luca Venturino, and Alessio Zappone. "Opportunistic radar in IEEE 802.11 ad networks." IEEE Transactions on Signal Processing 66, no. 9 (2018): 2441-2454.
[3] Kumari, Preeti, Junil Choi, Nuria González-Prelcic, and Robert W. Heath. "IEEE 802.11 ad-based radar: An approach to joint vehicular communication-radar system." IEEE Transactions on Vehicular Technology 67, no. 4 (2017): 3012-3027.