## Slide 1: 802.1AX Overview
Date: 2019-11-04
Authors:

## Slide 2: Abstract
This submission provides a short overview of 802.1AX specification.

## Slide 3: Link Aggregation Goals and Objectives [1]
IEEE 802.1AX includes a long list describing the benefits of link aggregation – below is a subset of those benefits that are also mentioned in [2]
  Increased bandwidth—The capacity of multiple links is combined into one logical link.
  Linearly incremental bandwidth—Bandwidth can be increased in unit multiples as opposed to the order-of-magnitude increase available through Physical Layer technology options (10 Mb/s, 100 Mb/s, 1000 Mb/s, etc.).
  Increased availability—The failure or replacement of a single link within a LAG need not cause failure from the perspective of an Aggregator Client.
  Load sharing—Aggregator Client traffic may be distributed across multiple links.
  Automatic configuration—In the absence of manual overrides, an appropriate set of LAGs is automatically configured, and individual links are allocated to those groups. If a set of links can aggregate, they will aggregate.
  Rapid configuration and reconfiguration—In the event of changes in physical connectivity, Link Aggregation will quickly converge to a new configuration, typically on the order of milliseconds for link down events and 1 s or less for link up events.

## Slide 4: Link Aggregation and IEEE 802 Architecture [2]

## Slide 5: Relationship to MAC Architecture (Figure 10.1)

## Slide 6: Link Aggregation Sublayer Block Diagram [2]
a) Frame Distribution. This block is responsible for taking frames submitted by the Aggregator Client
and submitting them for transmission on the appropriate Aggregation Port, based on a frame
distribution algorithm employed by the Frame Distributor. Frame Distribution includes a Frame
Distributor and an optional Marker Generator/Receiver used for the Marker protocol. (See 6.2.4,
6.2.5, and 6.5.)
b) Frame Collection. This block is responsible for passing frames received from the various
Aggregation Ports to the Aggregator Client. Frame Collection includes a Frame Collector and a
Marker Responder, used for the Marker protocol. (See 6.2.3, 6.2.6, and 6.5.)
c) Aggregator Parser/Multiplexers. On transmit, these blocks simply pass frame transmission requests
from the Frame Distributor, Marker Generator, and/or Marker Responder to the appropriate
Aggregation Port. On receive, these blocks distinguish among Marker Request, Marker Response,
and MAC Protocol Data Units (MPDUs), and pass each to the appropriate entity (Marker
Responder, Marker Receiver, and Frame Collector, respectively).
d) Aggregator. The combination of Frame Distribution and Frame Collection, along with the
Aggregator Parser/Multiplexers, is referred to as the Aggregator.
e) Aggregation Control. This block is responsible for the configuration and control of Link
Aggregation. It incorporates a Link Aggregation Control Protocol (LACP) that can be used for
automatic communication of aggregation capabilities between Systems and automatic configuration
of Link Aggregation.
f) Control Parser/Multiplexers. On transmit, these blocks simply pass frame transmission requests
from the Aggregator and Control entities to the appropriate Aggregation Port. On receive, these
blocks distinguish Link Aggregation Control PDUs from other frames, passing the LACPDUs to the
appropriate sublayer entity, and all other frames to the Aggregator
Aggregator
Parser/Multiplexer
Aggregator
Parser/Multiplexer
Aggregator
Parser/Multiplexer
Control
Parser/Multiplexer
Control
Parser/Multiplexer
Control
Parser/Multiplexer
Frame Distribution
Frame Collection
Frame
Distributor
Marker Generator/
Receiver (optional)
Frame
Collector
Marker
Responder
MAC
MAC
MAC
Link Aggregation
Control
Link Aggregation
Control Protocol
Aggregator Client
Aggregation
Control
Link aggregation
Sublayer
Aggregator
Marker
Frames
Aggregator
Client
Frames

## Slide 7: Principles of Link Aggregation
An Aggregator Client communicates with a set of Aggregation Ports through an Aggregator, which presents a standard ISS interface to the Aggregator Client. The Aggregator binds to one or more Aggregation Ports within a System.
It is the responsibility of the Aggregator to distribute frame transmissions from the Aggregator Client to the various Aggregation Ports, and to collect received frames from the Aggregation Ports and pass them to the Aggregator Client transparently.
A System may contain multiple Aggregators, serving multiple Aggregator Clients. A given Aggregation Port will bind to (at most) a single Aggregator at any time. An Aggregator Client is served by a single Aggregator at a time.
The binding of Aggregation Ports to Aggregators within a System is managed by the Link Aggregation Control function for that System, which is responsible for determining which links may be aggregated, aggregating them, binding the Aggregation Ports within the System to an appropriate Aggregator, and monitoring conditions to determine when a change in aggregation is needed.
Frame ordering has to be maintained for certain sequences of frame exchanges between Aggregator Clients (known as conversations, see Clause 3). The Frame Distributor ensures that all frames of a given conversation are passed to a single Aggregation Port. For any given Aggregation Port, the Frame Collector is required to pass frames to the Aggregator Client in the order that they are received from that Aggregation Port. The Frame Collector is otherwise free to select frames received from the Aggregation Ports in any order. Since there are no means for frames to be misordered on a single link, this guarantees that frame ordering is maintained for any conversation.
g
This standard does not impose any particular distribution algorithm on the Frame Distributor. Whatever algorithm is used should be appropriate for the Aggregator Client being supported.
Each Aggregation Port is assigned a MAC address, unique over the LAG and the IEEE 802.1Q Bridged LAN (if any) to which the LAG is connected. This MAC address is used as the source address (SA) for frame exchanges that are initiated by entities within the Link Aggregation sublayer itself (i.e., LACP and Marker protocol exchanges). NOTE—The LACP and Marker protocols use a multicast destination address (DA) for all exchanges, and do not impose any requirement for an Aggregation Port to recognize more than one unicast address on received frames.
Each Aggregator is assigned a MAC address, unique over the LAG and the IEEE 802.1Q Bridged LAN (if any) to which the LAG is connected; this address is used as the MAC address of the aggregation from the perspective of the Aggregator Client, both as a SA for transmitted frames and as the destination address (DA) for received frames. The MAC address of the Aggregator may be one of the MAC addresses of an Aggregation Port in the associated LAG (see 6.2.11).
conversation: A set of frames transmitted from one end station to another, where all of the frames form an ordered sequence, and where the communicating end stations require the ordering to be maintained among the set of frames exchanged.

## Slide 8: Link Aggregation Proposals in 802.11be [1,3]
Proposals discussed in 11be introduces Multi-Link Logical Entity
  Multi-link logical entity: A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
    NOTE –A Multi-link logical entity allows STAs affiliated with the multi-link logical entity to have the same MAC address
    NOTE – The exact name can be changed
MLLE construct seems to be equivalent
to 802.1AX Aggregator (minus
the many details).
STA construct was used to substantiate the
PHY/MAC layer

## Slide 9: Example of ML Architecture
Architecture
Multi-link
High MAC
Distributor
Collector
Controller
Low
MAC 1
Low
MAC 2
Low
MAC n
DS
Control
Parser/Multiplexer
Control
Parser/Multiplexer
Control
Parser/Multiplexer
…

## Slide 10: Explain of the architecture
Distributor. This block is responsible for taking frames comes from DS and submitting them for transmission on the appropriate low MAC. For flow level aggregation, the submission is based on the negotiation results between the two ML capable Device. For packet level aggregation, the submission is based on a frame distribution algorithm which is out of scope of 802.11 standard.
Collector. This block is responsible for passing frames received from the various low MACs to the DS.
Controller. This block is responsible for generate and process management frames.
Control Parser/Multiplexers. On transmit, these blocks simply pass frame transmission requests from the Distributor and Controller to the appropriate low MAC. On receive, these blocks distinguish Management frames from data frames, passing the management frames to the controller, and data frames to the Collector.
Notes: Solution 4有内容现有技术

## Slide 11: Conclusion
802.1AX provides a comprehensive description of the Link Aggregation sublayer.
802.1AX link aggregation sublayer seems to fit well with proposals discussed.
The recommendation is to make use of as many of 802.1AX components for modeling the 802.11be multi-link related work.

## Slide 12: References
https://mentor.ieee.org/802.11/dcn/19/11-19-0823-02-00be-multi-link-aggregation.pptx
IEEE 802.1AX-2014 IEEE Standard for Local and metropolitan area networks -- Link Aggregation - https://standards.ieee.org/standard/802_1AX-2014.html
https://mentor.ieee.org/802.11/dcn/19/11-19-0773-07-00be-multi-link-operation-framework.pptx

## Slide 13: SP
Do you agree to make use of relevant 802.1AX components for 11be MLA discussion?