## Slide 1: A-MPDU and BA
Date: 2019-11-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | Marvell |  |  | 

## Slide 2: Recap: Multiple A-MPDUs in HE MU PPDU
A multi-link AP/STA entity has multiple STA/APs.
A-MPDUs from one TID can be transmitted in multiple links.
Link 2
A-MPDU 1 of TID1
A-MPDU 2 of TID1
BA 2
BA 1
Link 1
Multi-link AP entity
MAC with Addr11
MAC with Addr21
Common MAC
Link1
Link2
Multi-link STA entity
MAC with Addr18
MAC with Addr28
Common MAC
Link1
Link2
A-MPDU1
A-MPDU2

## Slide 3: Recap: BA Agreement Negotiation and BA Architecture
ADDBA Request
ADDBA Response
Block Ack Parameter Set
WinSizeO <= Buffer Size in ADDBA Response
WinSizeR = Buffer Size in ADDBA Response
WinSizeB = Buffer Size in ADDBA Response

## Slide 4: BA Agreement Negotiation for Multi-link Operation
ADDBA Request
ADDBA Response
Block Ack Parameter Set
Single BA negotiation is applied to a TID between the initiator of the BA agreement and recipient for multiple links.

## Slide 5: Multi-link AP/STA Entity Architecture: Reuse the Current Sequence Number
Multi-link AP entity
MAC with Addr11
MAC with Addr21
Common MAC
Link1
Link2
Multi-link STA entity
MAC with Addr19
MAC with Addr29
Common MAC
Link1
Link2
A-MPDU1
A-MPDU2
(Re)Tx buffer (WinStartO, WinEndO, WinSizeO) shared by AP11, AP21
link1
link2
link1
link2
Scoreboard context (WinStartR, WinEndR, WinSizeR) shared by STA19, STA29
Reorder buffer (WinStartB, WinEndB, WinSizeB) shared by STA19, STA29
STA19’s Scoreboard context (WinStartR, WinEndR, WinSizeR)
link1
link2
link1
link2
AP11’s (Re)Tx buffer (WinStartO, WinEndO, WinSizeO)
AP21’s (Re)Tx buffer (WinStartO, WinEndO, WinSizeO)
A-MPDU2
A-MPDU1
A-MPDU2
STA29’s Scoreboard context (WinStartR, WinEndR, WinSizeR)
Reorder buffer (WinStartB, WinEndB, WinSizeB) shared by STA19, STA29
A-MPDU1
Reordering buffer per MPDUs
A-MPDU1 and A-MPDU2 for the same TID share the same Sequence Number space.

## Slide 6: BAR and BA
BA in each link is used to acknowledge the A-MPDU in the link.
The reception of BAR:
  The scoreboard context can be updated per the current rules since each link has separate scoreboard context.
  The reorder buffer should have different rules:
    For block ack agreement that is not a protected block agreement:
      Treat BAR as if in protected block ack agreement, or
      Redefine BAR: the initiator of BAR can indicate whether it wants the recipient of BAR to shift the WinStartB or not.
        If the initiator uses a BAR to shift the recipient’s WinStartB, the initiator shall guarantee that all the MSDUs/A-MSDUs whose Sequence Number values are less than the value in Block Ack Start Sequence Control field of the BAR will not be transmitted after the BAR.
    For protected block ack agreement, the current rules can be used, i.e. BAR is used to solicit BA only, the robust ADDBA Request is used to shift the WinStartB.
    The figure in the following slide gives the reason for such operation.

## Slide 7: BAR and BA (Cont’d)
STA19’s Scoreboard context (WinStartR, WinEndR, WinSizeR)
link1
link2
link1
link2
AP11’s (Re)Tx buffer (WinStartO, WinEndO, WinSizeO)
AP21’s (Re)Tx buffer (WinStartO, WinEndO, WinSizeO)
A-MPDU1
A-MPDU2
STA29’s Scoreboard context (WinStartR, WinEndR, WinSizeR)
Reorder buffer (WinStartB, WinEndB, WinSizeB) shared by STA19, STA29
Link1
Link2
A-MPDU1 (Seq 1 to 31, 60, 61)
A-MPDU1 (Seq 32 to 59)
BA
BA
BA
BAR
Adjust WinStartB
The retransmission of missed frames in A-MPDU1 is not helpful. The recipient will discard the retransmitted MPDUs in A-MPDU1 because of the adjusted WinStartB.
Some frames in A-MPDU1 are not received correctly.
BA is not received correctly.

## Slide 8: BA Creation
A Block Ack being transmitted in one link can acknowledge the A-MPDU being transmitted in another link in addition to acknowledge the A-MPDU of the link.
Link 2
AP MLLE’s A-MPDU 1 with TID1 for STA MLLE1
AP MLLE’s A-MPDU 2 with TID1 for STA MLLE1
BA
Link 1
BA acknowledges the frames in A-MPDU2 and optionally acknowledge the frames in A-MPDU1.

## Slide 9: Straw Poll 1
Do you support that
  Two MLLEs establish a single block ack agreement for a TID through one block ack negotiation.
  The established block Ack agreement allows the QoS Data frames of the TID, aggregated within the A-MPDUs, to be exchanged between the two MLLEs on any link to which the TID is mapped.
  The QoS Data frames of the TID transmitted by a MLLE to another MLLE share the same Sequence Number space.

## Slide 10: Straw Poll 2
Do you support that
  for each block ack agreement, there exists one receive reordering buffer based on MPDUs in the MLLE which is the recipient of the QoS Data frames for that block ack agreement.
  The receive reordering buffer operation is based on the Sequence Number space that is shared between the two MLLEs.

## Slide 11: Straw Poll 3
Do you support that
  The receive status of QoS Data frames of a TID received on a link shall be signaled on the same link and may be signaled on other link(s) where the TID is mapped?