## Slide 1: Multiple Link Power Save
Date: 2019-11-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | Marvell |  |  | 

## Slide 2: Recap: 11baseline Power Save
Operation mode change:
  NSS, BW change from STA side and AP side.
  The following power save feature works with the available BW announced by operating mode change.
Power save at STA.
  Power save mode,
  Power save state when working in Power Save Mode
SM (Spatial Multiplexing) power save.
…

## Slide 3: Recap: Multi-link Power Save
An AP/STA MLLE includes multiple APs/STAs that affiliated with it respectively.
For a MLLE each STA on an enabled link maintains its own power save mode/state.
An AP of an AP MLLE may transmit on a link a frame that carries an indication of individually addressed frames buffered for transmission on other link(s)
  An non-AP MLLE needs to be aware on which link(s) the AP MLLE provides the indication
An AP of an AP MLLE may be restricted to indicate individually addressed frames buffered for transmission on a link within frame only transmitted on that link.
This presentation discusses the power save mode/state change.

## Slide 4: Method 1: Multi-Link Power Save State
When multi-link STA entity is in Active mode in link1 and is in power save mode in link2, the multi-link AP entity can request multi-link STA entity in link2 to be in Awake state through the unicast message in link1, e.g. HE Control field.
STA awake notification:
  Option 1—explicit awake: after receiving awake request, the multi-link STA entity notifies power save STA’s awake through PS-Poll, QoS Null etc. in link2 or link1 (HE Control could be used when link2’s awake is notified in link1’s frame exchange).
  Option 2—implicit awake: multi-link STA entity announces the awake switch time through management frame, e.g. in Association Response frame. After the announced time period of the received acknowledgement of awake request, the request multi-link STA entity’s link becomes awake.
  Option 3 — AP’s request carries the target time.
With this method, a STA MLLE can skip the Beacons in a link while monitoring another link.
Link1 (master link)
Link2 (slave link)
Multi-link AP entity1
MAC Addr11
Common MAC
Link1
MAC Addr21
Link2
MAC Addr19
Common MAC
Link1
MAC Addr29
Link2
Multi-link STA entity
Power Save mode
Active mode
Beacon
Beacon
Beacon
Beacon
QoS Null
Ack
Request to awake addr29
A-MPDU1
A-MPDU2
MAC Addr29 is awake.
Frames for Addr29 is coming or high load traffic is coming.

## Slide 5: Method 2: Multi-Link Power Save State
TIM is used to notify the existing buffered frames in multi-link AP entity for link in Power Save mode.
STA awake notification:
  Assume link2’s STA in multi-link STA entity is in Power Save mode. the multi-link STA entity notifies power save STA’s awake through PS-Poll, QoS Null etc. in link2 or link1 (HE Control could be used when link2’s awake is notified in link1’s frame exchange).
Link1 (master link)
Link2 (slave link)
Multi-link AP entity1
MAC Addr11
Common MAC
Link1
MAC Addr21
Link2
MAC Addr19
Common MAC
Link1
MAC Addr29
Link2
Multi-link STA entity
Power Save mode
Active mode
Beacon
Beacon
Beacon
Beacon
QoS Null
Ack
Buffered frames for Addr29 (the indication can be in TIM of link2 Beacon also)
A-MPDU1
A-MPDU2
MAC Addr29 is awake.
BA
MAC Addr29 is doze
Frames for Addr29 is coming or high load traffic is coming.

## Slide 6: Straw Poll 1
Do you agree that an AP MLLE can recommend a STA instance of an non-AP MLLE to switch to awake state by signaling to another STA instance of that non-AP MLLE?