## Slide 1: Signaling Support for Multi-RU Assignment
Date: 2019-11-13
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Yanyi Ding |  |  |  | 
Urabe Yoshio |  |  |  | 
Rojan Chitrakar |  |  |  | 

## Slide 2
Background
Unlike 11ax, 11be shall allow more than one RUs to be assigned to a single STA [1].
This contribution addresses efficient signaling support for assigning one or more RUs to a single STA in an EHT MU PPDU.

## Slide 3
Assumption
A single transmission scheme (i.e. same MCS and NSTS, etc.) may be applied to all RUs assigned to a single STA in an EHT MU PPDU for minimizing implementation complexity.
An EHT MU PPDU comprises one or more HE-SIG-B-like content channels, each consisting of a Common field, if present, followed by a User Specific field.
  Common field contains information regarding RU allocation.
  User Specific field consists of one or more User Block field(s).
    A User Block field comprises one or more User fields.
    Each User field contains user-specific allocation information.

## Slide 4
Multi-RU Assignment Signaling (1/5)
Two options for 11be User field design can be envisioned.
Opt1: 11be User fields have similar formats to 11ax User fields.
  For example, a 11be User field has 22 bits
    STA-ID (11 bits), MCS (4 bits), Coding (1 bit)
    Spatial configuration or NSTS/Tx BF/DCM (6 bits)
  All User fields corresponding to multiple RUs assigned to a STA contain same user-specific allocation information if a single transmission scheme is applied to all RUs assigned to the STA.
  Pros: little specification impact
  Cons: STA’s power efficiency may be disadvantaged.
    STA may need to decode and parse all of User fields in User Specific field to search for its User fields
      STA has no idea about the number of assigned RUs.
    STA may keep processing remaining PPDU even when not all of User fields addressed to the STA are correctly decoded.
      Multiple User fields addressed to the STA may belong to different User Block fields. Some of the User fields may not be correctly decoded.
      STA is not able to determine whether all of User fields addressed to the STA are correctly decoded or not.

## Slide 5
Multi-RU Assignment Signaling (2/5)
Opt2: the formats of 11be User fields are optimised for improving STA’s power efficiency. For example,
  Define two types of User fields:
    Type 1 User field contains user-specific allocation information.
    Type 2 User field does not contain user-specific allocation information, but include some information which enables a STA to position its remaining User fields in the User Specific field in case that a single transmission scheme is applied to multiple RUs assigned to the STA.
    Both types of User fields have the same size.
  Pros: STA’s power efficiency may be improved
    STA may be able to expedite search for its User fields in User Specific field.
    STA would stop processing remaining PPDU when determining not all User fields addressed to the STA are correctly decoded.
  Cons: more specification impact and a little additional overhead.

## Slide 6
Subfield | Number of bits | Description
STA-ID | 11 | 
UF Type | 1 | indicate the type of this User field
Single RU Assignment Flag | 1 | indicate whether a single RU is assigned to the intended STA
NSTS/Tx BF/DCM or Spatial Configuration | 6 | 
MCS | 4 | 
Coding | 1 | 
Example Type 1 User field format
Subfield | Number of bits | Description
STA-ID | 11 | 
UF Type | 1 | indicate the type of this User field
Contiguous RU Assignment Flag | 1 | indicate whether multiple contiguous RUs are assigned to the intended STA.
Number of Assigned RUs | 2 | indicate total number of RUs assigned to the intended STA.
RU Position/Next Assigned RU | 9 | indicate the position of RU corresponding to this User field among all the assigned RUs in case of contiguous RU assignment; indicate the next assigned RU in case of non-contiguous RU assignment.
Example Type 2 User field format
Multi-RU Assignment Signaling (3/5)
Opt2 has two more bits per User field than Opt1

## Slide 7: Multi-RU Assignment Signaling (4/5)
Further Note on Opt2
  A STA may stop processing remaining User Specific field after a Type 1 User field indicating a single RU assigned to the STA is identified.
  A STA may stop processing remaining User Specific field after a Type 1 User field and a Type 2 User field indicating multiple contiguous RUs assigned to the STA is identified.
  A STA is able to determine decoding errors occur in at least one of its User fields and stop processing remaining PPDU when
    only a single User field is identified, which is a Type 1 User field indicating multiple RUs are assigned to the STA; or
    one or more User fields including at least one Type 2 User field addressed to the STA are identified, but the number of identified User fields is not equal to the number of assigned RUs indicated in any identified Type 2 User field.

## Slide 8
Example User field setting for Opt2:
  BW = 160 MHz
  SIG-B content channel 1
    RU allocations: 242-tone RU1, 484-tone RU2, 242-tone RU7
    User fields: UF11 to UF13
  SIG-B content channel 2
    RU allocations: 242-tone RU2, 484-tone RU3, 242-tone RU8
    User fields: UF21 to UF23
  RU assignment
    STA1: 242-tone RU1
    STA2 (contiguous): 484-tone RU3, 242-tone RU7
    STA3: (non-contiguous): 484-tone RU2, 242-tone RU2, 242-tone RU8
  Suppose a single transmission scheme is applied to multiple RUs assigned to a STA
Use-Specific Field | STA-ID | UF Type | Single RU Assignment Flag | Contiguous RU Assignment Flag | Number of Assigned RUs | RU Position/Next Assigned RU
UF11 | STA1’s ID | 0 | 1 | n.a. | n.a | n.a.
UF12 | STA3’s ID | 1 | n.a. | 0 | 3 | 242-tone RU2
UF13 | STA2’s ID | 1 | n.a. | 1 | 2 | 2nd RU
UF21 | STA3’s ID | 1 | n.a. | 0 | 3 | 242-tone RU8
UF22 | STA2’s ID | 0 | 0 | n.a. | n.a. | n.a.
UF23 | STA3’s ID | 0 | 0 | n.a. | n.a. | n.a.
Multi-RU Assignment Signaling (5/5)

## Slide 9: Summary
Two options of 11be User field design for support of assigning one or more RUs to a single STA in an EHT MU PPDU are addressed.
Option 1: 11be User fields have similar formats to 11ax User fields.
  Pros: less specification impact
  Cons: STA’s power efficiency may be reduced.
Option 2: the formats of 11be User fields are optimized for improving STA’s power efficiency.
  Pros: STA’s power efficiency can be improved
  Cons: more specification impact and a little additional overhead.

## Slide 10: Reference
11-19-1262-04-00be-specification-framework-for-tgbe

## Slide 11: SP #1
Do you prefer which option of 11be User field design for support of assigning one or more RUs to a single STA in an EHT PPDU transmitted to multiple STAs?
  Option 1: 11be User fields have similar formats to 11ax User fields.
  Option 2: the formats of 11be User fields are optimized for improving STA’s power efficiency.