## Slide 1: Further Ideas on EHT Preamble Design
Date: 2019-11-11
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
In [1] we proposed to bring future compatibility to WiFi preambles starting with 802.11be
  Solve the auto-detection issue for multiple standards starting with EHT, together
  Better coexistence than just L-SIG based deferral among future generations of 802.11
  Proposed a 2 symbol Pre-SIG with a mix of universal (version independent) and version dependent fields
In this contribution, we give some more thoughts on preamble design for EHT
  Pre-SIG Contents
  High Level SIG field structure for EHT
L-STF
L-LTF
L-SIG
EHT SIG fields (?)
RL SIG
Pre- SIG
2 symbols jointly encoded.
Contains universal and
version dependent fields
Common structure for EHT and beyond

## Slide 3: Pre-SIG Contents
The version independent fields in Pre-SIG carry information that could be
  Understood by WiFi devices starting from 11be
    E.g., WiFi version identifier starting from 11be
  Beneficial to by-standers
    E.g., Info about channel occupancy and coexistence (in time/frequency/link direction)
We propose to include the following version-independent fields
  Version identifier: 3 bits
  PPDU BW and puncturing information: TBD bits
  UL/DL: 1 bit
  TXOP: >=7 bits
  BSS color: >=6 bits
Also propose to carry PPDU type as a version dependent field (present in all PPDU types)
  Every PHY version might have a different set of PPDU types
  This information is mainly useful for intended receivers and not by-standers

## Slide 4: EHT SIG High Level Design
Take the following design principles
  Minimal additional overhead when compared to 11ax
  Borrow as much of the SIG-B design as possible
Proposal on high level SIG field structure
  An EHT PPDU sent to multiple users
    Propose a variable length, variable MCS EHT-SIG after the 2 symbol pre-SIG
      EHT-SIG has a common section and a per-user section
      Content channel structure TBD
  For SU PPDU, we have the following 2 options
    Re-use the MU PPDU format
    Have a separate SU PPDU format
      In this option, the EHT-SIG (after 2 symbol pre-SIG) can be just one symbol long and be sent at MCS0
  For TB PPDU
    Possible to avoid having any EHT-SIG, just pre-SIG maybe enough

## Slide 5: EHT PPDU to multiple users: SIG Structure
Divide the EHT-SIG into two sections
  EHT-SIG-common and EHT-SIG-per-user
EHT SIG is variable length and variable MCS
  Just like HE-SIG-B
EHT-SIG-common is bigger in size as it needs to accommodate overflow from the 2 symbol pre-SIG as well
L-STF
L-LTF
L-SIG
RL SIG
Pre-SIG
EHT-SIG Common
L-STF
L-LTF
L-SIG
RL SIG
HE-SIG-A
11ax MU PPDU
EHT PPDU sent
to multiple users
New fields
+
HE-SIG-B Common
HE-SIG-B per-user
EHT-SIG per-user

## Slide 6: EHT SU PPDU SIG structure (only if a separate SU PPDU format is desired)
New fields (those not present in 11ax) in EHT SU preamble can be
  Universal Fields
    Version Identifier ~ 3 bits
    Punctured channel info
    More bits in BSS Color, TxOP, BW (if needed)
  Version dependent fields
    PPDU type ~ 2 bits
    New feature bits
2 symbol Pre-SIG not enough to accommodate new fields and the 11ax-SIG-A-like information
Need an additional EHT-SIG symbol to accommodate the overflow from the 2 symbol pre-SIG
  Can be MCS0
  One symbol provides 16 more bits (after removing 6 bits tail and 4 bit CRC) which should be enough
L-STF
L-LTF
L-SIG
RL SIG
Pre-SIG
EHT-SIG
L-STF
L-LTF
L-SIG
RL SIG
HE-SIG-A
11ax SU PPDU
EHT SU PPDU
New fields
+

## Slide 7: EHT TB PPDU structure
Recall that in HE-SIG-A in HE TB PPDU
  We had a lot of reserved bits (9 which were copied from trigger frame and 1 more)
Bottom line: For TB PPDU, have a lot of free bits to accommodate any new fields of EHT
  No new SIG symbol is needed Can keep the same preamble overhead as 11ax
L-STF
L-LTF
L-SIG
RL SIG
Pre-SIG
L-STF
L-LTF
L-SIG
RL SIG
HE-SIG-A
11ax TB PPDU
EHT TB PPDU
Reserved bits
New fields
-
+

## Slide 8: Summary
We proposed the following for EHT preamble design
  Pre-SIG contents
  EHT-SIG after Pre-SIG
    Variable length and variable MCS in case of an EHT PPDU sent to multiple users
      Split into common and per-user sections like HE-SIG-B
    One symbol at MCS0, for the SU PPDU if a separate SU PPDU format is needed
    May not be needed for the TB PPDU

## Slide 9: Straw-poll 1
Do you agree to including the following version independent fields in the 2 symbol SIG field that goes immediately after the RL-SIG?
  TXOP: >=7 bits
  BSS color: >=6 bits
  PHY version identifier: 3 bits
  UL/DL: 1 bit

## Slide 10: Straw-poll 2
Do you agree with having a variable MCS and variable length EHT-SIG (immediately after the 2 symbol SIG that carries universal fields) in an EHT PPDU sent to multiple users?

## Slide 11: Straw-poll 3
Do you agree that the EHT-SIG (immediately after the 2 symbol SIG that carries universal fields) in an EHT PPDU sent to multiple users will have a common field and user-specific field(s) ?

## Slide 12: References
[1] Sameer Vermani et al, “Forward Compatibility for WiFi Preamble Design” , IEEE Document 11/19-1519r0