## Slide 1: Multi-link Acknowledgement
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Overview
There have been some contributions dealing with the multi-link acknowledgements [1-4]
We think acknowledgement including ack information of multiple links can improve efficiency
We also think the multi-link acknowledgement can easily be implemented with a small modification of 11ax
In this contribution...
  We first briefly introduce three candidate acknowledgement methods for multi-link
    Per-link acknowledgement
    Single aggregated acknowledgement
    Aggregated acknowledgement with duplication
  We address some considerations for the acknowledgement methods in sync and async modes
  We raise appropriate usage cases and requirement issues for the acknowledgements

## Slide 3: Multi-link acknowledgement methods
Per-link acknowledgement
  A recipient responds with an acknowledgement on the same link where the reception operation occurred
  It is independent of multi-link environment and synchronization mode
  Block Ack operation can be set up by using ADDBA request/response as is
  In this case, transmitter cannot distinguish between data failure and ack failure
    E.g., whether the data has failed or the ACK has failed, the data is to be retransmitted and it leads to inefficiency
STA:
AP:
MPDU1~2
Link A
Link B
MPDU1~2
ACK1~2
MPDU3~4
Link A
Link B
ACK3~4
ACK3~4
MPDU3~4
ACK1~2
Sync mode
Async mode
STA:
AP:
MPDU1~2
Link A
Link B
MPDU1~2
ACK1~2
MPDU3~4
Link A
Link B
ACK3~4
ACK3~4
MPDU3~4
ACK1~2

## Slide 4: Multi-link acknowledgement methods
Single aggregated acknowledgement
  An acknowledgement frame can contain ack information of multiple links
    In sync mode, all ack information is gathered and aggregated; an ack frame is sent on one of links on which the data was received
    In async mode, all ack information of multiple links during a certain period is aggregated and is sent on which the data was received
  A recipient may or may not respond with the aggregated acknowledgements on its own link
  Relatively low reliability and high throughput gain
STA:
AP:
MPDU1~2
Link A
Link B
MPDU1~2
ACK1~4
MPDU3~4
Link A
Link B
MPDU3~4
ACK1~4
Sync mode
Async mode
STA:
AP:
MPDU1~2
Link A
Link B
MPDU1~2
MPDU3~4
Link A
Link B
ACK1~4
ACK1~4
MPDU3~4

## Slide 5: Multi-link acknowledgement methods
Aggregated acknowledgement with duplication
  Duplicated acknowledgement frames containing ack information of multiple links are transmitted simultaneously over multiple links
    In sync mode, all ack information is gathered and aggregated; ack frames are duplicated and they are sent over links on which the corresponding data frame was transmitted
    In async mode, to respond with duplicated ack frames, any temporary synchronization is required
  High reliability due to the redundant acknowledgement information
STA:
AP:
MPDU1~2
Link A
Link B
MPDU1~2
ACK1~4
MPDU3~4
Link A
Link B
ACK1~4
ACK1~4
MPDU3~4
ACK1~4
Sync mode
Async mode
STA:
AP:
MPDU1~2
Link A
Link B
MPDU1~2
ACK1~4
MPDU3~4
Link A
Link B
ACK1~4
ACK1~4
MPDU3~4
ACK1~4

## Slide 6: Considerations on acknowledgent methods
Single multi-link acknowledgement in sync mode
  Ack channel should be considered (E.g., designated link for ack or explicit solicitation)
    Acknowledgement channel may be negotiated in advance (using ADDBA negotiation) or on-demand manner (per-TXOP or per-PPDU)
  In sync mode, this single multi-link acknowledgment does not need to be implemented especially in multiple frame exchanges since it is hard to utilize this free time
  If the ack method is determined per PPDU, implicit BAR should be able to indicate whether that ack includes per-link ack or multi-link ack; otherwise, it is not necessary
  If this single ack transmission becomes failure, retransmission method needs also be considered
    To guarantee reliable transmission, acks may be transmitted with duplication for the repeated transmission of failed transmissions
STA:
AP:
MPDU1~2
MPDU3~4
MPDU3~4
ACK3~4
ACK3~4
MPDU1~2
MPDU1~2
MPDU5~6
MPDU5~6
ACK
1~2,5~6
ACK
1~2,5~6
Link A
(Ack channel)
Link B
(Data channel)
Link A
(Ack channel)
Link B
(Data channel)
MPDU1~2
MPDU1~2
MPDU3~4
MPDU3~4
ACK1~4
MPDU1~2
MPDU1~2
MPDU3~4
MPDU3~4
ACK1~4
ACK1~4
ACK1~4
ACK1~4
STA:
AP:
Link A
(Ack channel)
Link B
(Data channel)
Link A
(Ack channel)
Link B
(Data channel)
ML Implicit BAR
No Ack
ML Implicit BAR
No Ack
ML Implicit BAR
ML Implicit BAR
ML Implicit BAR
No Ack
Data failure case
Ack failure case

## Slide 7: Considerations on acknowledgent methods
Single multi-link acknowledgement in async mode
  Ack channel should be considered for the same reason as above
  Acknowledgement information needs to be solicited or indicated by the PPDU with implicit BAR
  It is possible to use BAR frame since it has BA bitmap field, however, it causes additional performance loss
  BAR frame may indicate whether it is for multi-link BAR or not according to the negotiation of acknowledgement
STA:
AP:
MPDU1~2
Link A
(Ack channel)
Link B
(Data channel)
MPDU1~2
MPDU3~4
Link A
(Ack channel)
Link B
(Data channel)
MPDU3~4
ACK1~4
ACK1~4
MPDU1~2
MPDU1~2
MPDU3~4
MPDU3~4
MPDU3~4
MPDU3~4
ACK1~4
ACK1~4
ML BAR
ML BAR
STA:
AP:
Link A
(Ack channel)
Link B
(Data channel)
Link A
(Ack channel)
Link B
(Data channel)
ML Implicit BAR
No Ack
No Ack
Block Ack
Block Ack
Using implicit BAR
Using explicit ML BAR

## Slide 8: Considerations on acknowledgent methods
Aggregated acknowledgement with duplication in sync mode
  Link A of the AP can recognize whether the data failed or the ack failed by means of BlockAck on Link B
    In this case, unnecessary transmission can be avoided if the block ack frame is failed
  To this end, (implicit) BAR should be able to indicate that it is requesting acks over multi-link to distinguish between per-link ack and aggregated ack
  Ack failure can occur especially often when the stations are on the edge side of the BSS
  For the same reason as above, implicit BAR may indicate whether it is for multi-link BAR or not according to the negotiation of acknowledgement
STA:
AP:
Link A
Link B
MPDU1~2
MPDU3~4
Link A
Link B
MPDU1~2
ACK3~4
ACK3~4
MPDU1~2
MPDU1~2
MPDU5~6
MPDU5~6
ACK1~2,5~6
ACK1~2,5~6
ACK1~2,5~6
ACK1~2,5~6
MPDU1~2
MPDU1~2
MPDU3~4
MPDU3~4
ACK1~4
ACK1~4
MPDU5~6
MPDU5~6
MPDU7~8
MPDU7~8
ACK5~8
ACK5~8
ACK5~8
ACK5~8
ACK1~4
Data failure case
Ack failure case
ML Implicit BAR
ML Implicit BAR
ML Implicit BAR
ML Implicit BAR
ML Implicit BAR
ML Implicit BAR
ML Implicit BAR
ML Implicit BAR

## Slide 9: Considerations on acknowledgent methods
Aggregated acknowledgement with duplication in async mode
  To transmit multiple duplicated ack frames at the same time, transmission time have to be synchronized
    New ack policy needs to be introduced to align the acks when there is no BAR
  Block Ack Request frame can be used to synchronize time to transmit acks
    However, there is a wasted period, further, the performance gain may be more worse due to the redundant control frames
    With the BAR frame, operation mode is subject to change from async mode to sync mode
  Implicit BAR or BAR frame may need to indicate whether it is for multi-link BAR or not according to the negotiation of acknowledgement
STA:
AP:
MPDU1~2
Link A
Link B
MPDU1~2
MPDU3~4
Link A
Link B
MPDU3~4
ACK1~4
ACK1~4
MPDU1~2
MPDU1~2
MPDU3~4
MPDU3~4
ACK1~4
ACK1~4
ACK1~4
ACK1~4
ACK1~4
ACK1~4
ML BAR
ML BAR
ML BAR
ML BAR
STA:
AP:
Link A
Link B
Link A
Link B
Implicit time sync
Explicit time sync
Block Ack
Block Ack
New Ack Policy
ML Implicit BAR

## Slide 10: Appropriate usage cases
Per-link acknowledgement
  If there is a relationship between TID and link, fetching ack information from other links may be improper
  In this case, per-link acknowledgement should be used
Single aggregated acknowledgement
  Applications requiring high performance
    The channel should be relatively good
  It can be more effective with asynchronous mode
    If it is used in synchronous mode, a free time cannot be utilized especially for multiple frame exchange
Aggregated acknowledgement with duplication
  Reliable communications
  More suitable for synchronous mode even if it is available for asynchronous mode with some negotiations or ack solicitations

## Slide 11: Considerations
MAC sequence space per <TID & RA>, transmit window and reception window should be shared between APs/STAs within an MLLE
Bitmap size for acknowledgement may need to increase to support the aggregated ack information
If BlockAck frame is requesting other links’ ack information, this can be explicitly indicated by means of any indication bit
In (implicit) BAR, it should be indicated whether or not the BAR is requesting multi-link block ack
  If the acknowledgement method is designated for a particular period, e.g., per ADDBA, ML implicit BAR or ML BAR may not be needed
If sync mode operates opportunistically, it is better to select ack methods opportunistically as well

## Slide 12: Conclusion
Data failure case and ack failure case can be distinguished and thus unnecessary retransmission can be avoided with aggregated acknowledgement
Using single aggregated ack, performance gain can be relatively higher especially when async mode is operating
With some changes and allowing that an acknowledgement frame can contain ack information of multiple links, aggregated acknowledgement with duplication and single multi-link ack can easily be adopted
Also, mentioned three ack methods can selecvitely used depending on channel environment and traffic property on-demand manner

## Slide 13: SP #1
Do you agree to add the following text to the TGbe SFD?
  TGbe shall support that a block ack frame can be transmitted on the link where the corresponding data frame is transmitted in multi-link environment.

## Slide 14: SP #2
Do you agree to add the following text to the TGbe SFD?
  TGbe shall support that a block ack frame containing ack information from other links where the corresponding data frame is not transmitted can be transmitted in multi-link environment.

## Slide 15: References
[1] 19/1512r2, “Multi-link acknowledgement”
[2] 19/1532r0, “Discussion on multi-link acknowledgement”
[3] 19/1575r0, “Multi-link BA operation”
[4] 19/1591r1, “BA setup for multi-link aggregation”