## Slide 1: Discussion on 240MHz Bandwidth
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In the September F2F meeting, TGbe decided to support 320 / 160+160 MHz
In this contribution, we propose that 11be supports 240 / 160+80 MHz transmission
In addition, we discuss a tone plan and a bandwidth indication method for 240 / 160+80 MHz

## Slide 3: 240 / 160+80 MHz Bandwidth
240 / 160+80 MHz Bandwidth would be helpful to improve average throughput and efficiency
  If a certain 80MHz channel within 320 / 160+160 MHz bandwidth is busy due to an OBSS transmission, it is better to use 240 / 160+80 MHz bandwidth than to use only 80 / 160 MHz bandwidth for a PPDU transmission
  Exploiting these two types of bandwidth modes (240/160+80 MHz, 320/160+160 MHz) can provide better throughput (maximum 12% gain) and efficiency compared to using only the 320/160+160 MHz bandwidth [1][2]
We propose to support 240 / 160+80 MHz bandwidth in 11be which is constructed from three 80MHz channels including primary 80MHz
  240 / 160+80 MHz can be formed by 80MHz preamble puncturing in the 320 / 160+160 MHz bandwidth

## Slide 4: Tone Plan
Tone plan of 240 / 160+80 MHz can be determined based on that of 320 / 160+160 MHz if we consider 80MHz preamble puncturing
  For example, if 2x2020-tone RU based tone plan [3] is used for 320 / 160+160 MHz, the tone plan of 240 / 160+80 MHz can be composed of 2020-tone RU and 996-tone RU based structure
For a simple implementation, 11ax 80MHz tone plan can be repeated three times for both OFDMA and non-OFMDA tone plans of 240/160+80 MHz regardless of the 320 / 160+160 MHz tone plan
12 left guard
23 null tones
5 null tones
11 right guard
996-tone RU
5 null tones
996-tone RU
5 DC
996-tone RU
23 null tones
5 null tones
12 left guard
23 null tones
2020-tone RU
5 null tones
11 right guard
996-tone RU

## Slide 5: Bandwidth Indication (1/2)
Similar to the 11ax PPDUs, TGbe can consider various PPDU types, for example,
  EHT SU PPDU for SU transmission using an entire bandwidth, i.e., 20/40/80/160/80+80/240/160+80/320/160+160 MHz
  EHT OFDMA PPDU for MU transmission and SU transmission with multiple RU allocation based on preamble puncturing as well (Separate PPDUs can be defined for MU and SU transmission)
  EHT ER SU PPDU, EHT TB PPDU, etc.
  PPDU names can be changed
80MHz preamble puncturing can be considered in EHT SU PPDU to form 240/160+80 MHz while any kind of preamble puncturing (e.g., 20MHz preamble puncturing) can be applied to EHT OFDMA PPDU to enhance efficiency
  We consider that EHT SU PPDU doesn’t have a field like HE-SIG-B, and thus, exact puncturing patterns need to be indicated in a Bandwidth field

## Slide 6: Bandwidth Indication (2/2)
In EHT SU PPDU, 3 bits may be sufficient to indicate the bandwidth including 240 / 160+80 MHz
  There are three possible cases for 240 / 160+80 MHz transmission
  Then, we can use the following Bandwidth field as an example
  For simplicity, we can only consider case 2 or 3 for 240/160+80MHz transmission, i.e., it is possible only if primary 160MHz is idle
We consider that primary 80MHz is always used when transmitting 240 / 160+80 MHz PPDU
To decode the PPDU, receivers need to know which channels are used to transmit the PPDU
Exact channel information needs to be indicated in the Bandwidth field if EHT SU PPDU doesn’t have a kind of the RU allocation field as in HE-SIG-B
0: 20MHz
1: 40MHz
2: 80MHz
3: 160/80+80MHz
4: 240/160+80MHz Case 1
5: 240/160+80MHz Case 2
6: 240/160+80MHz Case 3
7: 320/160+160MHz
Case 1
Case 2
Case 3
: not used or punctured

## Slide 7: Summary
We have proposed that 11be supports 240 / 160+80 MHz transmission
Its tone plan and bandwidth indication method have been discussed

## Slide 8: Straw Poll #1
Do you agree to add the following text to the TGbe SFD?
  11be supports 240 MHz and 160+80 MHz transmission
    240 / 160+80 MHz bandwidth is constructed from three 80MHz channels which include primary 80MHz
Y/N/A : 24/0/19

## Slide 9: Motion #1
Move to add the following text to the TGbe SFD
  240 / 160+80 MHz bandwidth is constructed from three 80MHz channels which include primary 80MHz
Moved by: Eunsung Park
Second:
Y/N/A :

## Slide 10: Straw Poll #2
Do you agree to add the following text to the TGbe SFD?
  For the tone plan of 240MHz and 160+80MHz, 11ax 80MHz tone plan is repeated three times
Y/N/A : //

## Slide 11: Straw Poll #3
Do you agree to add the following text to the TGbe SFD?
  11be supports EHT SU PPDU
    EHT SU PPDU is used for the DL/UL SU transmission using an RU which size corresponds to the bandwidth indicated in the Bandwidth field in a EHT-SIG field
      The bandwidth indicated in the Bandwidth field can be one of 20MHz, 40MHz, 80MHz, 160/80+80MHz, 240/160+80MHz, 320/160+160MHz, etc.
    Format is TBD
    Note: PPDU name can be changed
Y/N/A : //

## Slide 12: Straw Poll #4
Do you agree to add the following text to the TGbe SFD?
  In EHT SU PPDU, 3 bits are used for the Bandwidth field
Y/N/A : //

## Slide 13: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
  In EHT SU PPDU, the Bandwidth field includes the following description
    Set to TBD1 for 240/160+80MHz where primary 80MHz, secondary 80MHz, and lower 80MHz in secondary 160MHz are used for transmission
    Set to TBD2 for 240/160+80MHz where primary 80MHz, secondary 80MHz, and higher 80MHz in secondary 160MHz are used for transmission
    Set to TBD3 for 240/160+80MHz where primary 80MHz, and lower and higher 80MHz in secondary 160MHz are used for the transmission
    Note that secondary 160MHz indicates the 160MHz channel other than primary 80MHz and secondary 80MHz in 320/160+160MHz
Y/N/A : //
Y/N/A : //

## Slide 14: Straw Poll #6
Do you agree to add the following text to the TGbe SFD?
  In EHT SU PPDU, the Bandwidth field includes the following description
    Set to TBD1 for 240/160+80MHz where primary 80MHz, secondary 80MHz, and lower 80MHz in secondary 160MHz are used for transmission
    Set to TBD2 for 240/160+80MHz where primary 80MHz, secondary 80MHz, and higher 80MHz in secondary 160MHz are used for transmission
    Note that secondary 160MHz indicates the 160MHz channel other than primary 80MHz and secondary 80MHz in 320/160+160MHz
Y/N/A : //
Y/N/A : //

## Slide 15: References
[1] 802.11-19/0778r0 Consideration on 320MHz Bandwidth and 16 Spatial Streams
[2] 802.11-19/1066r0 Tone Plan Discussion
[3] 802.11-19/1492r0 Non-OFDMA Tone Plan for 320MHz