## Slide 1: MLA MAC Addresses Considerations
Date: 2019-11-xx
Authors:

## Slide 2: Introduction
We discuss the following in this presentation
  Recap of current MLA architecture proposal and focus on the link MAC addresses and the MAC-SAP MAC address
  Present some considerations and proposals on the MAC addresses on the AP side

## Slide 3: MLA Architecture recap
Each MLLE has a single MAC-SAP MAC Address that interfaces with upper layers
MLLE has a unique MAC-SAP MAC Address (upper MAC Address)
Each STA (link) has its own MAC Address
  They could be the same or different between links
  They could be the same or different than the upper MAC Address
Upper MAC
Lower MAC

## Slide 4: MLA Architecture recap (cont’d)
Upper-MAC maintains the following, shared by all links
  MAC-SAP MAC address
  Single BA session, single SN space (per TID)
    So MPDUs can be tx/retx on any link and have a common BA scoreboard
  Single Association and security context
    Single multi-link association established via signaling over a single link
    Single 4-way handshake to establish a single (common) security context
  Single PN (per MLLE)
    Helps maintain existing data reception processes on the receiver
      i.e., Replay check follows reordering based on common SN
    Single replay detection block follows reordering and BA block

## Slide 5: MAC-SAP MAC Address Considerations
A single upper MAC address should be the LAN MAC address of the MLLE (i.e., M in the figure) for other devices on the same LAN to communicate with
The upper MAC address needs to be a unique value (e.g., EIU-48) between MLLEs. It can be one of the following:
  Set to a value completely independent of any of the link MAC address
  Set to the link MAC address of one of the links e.g., M=x and (x≠y or x=y)

## Slide 6: Link MAC Addresses of an MLA AP Considerations
The link MAC addresses should be different to avoid confusing the legacy clients
  Beacon uses link MAC address
  BSS Color uses link MAC address. Otherwise the colors of the BSSs on two different bands will be the same from the same MLLE. Each link will need to have its own color
Have to be different in non-colocated case when two APs use the same channel on the two links on the same client (so their beacons won’t confuse the client)

## Slide 7: Link MAC Addresses of an MLA AP Considerations (Cont’d)
Prefer MLA AP to have different link MAC addresses on each link
Prefer all DL frames also carry the same link MAC addresses OTA
    Traditional receiver filtering
    SIFs turn around

## Slide 8: Link MAC Addresses of an MLA STA Considerations
MLA STA may have the same or different link MAC addresses on each link
Prefer all UL frames also carry the same link MAC addresses OTA
    Traditional receiver filtering
    SIFs turn around

## Slide 9: Conclusion
We presented some considerations of MLA MAC addresses
Conclusions:
  The MAC addresses sent OTA are the link MAC addresses
  AP uses different MAC addresses on each link
  STA may use same or different MAC addresses on each link

## Slide 10: SP1
Do you support the following?
The value of the RA/TA fields sent over-the-air in the MAC header of a frame is the MAC address of the STA affiliated with the MLLE corresponding to that link

## Slide 11: SP2
Do you support the following?
An AP MLLE uses different MAC addresses on each link (e.g., such as those set in the RA/TA fields of the MAC header)