## Slide 1: MLA Security Considerations
Date: 2019-11-xx
Authors:

## Slide 2: Introduction
We discuss the following in this presentation
  Recap of current MLA architecture proposal and focus on the link MAC addresses and the MAC-SAP MAC address
  Present some considerations and proposals on MLA security for group-addressed and unicast frames

## Slide 3: MLA Architecture recap
Each MLLE has a uniqee MAC-SAP MAC Address that interfaces with upper layers
Each STA (link) has its own MAC Address
  The MAC Addresses could be the same or different between links
  The MAC Addresses could be the same or different than the MAC-SAP MAC Address
Upper MAC
Lower MAC

## Slide 4: MLA Architecture recap (cont’d)
Upper-MAC maintains the following, shared by all links
  MAC-SAP MAC address
  Single BA session, single SN space (per TID)
    So MPDUs can be tx/retx on any link and have a common BA scoreboard
  Single Association and security context
    Single multi-link association established via signaling over a single link
    Single 4-way handshake to establish a single (common) security context
  Single PN (per MLLE)
    Helps maintain existing data reception processes on the receiver
      i.e., Replay check follows reordering based on common SN
    Single replay detection block follows reordering and BA block

## Slide 5: MLA Security Context Considerations
For simplicity we propose the following:
A single key set (i.e., PTK, etc) applied to all the links
Either individual per-link GTK/IGTK or a single GTK/IGTK (more on later slides)
PTK generated using the MAC-SAP MAC addresses of the two peer entities
  MAC-SAP MAC address servers as a common address for all the links
  Prefer this over using a link MAC address because the link may be disabled at times after association whereas the MAC-SAP MAC address is always there regardless of the state of the links

## Slide 6: Group-Addressed Frames Considerations
Currently, for link-specific group-addressed frames (e.g., robust management frames) uses Broadcast/multicast integrity protocol (BIP)
For BIP, a 48-bit IPN (IGTK PN) is used for replay attack protection
AAD uses FC, A1, A2, and A3
Problem: A2 may be identical between two links in MLA; Hence the AAD will not be unique
  A link-specific group-addressed frame transmitted on one link may be replayed on another link and still be accepted by the STA on the other link

## Slide 7: Security Options
Option 1
  Mandate for an MLLE of an AP to use different link MAC addresses on each radio. Use a single GTK/IGTK for all the links (or alternatively use one GTK/IGTK per link)
  Pros: no changes to the AAD and it works for legacy STAs as well
  Cons: requirement of using different link MAC addresses. Legacy STAs on one link will know the GTK of the STAs associated in the other links
Option 2
  Generate one IGTK per link during association
  Pros: no changes to AAD. If re-key is needed on one link, only the STAs on that link needs to be re-keyed
  Cons: more keys to maintain
Prefer Option 1

## Slide 8: Unicast Frames Considerations
Currently for single-link, CCMP/GCMP use the following:
  CCMP Nonce = Nonce flags || A2 || PN
  GCMP Nonce = A2 || PN
  AAD uses A1/A2/A3/A4
Next, we explore whether existing CCMP/GCMP derivation can be reused for MLA
  i.e., using the link MAC addresses as A1-A3 like today

## Slide 9: Unicast Frames Considerations (Cont’d)
Problem: the same Nonce value will be reused to encrypt different data (a security flaw) if all of the following are true:
  The A2 of two different links are the same (allowed by the MLA architecture)
  A frame is retransmitted on another link using the same A2 and same PN (PN remains the same across retransmissions to avoid out-of-order PN received after SN re-ordering)
  The A1 of two different links are different (allowed by the MLA architecture) <- different AAD data gets re-encrypted using the same Nonce
This is a violation of the spec per sub-clause 12.5.3.1
  “CCM requires a fresh temporal key for every session. CCM also requires a unique nonce value for each frame protected by a given temporal key, and CCMP uses a 48-bit packet number (PN) for this purpose. Reuse of a PN with the same temporal key voids all security guarantees.”

## Slide 10: Security Options
Option 1:
  Include a link identifier and a direction bit in the Nonce
    Nonce needs to be unique for the peer MLLEs that share the same TK
  Keep the length of the Nonce the same because the length is highly optimized for encryption computation
    Need to puncture the link identifier and direction bit into the current Nonce
    No strict requirements to contain all 48 bits of the TA. Justifications can be found in RFC 3610 Chapter 5 (Nonce Suggestions; last paragraph) for CCM and NIST SP 800-38D chapter 8.2.1 for GCM
  Pros:
    Maintain the current security level (A1-A4 fields protected like today)
    Allows same or different link MAC addresses
  Cons:
    Implementation modification to the Nonce input is needed

## Slide 11: Security Options
Option 2: mandate separate MAC addresses per radio
  Pros: clean solution. Can reuse all CCMP/GCMP for both unicast and group-addressed frames
  Cons:
    Excludes cases where only one MAC address is available
    Forces different link MAC addresses so more MAC addresses needed

## Slide 12: Conclusion
For MLA Operation, we presented some security issues associated with unicast and group-addressed frames that are specific to MLA operation
We presented some options to solve these issues for MLA

## Slide 13: SP1
Do you support the following?
After multi-link setup between two MLLEs, a single PMK/PTKSA and PN space are established, maintained and used across links

## Slide 14: SP2
Do you support the following?
An MLLE on an AP uses different MAC addresses on each link?