## Slide 1: Multiple RU discussion
Date: 2019-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Ross Jian Yu |  | F3-6A, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 

## Slide 2: Background
In [1], it is mentioned, multiple RUs for one user should be supported to enhance spectral efficiency, take advantage of frequency diversity.
This proposal discusses several aspects regarding multiple RUs for one user transmission:
  PPDU format
  Transmission in Data field
  Signaling

## Slide 3: Multiple RUs for one user - PPDU format
For EHT MU PPDU and EHT TB PPDU, since OFDMA is already supported, it is straightforward to support multiple RUs for one user.
  How many RUs can one STA support needs to be further evaluated, depending on the complexity and cost
For EHT SU PPDU, if 11be supports preamble puncture for SU PPDU. Because of puncture, there will be several discontiguous channels. If the discontiguous channels are seen as different RUs, and since SU is targeted for one user, then multiple RUs for one user should also be supported.

## Slide 4: Multiple RUs for one user – Transmission in Data Field
There can be several ways to transmit the data in multiple RUs:
 | Method | Pro | Con
Opt1 | act as transmit the data to two different users, each RU is encoded, interleaved separately | Can reuse existing Tx procedure. Full flexibility regarding MCS, NSS. | Robustness is not fully achieved Require parallel MAC processing
Opt2 | The bits are encoded together, and parse to different RUs, separate interleaver/tone mapper | Similar procedure as 160/80+80MHz transmission | Robustness is not fully achieved May need to define new encoding parameters
Opt3 | Opt1/Opt2+interleaver across RUs | Pro of Opt1/Opt2 Fully utilize the robustness | Need interleaver across RUs
Opt4 | Act as one big continuous RU | Can reuse existing Tx procedure if big RU is already defined RU | Need new parameters for encoding, interleaver if big RU is not defined

## Slide 5: Multiple RUs for one user - Signaling
Regarding signaling, for EHT MU PPDU and EHT TB PPDU, the simplest way is to enable the same AID for multiple user fields.
  May affect the procedure of parsing. Previously, the STA can stop decoding once its own AID is detected. May need some signaling to tell the STAs when to stop parsing.
With some restriction, for example, same MCS, NSTS, some further optimization regarding overhead can be considered.

## Slide 6: Wrap up
Several aspects regarding multiple RUs for one user transmission have been discussed regarding:
  PPDU format
  Transmission in Data field
  Signaling
More evaluation and simulations are needed.

## Slide 7: Straw Poll
 | Method
Opt1 | act as transmit the data to two different users, each RU is encoded, interleaved separately
Opt2 | The bits are encoded together, and parse to different RUs, separate interleaver/tone mapper
Opt3 | Opt1/Opt2+interleaver across RUs
Opt4 | Act as one big continuous RU
Which option do you prefer?
  Opt1
  Opt2
  Opt3
  Opt4
  Need more discussion

## Slide 8: Reference
1. https://mentor.ieee.org/802.11/dcn/19/11-19-1126-00-00be-enhanced-resource-unit-allocation-schemes-for-11be.pptx