## Slide 1: MLO Asynch Qsynch Synch
Date: 2019-10-20
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Ron Porat |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 2: Abstract
TGbe needs to examine each of the suggested operational modes for Multi-Link Operation (MLO)
Asynchronous mode
  Supports simultaneous TX on one link with RX on other links
Quasi-asynchronous mode
  Support staggered TX start times across links, with alignment of TX PPDU end times
Synchronous mode
  Only supports simultaneous TX across links when both the TX PPDU start times and TX PPDU end times are aligned

## Slide 3: Asynchronous
Simultaneous TX and RX on links
Independent EDCA per link
A desired mode of operation

## Slide 4: Synchronous
Simultaneous TX and RX not possible
Simultaneous TX allowed
  TX PPDU start times must be MAC-timing aligned
  TX PPDU end times must be MAC-timing aligned
  TX PPDUs on multiple links can be:
    From a single PHY, e.g. a single PPDU
      Any receiver can accept PPDUs from multiple links simultaneously
    From multiple PHYs, e.g. multiple PPDUs
Simulations suggest that performance measures are not improved
  Using multiple EDCA, requiring common winning start time

## Slide 5: Quasi-asynchronous
Simultaneous TX and RX not possible
  Or at least, impaired
Simultaneous TX allowed
  TX PPDU end times must be MAC-timing aligned
  TX PPDU start times can be MAC-timing offset
If TX PPDU start times are offset, then
  Q: How is the offset determined?
  A: Through EDCA on the second TX link
  Q: If simultaneous RX/TX is not possible, then how is EDCA possible on the non-transmitting link(s)?
  A: See next slide

## Slide 6: Partial EDCA (PEDCA)
Q-asynch second link EDCA will be partial EDCA
  The following CCA components will still function on link B after the start of a TX PPDU on one link A
    Pre-existing NAV countdown
    Pre-existing PHY Length field countdown
  The following CCA components will be impaired or non-functioning:
    Packet detection (e.g. providing medium BUSY indication)
    PHY header decode (e.g. providing PHY LENGTH information)
    PHY payload decode (e.g. providing DUR field information)
    ED (e.g. providing medium BUSY indication)

## Slide 7: Consequences of PEDCA
If some part of CCA is still operational, is this good enough to make a decision regarding a medium access attempt on a second link?
  What if some of the functions are impaired, but still functioning?
    E.g. is it still acceptable if the preamble detection minimum SINR rises from -82 to -78?
    E.g. is operation still acceptable if the ED function operates above -55
    What levels are acceptable?
  If multiple MLLE are waiting for the same NAV, will this create an increased probability of collision?
    Due to similar TX start times following the end of NAV and reduced probability of effective randomization
  Accidental spatial reuse occurs

## Slide 8: PEDCA Mitigation
Beacons advertise the fact that Qsynch operation is being performed
  I.e. a competing Asynch BSSs can avoid the Qsynch channels
  I.e. a competing Qsynch BSSs can share the Qsynch channels
Spatial Reuse considerations
  E.g. always allow SR on the second TX, or higher threshold
Define a minimum RX performance on the second link
  E.g. achieved through first link TX power constraint
  E.g. achieved through channel separation > X MHz
  E.g. achieved through design considerations
  Specify the minimum performance to keep the competition fair

## Slide 9: Why Q-asynch?
Limited Aysnch channel pairings
  Depends on isolation
  Possible pairings:
    The lower two 5 GHz 160 MHz channels
    The upper three or four 6 GHz 160 MHz channels
  I.e. not that many Asynchronous channel choices available
    Those channels will be crowed
Non-AP STA probably no Asynch option
  Necessary filtering potentially excessively expensive

## Slide 10: Is Q-asynch Worthwhile?
When Asynchronous links are not possible
  Q-asynch is certainly better than Synchronous
  And Q-asynch is better than one link

## Slide 11: Straw poll #1
Do you support that the SFD includes the following statements under the heading Multi-link Operation:
  The amendment shall define:
    An asynchronous mode of operation in which frames are transmitted using independent medium access functions on each asynchronous link and simultaneous TX/RX is allowed
    A new threshold for Minimum RX sensitivity which only applies for MLLE, and only when there is a transmission occurring on the nearest other link
      Existing Minimum RX sensitivity remains, e.g. 17.3.10.6 CCA requirements
      The use of the new threshold is advertised in beacons
    A mechanism for a STA to dynamically advertise a simultaneous RX/TX restriction
  YES
  NO

## Slide 12: Straw poll #2
Do you support that the SFD includes the following statements under the heading Multi-link Operation:
  The amendment shall include a mechanism for negotiating the use of asynchronous mode of multi-link operation and quasi-asynchronous mode of multi-link operation
    Possibly as a function of link operating channels
    Possibly as a function of various EDCA performance metrics
  YES
  NO
  ABS

## Slide 13: Straw Poll #3
Do you support that the SFD includes the following statements under the heading Multi-link Operation:
  The amendment shall include a mechanism for an MLLE to request PPDU end time alignment on parallel links when the PPDUs are transmitted from one MLLE to the requesting MLLE
    Request for alignment can be dynamically updated, when for example, a link is moved, or when a link is enabled or disabled
  YES
  NO
  ABS

## Slide 14: References
[1] Draft P802.11ax_D5.0
[2] 11-19-1291-03-00be-performance-aspects-of-multi-link-operations