## Slide 1: UL MU Efficiency and Multi-Link
Date: 2019-11-05
Authors:
Name | Affiliations | Address | Email
Jeongki Kim | LG Electronics | LG Seocho R&D Campus, Korea | jeongki.kim@lge.com
Suhwook Kim | LG Electronics |  | suhwook.kim@lge.com
Insun Jang | LG Electronics |  | insun.jang@lge.com
Jinsoo Choi | LG Electronics |  | js.choi@lge.com
HanGyu Cho | LG Electronics |  | hg.cho@lge.com

## Slide 2: Introduction
In 11ax, UL MU operation is one of important features in terms of high efficiency, which can reduce the contention by the EDCA based UL accesses significantly and thus the entire system throughput will be improved [1][2]
Multi-link operation is one of the main candidates for improving the WLAN performance in TGbe [3]-[9]
  A single device can support the multiple links and the data of the device can be delivered to another device through the multiple links
  Multi-link feature can increase the peak/average throughput of the device
Device A
Device B
Link 1
Link 2
Data 1
Data 2
Data 3
Data 4

## Slide 3: Background (1/2)
For better UL MU efficiency in 11ax, an HE STA can send a BQR/BSR to AP and AP can trigger the HE STA efficiently based on the BQR/BSR
  Based on the received BQR, the AP can know which channels of the STA are idle or busy before UL MU TX and allocate to the STA an UL RU which is located in idle channels
  Based on the received BSR, the AP can decide the proper UL RU size
For example, when an AP allocates UL RU to a STA without BQR, if the allocated RU is in busy channel, the allocated RU will not be used (i.e., resource wastage)

## Slide 4: Background (2/2)
And, if the NAV is non-zero value or the RU allocated for the BQR is busy, the STA will not send BQR in respond to the BQR Trigger
In that case the AP could not know why the STA didn’t send it or could not know the BQR of the STA or when the NAV of the STA becomes 0
  Finally, AP will try to send the BQR Trigger after a certain time to check the BQR
In this contribution we propose the NAV status information and available channel (BQR) information using multi-link
  Note that NAV status report using multiple link were already introduced in [4]

## Slide 5: NAV Status Report (NSR) using multi-link (1/3)
Each STA within a non-AP MLD can maintain NAV timer for its link
  If the STA supports two NAVs (Intra & Basic), two NAVs per link will be maintained
When the STA sends a UL frame on its link, the STA can include the NAV status report (NSR) for other link(s) within the same MLD in the UL frame
AP can send a STA within a non-AP MLD a Trigger frame to get the NSR of multiple links (i.e., other STAs) and the STA can send the NSR of other link(s) in response to the Trigger frame
Based on the received NSRs for multiple links from a STA, an AP can decide when the AP allocates RU to the STA through the links
  If the received NAV is 0, AP can allocate UL immediately. Otherwise, the AP can wait to trigger the STA until the NAV becomes 0
  At least, the AP can know in which links the NAV of the STA has non zero value

## Slide 6: NAV Status Report (NSR) using multi-link (2/3)
Example of unsolicited NSR method
Link 1
Link 2
Non-AP
Link 2
Link 1
AP
UL frame (NSR of link 2)
BA/Ack
UL frame
BA/Ack
TF
NAV

## Slide 7: NAV Status Report (NSR) using multi-link (3/3)
Example of solicited NSR method
Link 1
Link 2
Non-AP
Link 2
Link 1
AP
UL frame
(NSR of link 2)
BA/Ack
TF
UL frame
BA/Ack
TF
NAV

## Slide 8: BQR using multi-link (1/2)
When a STA within a MLD sends a UL frame on its link, the STA can include the available channel information (e.g., BQRs) of other links within the same MLD
An AP within an AP MLD can trigger a STA within a non-AP MLD in order to obtain the available channel information (e.g., BQRs) for other links within the same non-AP MLD
  i.e., BQR of a link should be able to be sent through another link
The STA can send a frame including the BQR(s) of other link(s) in response to the Trigger frame
When the AP MLD sends a Trigger frame for UL allocation through a indicated link, the AP MLD can choose the proper RU based on the received available channel information (e.g., BQRs) (i.e., RU in idle channel)

## Slide 9: BQR using multi-link (2/2)
Example
Link 1
Link 2
STA
Link 2
Link 1
AP
UL frame + BQR Control of link 1&2
BA/Ack
UL frame
BA/Ack
TF
BQRP TF (link 1&2)
UL frame
TF
BA/Ack

## Slide 10: Conclusion
We proposed the method of enhancing the UL MU efficiency using multi-link
  A STA within a non-AP MLD can report the NAV status(s) or the channel status(s) for other link(s) within the same non-AP MLD
  An AP with an AP MLD can trigger a STA within a non-AP MLD to get the NAV status(s) or the channel status(s) for other link(s) within the same non-AP MLD

## Slide 11: Reference
[1] 11-15/1095, OFDMA performance in 11ax
[2] 11-16/1363, 11ax PAR Verification through OFDMA
[3] 11-18/1171, View on EHT objectives and technologies
[4] 11-18/1525, EHT features for Multi-Band Operation
[5] 11-18/1908, Overview of Full Duplex over Multi- Band (FD-MB) for EHT
[6] 11-19/773, Multi-link Operation Framework
[7] 11-19/777, Performance on Multi-band Operation
[8] 11-19/823, Multi-Link Aggregation
[9] 11-18/1231r6, EHT Proposed PAR

## Slide 12: Straw Poll 1
Do you agree to support the following?
  A STA within a MLD can send a frame containing NAV status information of other link(s) within the same MLD to its AP
    The detail of NAV information is TBD

## Slide 13: Straw Poll 2
Do you agree to support the following?
  A STA within a MLD can send a frame containing the available channel information(e.g., BQR) of other link(s) within the same MLD to its AP
    The detailed format of the available channel information is TBD

## Slide 14: Straw Poll 3
Do you agree to support the following?
  An AP within an AP MLD can send a Trigger frame to a STA within a non-AP MLD, which is associated with the AP, to get the NAV status information of other link(s) within the same non-AP MLD
    The details of the Trigger frame is TBD

## Slide 15: Straw Poll 4
Do you agree to support the following?
  An AP within an AP MLD can send a Trigger frame to a STA within a non-AP MLD, which is associated with the AP, to get the channel status information (e.g., BQR) of other link(s) within the same non-AP MLD
    The details of the Trigger frame is TBD