## Slide 1: Revisiting HARQ Complexity
Date: 2019-11-08
Authors:

## Slide 2: Background
Various contributions on Hybrid Automatic Repeat Request (HARQ) have been presented in previous meetings [1-7]
In [8], HARQ complexity was addressed, with focus on 3 major aspects:
  Receiver LLR Memory requirements
  PHY LDPC codeword processing
  MAC layer processing
Here we want to address the first two aspects in detail, and give a different view, some of which is based on simulation results

## Slide 3: Receiver LLR Memory Requirements
We start out with similar assumptions as in [8]:
  An HARQ sequence (defined here as a block of data, e.g. PSDU, that is contained in the initial transmission and any subsequent HARQ retransmission) completes within a TXOP
  A single HARQ sequence is active at any time
  Memory is allocated for the LLRs for all code bits in the codeword
  Focus on Chase Combining
  5 bits are allocated for an LLR
In the next slides, we compute the memory size respective to various scenarios, just like [8]

## Slide 4: Receiver LLR Memory Requirements – Rough Estimate of LLR Memory Size
Let us begin with a discussion of the memory size required for the LLRs
We will reuse the same scenarios of data rates and durations given in the table below, and then compute the corresponding LLR memory size
Data Rate (Gb/s) | Duration of Data Field (ms)
1 | 1
5 | 1
10 | 1
1 | 5
5 | 5
10 | 5

## Slide 5: Receiver LLR Memory Requirements – Rough Estimate of LLR Memory Size
Let us look at how many codewords fail, on average, within a failed MPDU, where we assume 20% PER
We look at three different MCS – each with a different coding rate - for a 1500B MPDU
The results are shown in the figure on the right; the average number of failed codewords is:
  MCS 1 = 5.68 out of 13, ~43%
  MCS 4 = 6.11 out of 9, ~67%
  MCS 7 = 5.55 out of 8, ~69%

## Slide 6: Receiver LLR Memory Requirements – Rough Estimate of LLR Memory Size
Some things to consider before we compute the memory size:
  Rate of 1Gbps corresponds to 1Mbit transmitted within 1msec, which means which is a rather large aggregation; similarly, 10Gbps transmitted within 1msec corresponds to ~833 MPDUs…
    We assume packets of size 1500B are used for such high data rates
    These are far from being typical scenarios; nevertheless, we will adopt them
  Typical MCS selection/link adaptation works around 10% PER, however with HARQ we may aim for a higher, pre-combining PER, so let’s assume we operate around 20% PER
  On average, as shown in previous slide, roughly half the codewords fail within a failed MPDU, for practical PER; let’s assume 66% of codewords fail on average
  We need to store only LLRs corresponding to incorrectly decoded codewords
Based on the above, ~0.2*0.66= ~13% of transmitted codewords need to be stored (on average); the memory required for storing LLRs is the same irrespective of the HARQ feedback scheme, since only failed codewords are stored

## Slide 7: Receiver LLR Memory Requirements – Rough Estimate of LLR Memory Size
Based on the previous slide, we update the table with the respective LLR memory size, where we slightly modify the memory size computation from [8]: where D is the data rate in Gb/sec, T is the data field duration in msec, and C is the ratio of codewords that needs to be stored
We assume both C=13% and C=26%
Code rate 5/6 is assumed
Data Rate (Gb/s) | Duration of Data Field (ms) | Codeword Storage Ratio | LLR Memory Size (MB)
1 | 1 | 0.13 | 0.09
5 | 1 | 0.13 | 0.46
10 | 1 | 0.13 | 0.93
1 | 5 | 0.26 | 0.93
5 | 5 | 0.26 | 4.65
10 | 5 | 0.26 | 9.3

## Slide 8: Receiver LLR Memory Requirements – Required memory at STA (DL example)
We will assume, similar to [8], MCS 11 with 2 SS, and Chase Combining
Since there are 11ax chipsets fabricated at 14nm process [9] in the market, we expect 11be to be fabricated at 7nm or below
Given a conservative area ratio of 10:1 (from 28nm to 7nm process), we assume memory die size at 7nm to be 0.016mm2/Mb for memory cells
The resulting memory area is relatively negligible
Bandwidth (MHz) | Data Rate (Gb/s) | Duration of Data Field (ms) | Codeword Storage Ratio | LLR Memory Size (MB) | SRAM Area (7nm) (mm2)
80 | 1.2 | 1 | 0.13 | 0.11 | 0.014
160 | 2.4 | 1 | 0.13 | 0.22 | 0.028
320 | 4.8 | 1 | 0.13 | 0.45 | 0.055
80 | 1.2 | 5 | 0.26 | 1.11 | 0.13
160 | 2.4 | 5 | 0.26 | 2.23 | 0.27
320 | 4.8 | 5 | 0.26 | 4.47 | 0.54

## Slide 9: LDPC Codeword Processing
As indicated in [8], with HARQ – depending on the retransmission scheme – less time may be required to transmit the code bits respective to an LDPC codeword
This means that more codewords may be transmitted in a given period of time; for example, as shown below, if 50% of the coded bits are retransmitted, then within any given time twice as many codewords are transmitted within a reTx
It appears as if codeword processing rate may need to be increased; let us see if this is indeed true
100% of the code bits from the k-th LDPC Codeword
50% of the code bits from the k-th LDPC Codeword
1st Tx
2nd Tx
Time
50% of the code bits from the k+1th LDPC Codeword

## Slide 10: LDPC Codeword Processing
The LDPC decoder processing rate is mainly dictated by the number of decoding iterations
The figure below shows the number of iterations required for the 1st Tx (no combining) and the 2nd Tx (after combining), for a scenario where post-combining PER is 1%
Maximum number of iterations is set to 8
We assume here only 50% of the coded bits are retransmitted
The average number of iterations required for 1st and 2nd Tx are 6.6 and 3.7, respectively

## Slide 11: LDPC Codeword Processing
The result on the previous slide means that within the retransmission, where only 50% of the coded bits are transmitted, the LDPC decoder needs to ‘work’ only ~50% of the time as well, so there is no real increase in LDPC codeword processing requirement

## Slide 12: Conclusions
We looked at two aspects related to HARQ – the required memory, and the LDPC processing rate
We’ve shown that the impact of HARQ on the memory size and LDPC decoder processing is not as significant as previously thought
A later contribution will discuss the MAC processing rate aspect

## Slide 13: References
11-18-1587: HARQ for EHT, Sep. 2018
11-18-1955: HARQ for EHT – Further Information, Nov. 2018
11-18-1963: Discussion on HARQ for EHT, Nov. 2018
11-19-1992: HARQ Feasibility, Jan. 2019
11-19-2029: HARQ in EHT, Jan. 2019
11-19-1979: HARQ performance analysis, Jan. 2019
11-19-780: Consideration on HARQ, May 2019
11-19-1080: HARQ Complexity, Sep. 2019
https://www.qualcomm.com/news/releases/2019/01/07/qualcomm-demonstrates-continued-leadership-industry-transitions-wi-fi-6