## Slide 1: Consideration of EHT-LTF
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jinmin1230.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
The extensions of 16 streams and 320MHz are one of candidates in EHT
  Especially, multi-AP and MU-MIMO are the use cases of high order MIMO system (e.g. 16 spatial streams )
To support 16 streams and 320MHz, we need to define EHT-LTF
In this contribution, we consider how to design EHT-LTF in respect of overhead and PAPR performance

## Slide 3: Overhead Analysis
We assume that,
  MU-MIMO cases
    4 users, 4 spatial stream per user. So, total spatial streams are 16.
  Design EHT-LTF similar to legacy Wi-Fi,
    So, we need 16x16 P-matrix to support 16 spatial streams
The figure shows the ratio(%) between length of LTF and length of PPDU
  Even in case of 10k byte data size(TXTIME=227.2us), LTF length is more than 50% of total PPDU length
  If we use higher MCS, higher Nss per user or 4xLTF, overhead problem becomes worse.
80MHz MU PPDU in 11ax
MCS 6 (16QAM, R=¾)
2x LTF, 0.8us GI

## Slide 4: Candidates for EHT-LTF
A few contributions proposed new structure to design EHT-LTF to reduce overhead
  In [1,3], they propose interleaved LTF sequence between streams in multi-AP scenario
    We think it is also applicable to SU-MIMO and it is simple way to reduce overhead
  In [2], orthogonal sequence is proposed to reduce overhead and shows performance both in closed-loop and open-loop MIMO
    It can achieve large smoothing gain in open-loop MIMO cases
We believe that various techniques including the above methods can be considered for further enhancement
  For example, orthogonal sequence and interleaved method can be combined to achieve both CFO robustness and smoothing gain

## Slide 5: How to Generate 320MHz LTF
For 320MHz (and 240MHz), we need to generate longer sequence
  To generate 160MHz HE-LTF in 11ax, 80MHz sequence is duplicated with phase rotation to reduce PAPR
So, we can also generate 320MHz sequence by using duplication of 160MHz sequence defined in 11ax
  We assume that 320MHz tone-plan consists of repetition of 80MHz tone-plan. Of course, if 320MHz tone-plan is newly designed, we need a new method for EHT-LTF sequence

## Slide 6: 320MHz LTF Sequence
Generations method (e.g. 2xLTF)
  EHTLTF_2x_320M = [LTF160MHz_lower_2x, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, LTF160MHz_upper_2x]
    LTF160MHz_lower_2x = [LTF80MHz_lower_2x, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, LTF80MHz_upper_2x];
    LTF160MHz_upper_2x = [LTF80MHz_lower_2x, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, (-)LTF80MHz_upper_2x];
  LTF80MHz_lower_2x and LTF80MHz_upper_2x are defined in 11ax
  Similar approach can be applied to 1x and 4x LTF
Similar to 11ax, we apply phase rotation into LTF160MHz_upper_2x to reduce PAPR

## Slide 7: PAPR Performance
Assumptions
  4 times oversampling to measure PAPR
  P matrix and R matrix are applied(only for 2x, 4x LTF)
  Beamforming and small RU are not considered (FFS)
Phase rotation as in 11ax works well
For 320MHz, we think EHT-LTF has reasonable PAPR performance considering PAPR of data (see the Appendix)
BW | 4x LTF | 2x LTF | 1x LTF
80MHz (996RU) | 6.29 | 6.08 | 4.86
160MHz (2x996RU) | 7.09 | 6.72 | 4.91
320MHz (4x996RU) | 7.81 | 6.97 | 4.92
320MHz w/o PR | 9.44 | 9.52 | 7.62

## Slide 8: Further Considerations
Even though PAPR is reasonable in our simulation, we need more investigation in small RU cases
Moreover, since TGbe agreed that multiple RU can be allocated to single STA, we may need to check PAPR performance in various combinations especially in UL OFDMA
And, different from 11ax, we can optimize PAPR performance considering puncturing pattern since it’s the first stage of the design of EHT-LTF

## Slide 9: Conclusion
To extend 16 spatial streams and 320MHz BW, we need to develop EHT-LTF and we should take into account overhead and PAPR performance
  If possible, we can design EHT-LTF using similar way to 11ax for simplicity
However, since we agree that multiple RU allocation to single STA, we need further study EHT-LTF based on multiple RU allocation’s agreements
  E.g. Maximum number of RUs assigned to a single STA is a important factor to PAPR performance

## Slide 10: Straw poll 1
Do you agree to add the following text into SFD?
  EHT-LTF should be designed to support 16 spatial streams considering overhead reduction.
    Overhead reduction method is TBD including 2x or 1x HE-LTF concept defined in 11ax

## Slide 11: Straw poll 2
Do you agree to add the following text into SFD?
  EHT-LTF should be designed to consider PAPR performance when multiple RU allocation and/or preamble puncturing is applied

## Slide 12: References
[1] 19/1535r0, “Sounding-for-ap-collaboration”
[2] 19/1585r1, “Orthogonal-sequence-based-reference-signal-for-ltf-reduction”
[3] 19/1593r0, “Joint-sounding-for-multi-ap-systems”

## Slide 13: Appendix
Median PAPR in Data
RU type | DATA (BPSK) | DATA (QAM)
80MHz | 8.77 dB | 9.16 dB
160MHz | 9.18 dB | 9.54 dB
320MHz | 9.53 dB | 9.86 dB