## Slide 1: Multi-AP group formation follow-up
Date: 2019-11-11
Authors:
Name | Affiliations | Address | Phone | Email
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Po-kai Huang |  |  |  | po-kai.huang@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Notes: September 2012

## Slide 2: Motivation
In [1], we initiated discussions on the fundamental framework of Multi-AP coordination, i.e., the formation of a set of APs that will participate in Multi-AP transmissions.
  We proposed that we need the concept of a Multi-AP set.
  However, the specific procedures of how to form the Multi-AP set, could be implementation specific, and therefore outside of the scope of 11be.
This contribution further investigates Multi-AP group formation.

## Slide 3: Multi-AP coordination
The primary motivation for Multi-AP feature is to leverage the coordination among multiple APs to optimize a system-level metric, such as overall throughput or average latency.
In order to achieve the Multi-AP benefits, both long-term management domain coordination and specific triggering functions are needed.
  The long-term coordination basically includes management functions such as defining the boundary of Multi-AP functions and general operation rules.
  The specific triggering operations depend on different Multi-AP coordination techniques, such as conducting sounding sequence for coordinated/joint BF, initiating coordinated OFDMA transmission, and performing joint transmission.

## Slide 4: Boundary of Multi-AP operations
When designing protocols for various Multi-AP coordination functions, we should clearly define the boundary of these coordination functions.
  In legacy Single AP scenario, most of the functions between the AP and its associated STAs are limited to its own BSS.
  In Multi-AP scenarios, we should also limit the Multi-AP functions within a defined boundary. This basically means we need a way to indicate if an AP can be coordinated by another AP or not.
    For example, we may not want to allow the case that an AP in my neighbor’s home is able to coordinate the AP in my own home arbitrarily.
  In this case, a group concept is needed to define this boundary and place restrictions on the potential candidates of Multi-AP transmissions.
    Similar to the concept of SRG group defined in 11ax.
  If we want to enable the authentication of Multi-AP Trigger frames, including a way to distribute the key for authenticating and verifying the Multi-AP trigger frames sent among a certain set of APs, a group concept is also needed.
    Prevention from DoS attacks.

## Slide 5: Triggering operation
For each AP that participates in Multi-AP functions, there should be a way to indicate if it can initiate the coordination and trigger the other APs or not.
  Mode 1: Every AP can initiate and trigger coordination
    For example, any AP that has obtained a TXOP can initiate coordinated OFDMA with other APs [2].
  Mode 2: Only certain AP(s) can initiate and trigger the coordination operation
    Suitable in scenarios where fully scheduled/trigger-based access is preferred.

## Slide 6: Example of every AP can initiate coordination operations
AP1
AP2
AP3
AP4
STA
STA
STA
STA
STA
STA
STA
STA
STA
TXOP 1, obtained by AP1
DL OFDMA
UL Ack/BA
TXOP 2, obtained by AP3
UL OFDMA
DL Ack/BA
Trigger
Multi-AP Trigger
Multi-AP Trigger
Time
Time
Frequency
Frequency

## Slide 7: Overall proposal
We propose the following Multi-AP framework:
  1. Introduce the concept of a Multi-AP set consisting of APs that may participate in Multi-AP transmission. However, we do not need to define specific formation procedures of a Multi-AP set.
  2. Define a mechanism to determine whether an AP is part of a Multi-AP set that participates in Multi-AP transmission.
  3. For specific triggering operations, there may be different modes depending on whether an AP can initiate and trigger coordination operations or not.

## Slide 8: Straw Poll
Do you agree to define a mechanism to determine whether an AP is part of a Multi-AP set that participates in Multi-AP transmission?

## Slide 9: References
[1] 11-19-1616-01-00be-multi-ap-group-formation
[2] 11-19-1582-00-00be-introduction-to-coordinated-ap-ofdma-transmissions-in-11be